## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Basic Coastal Navigation
Approved USCG Auxiliary - Department of Education Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Chapter 1
Introduction to Coastal Navigation
Notes: <number>

## Slide 3: Introduction What We’ll Cover
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Basic Navigation Process
Basic Definitions
  Earth
  Great and small circles
  Measuring location
  Measuring direction
Notes: <number>

## Slide 4: Steps in Voyage Planning
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Assemble Required Reference Materials
Formulate Voyage Alternatives
Evaluate Alternatives
Select Best Voyage Plan
Prepare Float Plan
Complete Pre-Underway Vessel Checks
Weigh Anchor
Notes: <number>

## Slide 5: Steps in Underway Navigation
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Start
Update DR Plot
Search for FIX Opportunities
Piloting
Use Visual Methods
Electronic Navigation
Use Shipboard Electronics
Celestial
Observations
Compare FIX With DR Plot
Compute Current
Set and Drift
Repeat this process every 30 minutes while underway
A Circular System
Notes: <number>

## Slide 6: Planet Earth
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Oblate spheroid (flattened at poles)
  Diameter = 6,880 nautical miles
  Circumference = 21,614 nautical miles
Circumference divided into 360 degrees
Degrees subdivided into 60 minutes (written 32’)
Minutes subdivided into 60 seconds (written 17”)
Notes: <number>

## Slide 7: Great Circles
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Formed by planes passed through earth’s center.
Separate earth into two hemispheres.
Shortest distance between any two points lies on great circle connecting them.
Notes: <number>

## Slide 8: Equator
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Great circle equidistant between geographic poles called equator.
Forms demarcation between north & south hemispheres.
Notes: <number>

## Slide 9: Small Circles
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Plane passed through earth that does not touch the earth’s center.
Small circles parallel to equator termed latitude.
Equator
Small Circle
L = 30º N
Latitude is one of two reference coordinates used to describe position on the earth.
Notes: <number>

## Slide 10: Meridians
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Polar Axis
Great circles that pass through the polar axis of rotation.
  0º passes through Greenwich, England.
  Commonly called the Prime Meridian.
Lo = 130 º W
Lo = 70 º W
Lo = 50 º E
Lo = 110 º E
Measured east and west through 180º.
Provide the second coordinate - longitude.
Notes: <number>

## Slide 11: L & Lo Review
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Latitude (L)
Longitude (Lo)
Angular distance N or S of equator
Equator = 0º
Must indicate N or S
North pole = 90º N
Angular distance E or W of prime meridian
PM = 0º
Must indicate E or W
Naval Observatory, Washington, D.C. is 77º 3.9’W
Notes: <number>

## Slide 12: Describing Location
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Lo 37º 25.0’ W
L 52º 3.7’ N
Notes: <number>

## Slide 13: Measuring Distance
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
1 Degree of Latitude = 60 Minutes of Latitude
1 Minute of Latitude = 1 Nautical Mile
1 Degree of Latitude = 60 Nautical Miles
St. Augustine, FL, is at L 30 º N.
How many miles north of the equator is St. Augustine ?
30 º x 60 M/º = 1,800 M
Notes: <number>

## Slide 14: More Examples
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
What is the distance from the equator to:
  L 22 º 10.0’N?
(22º x 60 M/º) + 10.0’ x 1 M/min = 1,330 M
Your position: L 39º49.6’N and a vessel passing you is 3 NM South.
  What is the vessel’s latitude ?
L: 39º49.6’N – (3 M / 1 M/min) = 39º46.6’N
Notes: <number>

## Slide 15: Scales for L & Lo
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Minutes of L & Lo delineated along chart edges.
  Bar color alternates, black to white, for ease of reading.
  Each bar divided into tenths.
L & Lo lines drawn chart every 5 minutes of L & Lo.
  Helpful to determine position on chart.
Notes: <number>

## Slide 16: Reading Latitude
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
The latitude markings are on right and left sides of your 1210 TR chart, read from bottom to top.
What is the latitude indicated for the bottom of the chart?
41º 09.0’N
What is the latitude indicated for the top of the chart?
41º 45.0’N
Notes: <number>

## Slide 17: Reading Longitude
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Measured along top and bottom of chart, measured E to W in western hemisphere (right to left).
What is the longitude indicated for the left side of the chart?
71º 35.0’W
What is the Longitude indicated for the right side of the chart?
70º 36.0’W
Notes: <number>

## Slide 18: How Big is Your Chart ?
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
What is the difference in latitude and longitude between the respective edges of the 1210 TR chart?
L 41º 09.0’N - L 40º 45’N = 0.36’
Lo 70º 36.0’W - Lo 71º 35’W = 0.39’
Notes: <number>

## Slide 19: What We Really Need to Know is Distance:
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
How far is it in nautical miles from the bottom to the top of the chart?
0.36’ = 36 NM
Notes: <number>

## Slide 20: Point to Consider
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Distance between minutes of latitude is constant.
  So, we can use latitude to measure distance.
Is this true of longitude?
  No - longitude lines converge at poles.
  So - distance between minutes gets smaller as you go north or north from equator.
How do you measure width on charts?
Notes: <number>

## Slide 21: Measuring Other Distances
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Two ways:
  One: Use dividers to transfer measurements taken from L scale and apply them to Lo.
  Two: Use distance scale found at top and bottom of chart in the same way.
Using either of these methods, how far is it in nautical miles from right to left side of your chart?
44.3 Nautical Miles
Notes: <number>

## Slide 22: Measuring Directions
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
110°
85 °
300 °
Direction, too, must be keyed to a reference.
We use notion of north & south poles as references.
But, what is exact location of poles?
Depends on whether we use magnetic or geographic poles as reference.
Notes: <number>

## Slide 23: Geographic vs. Magnetic Poles
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Earth’s Axis of Rotation = Geographic Poles.
  Where meridians converge.
Earth is also a magnet.
  N & S magnetic poles are not the same as geographic.
  Not only that … they move!
Notes: <number>

## Slide 24: Polar and Magnetic North
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Difference between
GEOGRAPHIC NORTH
and
MAGNETIC NORTH
is termed
VARIATION
Notes: <number>

## Slide 25: Variation
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Variation is angular difference between locations of geographic and magnetic poles.
Geographic North Pole
Magnetic North Pole
Observer’s Position
Notes: <number>

## Slide 26: Variation
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Variation depends on observer’s location.
Geographic
North Pole
Magnetic North Pole
Variation one thing at this location
Variation different at this location
Notes: <number>

## Slide 27: “Sense” of Variation
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Variation is EAST ...
  if magnetic north is to the EAST of true north from your location.
Variation is WEST ...
  if magnetic north is to the WEST of true north from your location.
Notes: <number>

## Slide 28: Magnetic Pole Movement
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Canadian scientists chart pole’s moving position.
Northwesterly motion averages 10 km per year.
Magnetic pole also wanders daily in an elliptical path
Due to magnetic disturbances caused by the sun.
Notes: <number>

## Slide 29: Finding Variation
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Variation indicated at center of each compass rose on chart.
In this case:
  VAR = 10º00’W (1988)
  ANNUAL INCREASE = 6’
Notes: <number>

## Slide 30: Relative Bearings
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Direction of targets sometimes measured with reference to vessel’s bow.
Measured clockwise from dead ahead.
045 R
Hdg =
090 T
Notes: <number>

## Slide 31: Relative Bearings
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Relative bearing of target added to ship’s heading to determine actual bearing of target.
If heading “True”, target bearing also “True”, etc.
Hdg 090 T
Rel Brg + 045
Brg 135 T
Notes: <number>

## Slide 32: Relative Bearings
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Sometimes the result of calculation may exceed 360º.
To correct, subtract 360º.
Hdg 345 M
Rel Brg + 050
395 M
Correct - 360
Brg 035 M
Notes: <number>

## Slide 33: Reciprocal Bearings
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
270º
090º
160º
340º
Reciprocal bearing is the 180º opposite of a bearing.
If true course to target is 160º, reciprocal (course from target to your vessel) would be 340º.
When calculation exceeds 360º, Subtract 360º.
Brg 273 T
Add 180º + 180
453 T
Correct - 360
Reciprocal 093 T
Notes: <number>

## Slide 34: End of Chapter 1
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 1 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>