## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Basic Coastal Navigation
Approved USCG Auxiliary - Department of Education Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Chapter 5
Dead Reckoning
Notes: <number>

## Slide 3: Dead Reckoning
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Simplest, most basic technique of navigation
DR is deduced position
Origin of term lost in antiquity
Some say that the word “dead” should be written “ded”-meaning deduced
Notes: <number>

## Slide 4: Dead Reckoning
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
One of the most important navigation techniques.
Electronics, celestial, or piloting not complete systems.
  Serve to check accuracy of DR positions
  Subject to various failures.
  e.g. Storms, power loss, reduced vision and equipment failure.
Notes: <number>

## Slide 5: What is Dead Reckoning?
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Your intended or assumed path through the water.
Plotted as a line w/ symbols on a chart.
Based on:
  COURSE (direction traveled)
  SPEED & TIME (distance run)
Notes: <number>

## Slide 6: Information Considered DR Plot
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Use:
  Course known to have been steered.
  Speed through the water (STW).
Do not consider:
  Effects of Current.
  Effects of Wind.
Notes: <number>

## Slide 7: DR Terms Planning Voyage
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Course of Advance (COA) or Track (TR)
  The direction of the INTENDED path over ground.
Speed of Advance (SOA)
  The speed INTENDED to be made over ground along the COA.
Notes: <number>

## Slide 8: DR Terms During Voyage
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Course Over Ground (COG)
  Instantaneous direction of the actual path over ground.
Speed Over Ground (SOG)
  Speed made good at any instant along the (COG).
Speed Through the Water (STW)
  Apparent speed over COG.
Notes: <number>

## Slide 9: DR Terms After Voyage
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Course Made Good (CMG)
  The resultant direction from the beginning of the voyage to the end.
Speed Made Good (SMG)
  The overall actual speed of voyage.
Notes: <number>

## Slide 10: More DR Terms
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Current - Has two components:
  Set - Direction TOWARDS which the current is moving.
  Drift - Speed in kts at which current is moving.
Line of Position (LOP) - Bearing to an object.
Estimated Position (EP) - An improved position based on DR position.
Fix - A known position.
Notes: <number>

## Slide 11: Purpose of a DR Plot
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Before sailing (voyage planning):
  Determine course and speed to make.
  Identify checkpoints and waypoints,
    Locate fuel and other needed stops.
    Estimate: Fuel, time, and other parameters.
While underway to plot or follow actual progress, (tactical plot).
Notes: <number>

## Slide 12: Elements of DR Plot
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Course is a solid line.
Starts from a fix or point-of-departure.
Direction or Heading:
  Labeled by 3 digit True or Magnetic.
    Preceded by “C” for ‘course’.
    Followed by “M” if magnetic.
  Speed “S” is beneath the course line.
C 030
S 5.4
Notes: <number>

## Slide 13: Standards of Precision
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>

## Slide 14: Planning DR Plot
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Using chart 1210TR for a Buzzards Bay voyage.
  Starting Point: Buoy BR Qk Fl G at 1300.
  Course 360 True.
  Speed 6.1 knots.
How do we plan the cruise to arrive at our terminus at Pasque Island?
Notes: <number>

## Slide 15: Planning DR Plot
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>

## Slide 16: Tactical DR Plot
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Prepared as you go:
  Reflects actual progress through fixes.
  Reflects actual starting time.
  Reflects actual fixes.
  Also reflects near-term planning.
  Is updated after each fix.
Notes: <number>

## Slide 17: Tactical DR Plot
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Departed Block Island 1430
  Buoy “3” FL G 2.5 sec.
  Course 024, Speed 4 knots.
At 1615 we take 3 bearings.
  Whistle buoy R2 bearing 349T
  Sandy Pt light bearing 227T
  Buoy R2 Fl R, bearing 321T
Plot the FIX, new position, and begin the new DR Plot.
Notes: <number>

## Slide 18: Important! Starting a New DR
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
At 1615 we plotted a FIX.
A FIX gives an accurate position.
With a FIX (or a running FIX), you start a new DR plot.
Notes: <number>

## Slide 19: Rules for DR Plots
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>

## Slide 20: Keeping A Log
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
The ship’s log is a matter of taste.
A DR Log should include:
  Time
  Course
    Compass, Magnetic, True
  Speed
    RPM, STW
  L and Lo
  Remarks
Notes: <number>

## Slide 21: Calculating Time, Speed & Distance
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Distance = Speed times Time divided by 60
D = ST/60
Speed = Distance times 60 divided by Time
S = 60D/T
Time = Distance times 60 divided by Speed
T = 60D/S
Notes: <number>

## Slide 22: Example Calculations
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Speed 10 kts, run time 20 min; compute distance:
D = ST/60 = 10x20/60 = 3.3 nm
Distance to destination 12 mi, time enroute is 40 min; compute speed:
S = 60D/T = 60x12/40 = 18.0 kts
Cruising at 15 kts, distance to destination is 12 mi; compute time to destination:
T = 60D/T = 60x12/15 = 48 min
Notes: <number>

## Slide 23: Speed Table
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Timed runs made out & back on measured course at multiple RPMs.
Calc’d speeds averaged at each RPM.
Notes: <number>

## Slide 24: Speed Curve
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Speed table data plotted in graphical form for easier use.
Notes: <number>

## Slide 25: End Chapter 5
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 5 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>