## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Basic Coastal Navigation
Approved USCG Auxiliary - Department of Education Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Chapter 3
The Nautical Chart
Notes: <number>

## Slide 3: What We’ll Cover
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Construction of charts.
Reading nautical charts.
Using nautical charts to determine:
  Position
  Direction
  Distance
Notes: <number>

## Slide 4: Construction of Nautical Charts
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Representing a spherical surface on a flat surface difficult.
Always some distortion in:
  Distance
  Direction
  Shape or Area
Notes: <number>

## Slide 5: Using Gores
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Flat map cut and bent to spherical surface
Measuring direction or distance difficult
We use “projections” to make charts
Notes: <number>

## Slide 6: Chart Projection Goals
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Balance and minimize distortions.
Create a representation that preserves:
  Direction
  Distance
  Shape and Area
  Angular relationships (conformal)
All projection methods have limitations.
Notes: <number>

## Slide 7: Many Projection Methods
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Of Interest to Mariners:
  Mercator Polyconic
Other Methods:
  Azimuthal-Equidistant Gall-Peters
  Goode Homolosine Lambert Azimuthal Equal Area
  Lambert Conformal Miller Cylindrical
  Mollweide Orthographic
  Polar Stereographic Polar Gnomonic
  Robinson Simple Conic
  Sinusoidal Van der Grinten
Notes: <number>

## Slide 8: Mercator Projection Method
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Developed in 1569 by Flemish geographer.
Earth’s surface projected onto a cylinder.
Cylinder tangent to the equator.
Distorts areas – esp. at poles.
U.S. Appears the same size as Greenland.
Actually more than 4 times larger.
Notes: <number>

## Slide 9: Mercator Projection Characteristics
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Projection never includes poles.
Great circles appear as curved lines
Except for the meridians and equator.
Notes: <number>

## Slide 10: Other Mercator Characteristics
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Meridians and parallels expanded at same ratio with increasing latitude.
Line of constant direction = rhumb line.
  e.g. cross every meridian at the same angle.
  Straight line on Mercator projection.
  Very handy when drawing courses on charts!
But ...
Notes: <number>

## Slide 11: Rhumb Line or Loxodrome
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Loxodrome crosses each meridian at the same angle.
A spiral that has no end.
Not usually a good long range navigation technique!
Notes: <number>

## Slide 12: Using a Mercator Chart to Measure a Position
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Format of Mercator charts is a rectangle
Latitude & Longitude are coordinate system.
North usually at the top.
Longitude scale at top and bottom.
Latitude scale on right and left.
  Also used for measuring distance.
Notes: <number>

## Slide 13: Measuring a Position’s Latitude & Longitude
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
L 33° 19.0’ N
Lo 77° 40.0’ W
Pick off distance from parallel to ruler edge.
Transfer distance. Read latitude from scale.
Repeat process using longitude scale.
Notes: <number>

## Slide 14: Example Measurement
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
What is L & Lo of
Buzzards Light?
Lo = 71° 02.0´ W
L = 41° 23.8´ N
Notes: <number>

## Slide 15: Describe Buzzard’s Light
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
The Light?
  White, flashing every 2.5 seconds
The Seabed?
  Rocky
Depth of the Water?
  Approx 60 ft, rising at light to 37 ft
What other information is provided?
  Light is 101ft high, visible for 22 mi
  Radio beacon, frequency of 314 MHz
  Code: Dash followed by three dots
  Horn
Notes: <number>

## Slide 16: Determining Direction
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Compass rose:
  Shows True and Magnetic directions.
  Use rose nearest measurement.
Use parallel rules or course plotter.
Notes: <number>

## Slide 17: Determining Direction Using Parallel Rules
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Draw line for expected course.
“Walk” parallel rulers to center of compass rose.
Read True direction from outer ring.
Notes: <number>

## Slide 18: Determining Direction
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Find direction, R“2” to Buzzards Light:
Draw line, R“2” to Buzzards.
Measure direction from Buzzards to R“2”.
Notes: <number>

## Slide 19: Measuring Distance
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Use dividers to transfer distances between objects and distance scales.
Use latitude scale or distance scale.
Notes: <number>

## Slide 20: Longer Distances
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
“Walk” dividers to measure large distances.
Read amount “left-over” on distance scale.
Notes: <number>

## Slide 21: Polyconic Projection Method
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Projection onto series of cones.
  Cones tangent at different parallels of latitude.
  Cones concentric with earth’s axis.
Not conformal.
  Distortion negligible for charts used by small boat operators.
Charts use compass roses.
Central Meridian
45º Tangent Parallel
30º Tangent Parallel
15º Tangent Parallel
Notes: <number>

## Slide 22: The Polyconic Chart
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Distortion least at central meridian.
  Increases toward the sides of the chart.
Parallels appear as slightly curved lines.
Meridians converge to imaginary spot off top of chart.
Distortions not readily apparent in small scale charts.
Notes: <number>

## Slide 23: Where Polyconic Projections Used
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Most charts for Great Lakes are polyconic projections.
Distances on Great Lakes charts given in statute miles.
Notes: <number>

## Slide 24: Measuring Position
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
LONGITUDE SCALE
(Along Parallel)
LATITUDE SCALE
(Along Meridian)
Plot meridian from upper
Lo scale to lower Lo scale.
Measure L with
dividers along
plotted meridian.
Notes: <number>

## Slide 25: Mercator & Polyconic Contrasted
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>

## Slide 26: Mercator & Polyconic Contrasted
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>

## Slide 27: Scale of a Chart
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Scale:
  Number of distance units on earth’s surface represented by same distance unit on a chart.
Example:
  One inch on a chart is equal to 2,500 inches on earth’s surface.
  This is written 1:2,500
Notes: <number>

## Slide 28: “Large” vs “Small”
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
The smaller the ratio, the larger the scale.
Large scale charts show:
  Less area, more detail
  1:2,500 is considered large-scale.
Small scale charts show:
  More area, less detail
  1:5,000,000 is considered small-scale.
Notes: <number>

## Slide 29
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Use Large Scale Chart To Show Maximum Detail
Approach to Woods Hole can be tricky, with strong currents. Use more detailed charts!
Notes: <number>

## Slide 30: Types of Marine Charts
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Sailing Chart
  Scale - 1:600,000 and smaller.
  Used off-shore, outside of coastal areas or between distant coastal ports
General Chart
  Scale – 1:150,000 to 1:600,000.
  Used for off-shore but within coastal zones outside of outlying reefs and shoals.
Notes: <number>

## Slide 31: Types of Marine Charts
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Coast Charts
  Scale - 1:40,000 to 1:150,000.
  Used for in-shore navigation of bays and harbors of considerable width and for large inland waterways and coastal passages.
Harbor Charts
  Scale – Larger than 1:40,000.
  Used in harbors, anchorages areas and small waterways.
Notes: <number>

## Slide 32: Small Craft Charts
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Scale - 1:40,000 and larger.
Composite type chart of inland waters.
  Mercator projection is used
  North may not be at top - made to fit the expanse of water on the chart.
  Contains information of interest to small boat operator.
Notes: <number>

## Slide 33: Chart Classification Summary
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>

## Slide 34: Three Choices: Point Judith Harbor
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Harbor Chart scale is 1:15,000.
Upper left is 1:80,000.
Upper right from Coast Chart.
Notes: <number>

## Slide 35: Title Block
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Location
Title
Projection & scale
Datum
Notes: <number>

## Slide 36: Information Found on Nautical Charts
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Water depth
Aids to Navigation
  Lights (Color & Timing)
  Other characteristics
Landmarks
Shoreline shape
Bridge Clearances
Direction measurement
Bottom characteristics
Distance measurement
Navigational hazards
Notes: <number>

## Slide 37: Datum
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Gay Head Light
Base line or plane from which measurements are made.
Datum for water depth is important.
  East coast has two tides very similar.
  West coast has two tides of uneven depth.
  Standard is mean lower low water (MLLW).
  Former standard was mean low water (MLW).
Notes: <number>

## Slide 38: Low Water
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Mean means an average of all depths.
MLLW is intended to be conservative.
Most of the time you will have greater depth - BUT NOT ALWAYS.
Nobska Point Light
Notes: <number>

## Slide 39: Depth Contours
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Connect points of equal depth:
  (i.e. 30 ft - 60 ft - 90 ft – etc).
  Profile the bottom shape.
Numbers or color codes indicate depth. 
Depth is given in feet, fathoms or meters.
  (1 fathom = 6 feet)
Chart also indicates characteristics of the bottom. 





Notes: <number>

## Slide 40: Landmarks
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Large circle with dot in center:
  Denotes accurately located landmark.
  Shown in “ALL CAPITAL LETTERS”.
Small circles without dot in center:
  Denote landmarks not accurately located.
  Shown on chart in “Initial Capital Letters”.
Chilmark Spire
Notes: <number>

## Slide 41: Object Detection
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Objects on charts may not be visible in all situations.
Masked by other objects
Hazy visibility
Lighting
Tide height
Gay Head Light is masked from some directions.
Notes: <number>

## Slide 42: Local Notices to Mariners
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Published by each Coast Guard District.
Disseminate information important to navigation.
Include updates to ATONs.
Indicate temporary changes:
  Dredging, marine construction, whale migration, bridge construction, buoys, special activities, etc.
On the web at: www.navcen.uscg.gov/lnm/
Notes: <number>

## Slide 43: The Four R’s for Charts
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
RECENT
RIGHT SCALE
READILY AVAILABLE
REVIEWED BEFORE SAILING
Notes: <number>

## Slide 44: End Chapter 3
<number>
13 Dec 04
Basic Coastal Navigation - Chapter 3 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>