## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Basic Coastal Navigation
Approved USCG Auxiliary - Department of Education Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Chapter 2
The Marine Magnetic Compass
Notes: <number>

## Slide 3: What We’ll Cover
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Brief history
Compass design
Principles of operation
Deviation & swinging ship
Compass calculations
Notes: <number>

## Slide 4: Brief History
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Phoenicians used magnetic direction finder.
Evidence for use in Europe/China ~1100.
Compass card invented ~ 1300.
Variation understood by 1492.
Charts showed variation by 1700.
Notes: <number>

## Slide 5: Brief History
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Flinders bar to compensate for deviation developed 1801.
Ritchie liquid filled compass - 1859.
Modern gyrocompass developed by Speery and Anschutz-Kanpfe ~1900.
Notes: <number>

## Slide 6: Parts of a Compass
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Constructed of non-magnetic materials.
Notes: <number>

## Slide 7: Parts of a Compass
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Indexed card to read direction.
Notes: <number>

## Slide 8: Parts of a Compass
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Lubber line pins to align compass with boat.
Notes: <number>

## Slide 9: Parts of a Compass
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Gimbal system to keep card level when boat heels and pitches.
Notes: <number>

## Slide 10: Parts of a Compass
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Spherical bowl with expansion diaphragm.
Notes: <number>

## Slide 11: Parts of a Compass
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Fluid filled damping system to impede rapid card movement.
Notes: <number>

## Slide 12: Parts of a Compass
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Compensation system to reduce deviation error.
Notes: <number>

## Slide 13: Steering Compass Styles
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Top Reading Card
Usually used in binnacle steering stations.
Front Reading Card
Used when compass mounted on bulkhead.
Notes: <number>

## Slide 14: Hand Bearing Compass Styles
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Front/Top Reading
Hockey Puck
Digital/Scope Style
Notes: <number>

## Slide 15: Compass Card
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Graduated in degrees from 000 to 359.
Graduated in 1, 2, 5 degree increments.
Numbers spaced every 10-30 degrees.
Usually show cardinal points: N, S, E & W.
May show intercardinal points: NE, SE, SW & NW.
Notes: <number>

## Slide 16: Compass Errors Deviation and Variation
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
The ugly Truth …
Compasses don’t point to True North!
Notes: <number>

## Slide 17: Compass Errors
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Variation:
  Geographic (true) vs. magnetic north.
  Common to all parts of the globe.
  Identified on every chart’s compass rose(s).
Deviation:
  Caused by shipboard magnetic influences.
  Exists on all vessels; different for each vessel.
  Depends on vessel's heading.
  Can vary widely.
Notes: <number>

## Slide 18: Variation: Earth - A Magnet
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Locating exact source of magnetism difficult.
  Alignment of magnetism changes.
  Strength of pull varies over earth.
Notes: <number>

## Slide 19: World-Wide Variation
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Isogonic Chart
Illustrates magnetic variation (1995)
Notes: <number>

## Slide 20: Deviation: Boat-Specific Error
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Due to on-board magnetic influences:
  Magnetic items
  Items to which magnets are attracted.
  Wires carrying DC electrical current.
Reduce effects as much as possible:
  Keep compass away from influences
  Twist nearby DC wire pairs.
Usually can’t eliminate them all.
Notes: <number>

## Slide 21: Compensation
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Deviation often greater than 10º.
Special magnets (compensators) installed in compasses to reduce error.
Most compasses come with instructions.
Or, engage services of professional compass adjuster.
Can still have significant deviation error after compensation.
Notes: <number>

## Slide 22: “Swinging Ship”
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Process of measuring residual deviation error after compensation.
Usually determined in 15º - 30º heading increments.
Recorded in form of deviation table.
Compass adjuster can provide service.
Or, you can do it yourself ...
Notes: <number>

## Slide 23: Measuring Deviation Yourself
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
We’ll get to that later.
First you have to know how to do some compass calculations.
Notes: <number>

## Slide 24: Additive Effect of Compass Errors
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Error due to 015° W variation
Additional error due to 005° W deviation
Compass heading must be adjusted 020° to compensate.
Desired True heading
Notes: <number>

## Slide 25: Computing Compass Corrections
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
T True Heading
V Variation on Chart
M Magnetic Heading
D Deviation
C Compass Course
+W
000
015 W
015
005 W
020
Notes: <number>

## Slide 26: Computing Compass Corrections
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
T
V
M
D
C
+W
Memorize it!
You’re going to use it again and again and again!
Notes: <number>

## Slide 27: Back to Measuring Deviation
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
For each 15º - 30º, you need to:
  Know exactly what direction (magnetic) your boat is pointed.
  Compare with compass reading.
  Compute deviation.
Key to puzzle is knowing exactly what direction you’re headed.
There are several ways ...
Notes: <number>

## Slide 28: Example Way to Know Your Heading
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
In calm water with minimal current:
Remaining in vicinity of ATON …
Record both compass heading & relative bearing every 15° -- 30°.
Using TVMDC, compute deviation for each heading.
Known
Direction
Close to
Reliable
ATON
Charted
Object
6+ Miles
Distant
Means to Take
Relative
Bearing
Notes: <number>

## Slide 29: Measuring Relative Bearings: The Pelorus
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Mounted parallel to vessel’s keel with all-around view.
0º aligned with keel.
Align targets in sights.
Read relative bearing on scale.
Notes: <number>

## Slide 30: Compasses: Selection & Mounting
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Best you can afford.
Dial large enough for easy reading.
Style suitable for mounting location.
Handheld compass recommended for taking bearings.
Easily visible to helm.
Away from magnetic influences.
Align lubber line.
Determine deviation.
Recheck when new equipment installed.
Selection
Mounting
Notes: <number>

## Slide 31: Electronic Steering Compasses
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Use fluxgate transducers and digital displays.
Transducer can be mounted remotely, away from magnetic influences.
Feature automated deviation elimination!
Notes: <number>

## Slide 32: Local Magnetic Disturbances
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Compass still seems wrong?
In some locations there are local magnetic disturbances that can affect you compass.
Often noted on charts.
Notes: <number>

## Slide 33: All this sound complex?
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Practice ...
Practice ...
Practice!
Perhaps, but the best solution is:
Notes: <number>

## Slide 34: End Chapter 2
<number>
12 DEC 04
Basic Coastal Navigation - Chapter 2 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>