## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Advanced Coastal Navigation
Approved USCG Auxiliary - Department of Education Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Chapter 10
Navigation Reference Publications
Notes: <number>

## Slide 3: Navigation Reference Publications
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
We’ll cover:
  Four federal publications to assist mariner with navigation:
    United States Coast Pilot
    Light List
    Local Notice to Mariners
    Notice to Mariners
  Calculating of range of visibility of lights.
Notes: <number>

## Slide 4: Coast Pilot
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Supplements chart information.
  9 volumes
  Published by NOA/C&GS/NOAA.
Encyclopedia of local knowledge.
Contributions from:
  Multiple governmental agencies
  Individuals
Notes: <number>

## Slide 5: Topics in Coast Pilot
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Channel descriptions
Anchorages
Bridge & cable clearances
Currents
Tide and water levels
Prominent features
Pilotage
Towage
Weather
Routes
Dangers
Ice conditions
Wharf descriptions
Traffic separation schemes
Small-craft facilities
Federal regulations applicable to navigation.
Enough, already?
Notes: <number>

## Slide 6: Evaluating Voyage Alternatives
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Traveling from Buzzards Bay to Vineyard Sound.
Quick’s Hole is shorter.
Should you go that way?
Notes: <number>

## Slide 7: Coast Pilot Excerpt
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Quick’s Hole, between Pasque Island and Nashawena Island is the only passage between Vineyard sound and Buzzards Bay eastward of Cuttyhunk available for vessels of over 10 ft. draft.….. The channel is nearly straight with a width of about 0.2 mile….. The eastern side of Quick’s hole is foul and no attempt should be made to pass eastward of the lighted buoy. Felix Ledge, 0.2 mile off the eastern shore of Nashawena Island, is covered 16 ft and marked with a buoy. Lone Rock, covered 4 ft and marked with a buoy is off the northern entrance, about 0.7 mile.
Tides and Currents. - The mean range of the tide is 2.5 ft. at the south end and 3.5 ft. at the north end of Quick’s Hole. The tidal currents have considerable velocity, about 2 to 2.5 knots and a sailing vessel should not attempt to pass through unless with a strong favorable wind on a favorable current… With a strong westward current in Vineyard Sound there is a northward current through Quick’s Hole: with a strong eastward current the current sets southward through Quick’s Hole.
Maybe we’d better excerpt more ...
Notes: <number>

## Slide 8: Coast Pilot Excerpt
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
… “available for vessels of over 10 ft. draft ...
… channel is nearly straight with a width of about 0.2 mile ...
… tidal currents … about 2 to 2.5 knots ...
… sailing vessel should not attempt to pass through unless with a strong favorable wind on a favorable current ...
… with a strong westward current in Vineyard Sound there is a northward current through Quick’s Hole …”
Suggests that, unless you’ve got a strong, reliable engine, you should not attempt if there is a strong westward current running in Vineyard Sound.
Notes: <number>

## Slide 9: Light List
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
More complete information about ATONs than can be shown on chart.
Seven volumes cover the United States.
Describe ATONs in very specific detail
Notes: <number>

## Slide 10: Light List Appearance
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>

## Slide 11: Light List Details
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Number
  Assigned for reference
Name & location
Position
  L & Lo to facilitate location on chart
Characteristic
  Of light, if any
Height
  Of light above water
Range
  Nominal, nautical miles
Structure
  Description of appearance of aid
Remarks
  Fog signal, arc of visibility, radar reflector, etc.
Notes: <number>

## Slide 12: Visibility of Lights
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Three types of range of visibility:
Nominal Range:
  Maximum range in “clear” weather.
  Meteorological visibility of 10 nautical miles.
  Indicated on charts.
Luminous Range:
  Greatest range to be expected in prevailing meteorological visibility.
Geographic Range:
  Governed by curvature of earth.
Notes: <number>

## Slide 13: Luminous Range Diagram
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Diagram included in Light List
International Visibility Codes
0 < 50 yards
1 50 - 200 yards
2 200 - 500 yards
3 500 - 1,000 yards
4 1,000 yds to 1 NM
5 1 - 2 nautical miles
6 2 - 5.5 nautical miles
7 5.5 - 11 nautical miles
8 11 - 27 nautical miles
9 > 27 nautical miles
Notes: <number>

## Slide 14: Determining Luminous Range
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Buzzards Light:
  Nominal visibility = 17 NM
Prevailing visibility:
  2 NM (category 5/6)
Draw horizontal to luminous range scale.
Visibility estimate:
5 nautical miles
Notes: <number>

## Slide 15: Geographic Range
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Limitation of visibility due to earth’s curvature.
Depends on:
  Height of object
  Height of eye of observer
Use Table 6-2 in your text to estimate.
Example:
  Buzzards @ 67 ft high.
  Eye @ 10 ft.
  Visibility:
  13.1 nautical miles
From Table 6-2
Notes: <number>

## Slide 16: Calculating Actual Range of Visibility
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Actual range of visibility will be the lesser of:
  Luminous Range
  Geographic Range
What we know from past slides:
  Nominal range: 17 nautical miles
  Luminous range: 5 nautical miles
  Geographic range: 13.5 nautical miles
Therefore, the probable range of visibility would be: 5 nautical miles.
Notes: <number>

## Slide 17: Local Notice to Mariners
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Primary resource to update information on:
  ATONs
  Hazards to navigation
  Other items of interest to mariners
Needed to keep charts, Light Lists, Coast Pilots and other nautical publications up-to-date.
Published weekly.
Free from each Coast Guard District.
On the web: http://www.navcen.uscg.gov/lnm/
Notes: <number>

## Slide 18: Notice to Mariners
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Corrects NIMA and NOS charts
Uses information collected from many sources, including Coast Guard Local Notices
Contains only those chart corrections of interest to ocean going vessels.
On the web: pollux.nss.nima.mil/untm/
  Database query by date & chart.
Notes: <number>

## Slide 19: Broadcast Warnings
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Coast Guard broadcasts information too urgent to wait for LNTM:
  Broadcast Notice to Mariners
  Announced on VHF Ch 16
  Then, sent on VHF Ch 22A
Notes: <number>

## Slide 20: Cruising Guides
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Commercial cruising guides and other publications also provide valuable information.
  Most lack formal update information.
  Still need to rely on LNTM.
Notes: <number>

## Slide 21: End Chapter 10
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 10 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>