## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Advanced Coastal Navigation
Approved USCG Auxiliary - Department of Education Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Chapter 11
Fuel & Voyage Planning
Notes: <number>

## Slide 3: Fuel and Storage Planning
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Understand how to relate:
  Fuel consumption
  Fuel efficiency
… to compute:
  Effect of current on fuel usage
  Fuel Reserves
How to develop “Howgozit” planning chart
Notes: <number>

## Slide 4: Fuel Consumption Chart
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Relates vessel’s speed curve and engine fuel consumption data to fuel consumed at speed.
Vessel Speed Curve
Engine Fuel Burn Rate
Fuel Consumption Chart
Notes: <number>

## Slide 5: Charting the Data
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
First, develop the data:
  Engine RPM
  Speed Through Water
  Fuel Consumption Rate
Considerable effort
Data accuracy improves fuel planning process
Notes: <number>

## Slide 6: Fuel Consumption Data
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Published test results:
  Owner’s manuals & periodicals.
  Must verify for your vessel.
Measured data:
  Fuel flow meters are probably best.
  Measurement of fuel used after period of running - low tech but tedious.
  Do not trust fuel gauges.
Notes: <number>

## Slide 7: Fuel Efficiency
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Data most obviously plotted as FCR vs.speed.
Also useful to compute and graph fuel efficiency (MPG) vs.speed.
MPG = (Speed) / (FCR)
Notes: <number>

## Slide 8: Fuel Efficiency
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Aventura has typical displacement hull efficiency characteristics.
Efficiency levels off just under 6 knots, approaching Aventura’s hull speed (HS).
HS = 1.34 (LWL)½
Efficiency declines rapidly thereafter.
Notes: <number>

## Slide 9: Fuel Efficiency
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Planing hull vessels have very different efficiency curves.
Typically, efficiency is:
  Good at low speed.
  Declines deeply through transition to planing mode.
  Rises, again, when on plane; sometimes higher than at low speed.
Notes: <number>

## Slide 10: Range and Endurance
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Range:
  Distance a vessel can travel on a load of fuel.
Endurance:
  Time a vessel can operate on a load of fuel.
Both depend on how fast the vessel runs.
Basis: 200 Gal Fuel Capacity
Notes: <number>

## Slide 11: Range Chart
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Perhaps a more eye opening look at the data is on a chart.
It is clear that range is dramatically affected by engine speed.
So, too, is the amount of time the voyage will take!
Notes: <number>

## Slide 12: Other Efficiency Factors
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Fuel and water tank levels
Hull condition … recently repainted & clean?
Props … diameter, pitch & condition:
Weight of passengers & stores
Weight distribution
Trim tab settings
Winds
Sea state
Engine tune-up state
Engine ventilation & temperature
etc ...
Notes: <number>

## Slide 13: Fuel Reserves
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Calculations, so far, have left no reserves.
Not a wise approach to cruising.
No hard rules for setting reserve amounts.
Consider predictability of conditions.
Generally allow 10%-20%.
In the end, it’s up to the individual to decide.
Notes: <number>

## Slide 14: Range & Endurance: Effects of Reserves
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
As expected, both range and endurance reduced when making reserve allowances.
Basis: 200 Gal Fuel Capacity
Notes: <number>

## Slide 15: Effect of Current on Range
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Effects of current can be important.
  Impact range and ETA.
  Especially on slower boats.
Need to understand tradeoffs underway.
  Optimal throttle setting for conditions.
  Effect on reserves.
Notes: <number>

## Slide 16: Calculating Effect of Current on Range
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Plotting makes it easier to understand the effects.
Basis: 200 Gal Fuel Capacity
Notes: <number>

## Slide 17: Charted Effect of Current on Range
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notice that a maximum range occurs with foul current.
Optimum RPM increases slightly with increasing foul current.
Notes: <number>

## Slide 18: Keeping Track of Progress
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
We’ve covered fuel consumption tools.
  Useful for voyage planning phase.
Before departure:
  Verify fuel levels.
  “Stick” the tanks?
Need a tool to follow progress underway.
  HOWGOZIT chart is such a tool.
Notes: <number>

## Slide 19: HOWGOZIT Chart Preparation
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Similar to a “Danger Bearing”
Prepare chart frame.
Draw line for “No Reserve”
Draw line for “Reserve”, In this case, 20%
Notes: <number>

## Slide 20: HOWGOZIT Chart Underway
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Periodically plot fuel remaining.
OK if point is on or above “Reserve” line.
Concern if point between lines.
Problem if point below “No Reserve” line.
Notes: <number>

## Slide 21: Improving Fuel Management
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
General Planning
  Develop fuel vs. throttle setting curve.
  Consider voyage routing & timing to minimize foul currents, adverse weather.
  Determine fuel availability on route.
  Determine necessary fuel reserve.
  Consider speed vs. fuel consumption tradeoffs.
Notes: <number>

## Slide 22: Improving Fuel Management
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
While Underway
  Don’t trust gauges. Verify fuel levels before and during trip.
  Maintain a “HOWGOZIT Chart” or maintain a fuel log.
  Be prepared to divert to an alternate destination.
Notes: <number>

## Slide 23: Improving Fuel Management
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Maintenance
  Keep engines tuned.
  Clean bottom periodically.
  Fill tanks after each trip to minimize condensation.
Vessel Equipment; Consider installation of:
  Fuel tank cross-feeds.
  Fuel management system.
  Trim tabs.
Notes: <number>

## Slide 24: End of Chapter 11
<number>
16 DEC 04
Advanced Coastal Navigation - Chapter 11 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>