## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Advanced Coastal Navigation
Approved USCG Auxiliary - Department of Education Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Chapter 9
Radio Navigation
Notes: <number>

## Slide 3: Types of Radio Navigation
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
RDF: Radio Direction Finding
  Rarely used today
LORAN: LOng RAnge Navigation
GPS: Global Positioning System
RADAR: RAdio Detection And Ranging
Notes: <number>

## Slide 4: What You Will Learn
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Principles of LORAN-C and GPS.
How to use a navigation receiver for coastal piloting.
Principles of operation of RADAR.
Use of RADAR for collision avoidance.
How to plot RADAR targets.
Notes: <number>

## Slide 5: Radio Navigation
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Caution!
Radio navigation requires constant source of power.
Lightning strikes can destroy it all in an instant.
Provide an acceptable method for verifying DR.
Provide an acceptable source for LOP and FIX.
Provide good navigational aid.
Replace the DR plot.
Provide an independent means of navigation.
DOES
DOES NOT
Notes: <number>

## Slide 6: More Caution!
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Radio navigation heading outputs do not consider:
  Hazards to navigation.
  Land masses.
Headings to waypoints are only headings.
They may not be safe courses to steer!
  Verify course safety using your chart.
Notes: <number>

## Slide 7: LORAN-C
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
First reliable, affordable long-range navigation system.
To be maintained until 2010.
US & 1,000 miles offshore.
Some other countries.
Accuracy 0.1 - 0.25 mi.
Repeatable accuracy much better; ~75 ft.
Notes: <number>

## Slide 8: LORAN-C Principle of Operation
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
“Chains” of 3 - 5 land-based transmitters.
  Separated by several hundred miles.
  Master (M) & secondaries (W, X, Y & Z) transmit timed signals on 100 kHz.
Onboard LORAN-C receiver.
  Listens to all transmitters in chain.
  Measures “time differences” (TDs) between arrival of master and secondary signals.
  TDs equate to LOPs.
  Receiver selects best two LOPs for fix.
Notes: <number>

## Slide 9: LORAN-C Signal Anatomy
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Master
Pulses
Secondary
X Pulses
Secondary
Z Pulses
Master
Pulses
LORAN C Chain GRI = 89700 µ sec
1000 µ sec
Time Delay
Time Delay
Time Delay
Secondary
Y Pulses
8970-Y-49950
8970 = GRI (Group Repetition Interval)
Y = Identifies secondary transmitter
49950 = TD in µsec
µsec = one millionth of a second
Notes: <number>

## Slide 10: Northeast US LORAN-C Chain
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
M
W
X
Y
Z
M is the master transmitter.
W, X, Y & Z are secondaries.
Shaded portion indicates coverage area.
Notes: <number>

## Slide 11: LORAN-C Fix
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Two LORAN-C LOPs needed for fix.
9960-W-13370 TD LOP
9960-X-32200 TD LOP
LORAN-C fix complete.
Notes: <number>

## Slide 12: LORAN-C Accuracy
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Geometry a consideration:
  TD gradient (how far you are from transmitters).
  TD crossing angle considerations.
  Additional secondary phase factors (ASF).
Therefore, accuracy depends on location.
Notes: <number>

## Slide 13: LORAN-C Display
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Basic display shows TDs and identifies TDs in use.
Intersection of TD lines is a fix.
Fix should be periodically plotted on chart.
LORAN-C receivers also display L & Lo.
Notes: <number>

## Slide 14: LORAN-C Overprint
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
TDs are overprinted on most charts.
Appear as faint gray, light blue and magenta lines.
Display the Group Repetition Interval (GRI).
Notes: <number>

## Slide 15: Plotting a LORAN-C Fix
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Locate TDs on chart.
Need to interpolate between overprinted TDs.
You can estimate or use an interpolator card.
Position card so that scale aligns with printed TDs.
Mark the TD on the chart.
Notes: <number>

## Slide 16: GPS
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Global Positioning System
  Satellite-based
  Worldwide coverage
  Operable 1992
  Fully operational 1995
Maintained and operated by Department of Defense.
Notes: <number>

## Slide 17: GPS
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Provides:
  Three dimensional position.
  Velocity.
  Time.
Most accurate electronic navigational aid now generally available.
Notes: <number>

## Slide 18: GPS Segments
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Space segment:
  24 satellites orbiting @ 20,200 km.
Control segment:
  Ground based. Master control, 5 monitors & 3 antennas.
User segment:
  Receiver.
Notes: <number>

## Slide 19: How GPS Works - 1
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Basis of GPS operation is “triangulation” from satellites.
Notes: <number>

## Slide 20: How GPS Works - 2
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Receiver measures distance from satellite to receiver
Uses travel time of radio signals
Notes: <number>

## Slide 21: How GPS Works - 3
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Needs very accurate timing to measure travel time.
Achieved with some electronic tricks.
Notes: <number>

## Slide 22: How GPS Works - 4
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Must also know exactly where satellite located in space.
High orbits and careful monitoring are essential.
Monitoring and control done by ground monitoring and master control and transmitting antennas.
Notes: <number>

## Slide 23: How GPS Works - 5
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Finally, corrections applied for delays signal experiences traveling through atmosphere.
Notes: <number>

## Slide 24: GPS Spherical “LOPs”
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
One measurement puts us
somewhere on a sphere.
Two measurements put us
somewhere on a circle.
Three measurements put us at one of two points. (One usually deep in space & discarded.)
Fourth measurement needed for clock correction.
Notes: <number>

## Slide 25: GPS Receivers
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Acquire and process data from satellites to calculate position.
Switch satellites as necessary.
Manage system status and setup:
  Units, datum, etc.
Display basic info:
  Position, course, speed.
Notes: <number>

## Slide 26: More Than One GPS Accuracy
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Basic GPS
  With or without selective availability (SA)
DGPS
  Differential GPS
  USCG sponsored
WAAS
  Wide Area Augmentation System
  FAA sponsored
Notes: <number>

## Slide 27: Dilution of Precision
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
DOP measures satellite fix geometry quality.
As in any crossed bearing fix, prefer crossing angles near 90%.
Good
Geometry
Poor
Geometry
Notes: <number>

## Slide 28: Selective Availability
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
SA discontinued May 1, 2000.
Military still has ability to selectively “mess up” accuracy in specific areas.
SA On
Longitude
Latitude
SA Off
Longitude
Latitude
Notes: <number>

## Slide 29: DGPS
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Note: Great Lakes stations not shown.
Series of shore-based stations broadcast corrections to GPS signal.
  Uses former RDF stations.
Supplementary receiver needed.
Notes: <number>

## Slide 30: WAAS
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Primary purpose:
  Improved flight navigation.
  Enroute through precision approach.
Errors reduced:
  Signal distortion through ionosphere.
  Drift of atomic clocks in satellites.
  Drift of satellite orbits.
Additional satellites transmit extra info to specially equipped GPS receivers.
Notes: <number>

## Slide 31: Accuracy Specs
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
GPS - SA off
  < 30 meters 95% of time
  Coverage: World-wide
DGPS
  < 10 meters 95% of time
  Coverage: ~200 miles
WAAS
  < 2.5 meters 99.9% of time
  Coverage: World-wide
Notes: <number>

## Slide 32: Additional Receiver Displays & Functions
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Position Alarms.
Waypoint & route setup.
Bearing, range, ETA to waypoint.
Cross-track error (XTE) & graphics.
Track graphics & chart plotting.
Interface with autopilots & computers.
Notes: <number>

## Slide 33: Waypoints
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Named location stored in memory.
Key requirement for navigation capabilities.
Specified by entering L/Lo, saving current location or by cursor on map.
Used for “GOTO” navigation.
Notes: <number>

## Slide 34: Cross Track Error (XTE)
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Distance and direction the vessel drifted off intended track.
Shown numerically or by graphical display.
Used to drive steering decisions as in autopilot input.
Notes: <number>

## Slide 35: Routes
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Ordered string of waypoints used to define a cruise.
Created by listing existing waypoints or by point & click on chart graphic display.
Can be manipulated by reversing, editing, etc.
Notes: <number>

## Slide 36: Track & Chart Plotting
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Simplest is graphic display of history of positions.
More elaborate displays on graphical chart display.
Notes: <number>

## Slide 37: Alarms
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Typical alarms:
  Arrival
  Anchor Drag
  Off Course
  Accuracy
Notes: <number>

## Slide 38: Autopilot Connections
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Auto Pilot steers boat.
Receives course changes from GPS.
GPS derives course corrections from XTE and distance to go.
Notes: <number>

## Slide 39: Tide Predictions
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Uses tide data as in other computer programs.
Uses GPS positioning information to help select nearby tide & current stations.
Notes: <number>

## Slide 40: Computer Connections
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Several reasons for connections.
Upload waypoints & routes.
Real-time position-plotting on chart loaded on the computer.
Notes: <number>

## Slide 41: Navigation Receivers
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Cost may be a criterion
Generally get what you pay for
More features = higher price
Rapidly improving
Notes: <number>

## Slide 42: Criteria For Receiver Selection
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Size and legibility of display
Ease of use
Ease of data entry
Quality of owner’s manual
Ability to interface with other electronics
Technical features
Notes: <number>

## Slide 43: Antennas & Sensors
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Read owner’s manual to learn how to mount antenna.
  Generally needs to “see” the sky.
A sensor is receiver without controls or display screens.
  Provide GPS output for components, such as chart plotters or radar.
  Often look like antennas.
Notes: <number>

## Slide 44: Tips: Establishing Waypoints
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Do not place at exact location of ATON.
Take advantage of "long names".
Keep a log for reference.
Use large scale charts to determine positions.
Plot on chart.
Notes: <number>

## Slide 45: Tips: Using Waypoints
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
WP 02
WP 01
Check for hazards on legs between waypoints.
Establish some waypoints close to ATONs.
Use rounded-off coordinates for intermediate waypoints.
Verify distance and bearing between waypoints.
Notes: <number>

## Slide 46: Tips: Other GPS Use
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Practice during ideal conditions.
Use alarms sparingly.
Periodically check for malfunctions.
Periodically re-read owner’s manual.
Carry extra batteries.
Notes: <number>

## Slide 47: Tips: General Navigation
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Record position periodically in case receiver fails.
Do not rely on single means of navigation.
Take hand-held receiver as backup.
Have conventional paper charts.
Notes: <number>

## Slide 48: Tip: Sailing Upwind
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
XTE can be used to establish bounds for sailboat tacks.
Notes: <number>

## Slide 49: USCG Navigation Center (NAVCEN)
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Navigation Notes and Information
GPS & DGPS
LORAN C
Electronic Navigation
Maritime Telecommunications
Local Notice to Mariners (LNM)
Navigation Pubs and Documents
http://www.navcen.uscg.gov
Notes: <number>

## Slide 50: Radar
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Primary uses:
  Collision avoidance
  Navigation
Operation is self-contained:
  Transmits pulse
  Listens for return
  Displays return
Antenna
Transceiver
Display
Notes: <number>

## Slide 51: Radar Returns (Images)
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Strength depends on target reflectivity.
  Steel boat reflects better than fiberglass.
Displays bearing and range.
  Can show land contours, location of buoys and ships.
Max range depends on:
  Antenna height & transmitter power.
Min range depends on pulse width (“on” time).
  Approx 30 yds for small boats.
Notes: <number>

## Slide 52: Ship’s Head Up Display (SHU)
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Not tied to on-board navigation system.
  Unstabilized
Bearings are relative.
Inexpensive, most popular.
Small boat application.
Notes: <number>

## Slide 53: SHU Display
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
SHU
Range: 5NM
Ship’s Heading
Rings: 1 NM
Fixed Range Markers
Rotating Electronic
Bearing Line
Notes: <number>

## Slide 54: North-Up Display (NU)
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Tied to ships Nav system.
  Stabilized
Top of display is north (T or M).
Targets remain in place when ship turns.
“Heading Flash” indicates vessel bearing.
Rel bearings must be calculated.
More expensive; seen on larger vessels.
Notes: <number>

## Slide 55: NU Display
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
NU
Range: 5NM
Ship’s Heading Flash
North (T or M)
Rings: 1 NM
Fixed Range Markers
Notes: <number>

## Slide 56: Radar Calculations
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Relative Motion Plot (RMP)
  Plot of maneuvering vessel on M-board
Relative Motion (RM)
  Direction (DRM) & speed (SRM)
Closest Point of Approach (CPA)
  Time & distance
Target movement
  Course & speed
Notes: <number>

## Slide 57: Example Radar Calculations
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Altar making 5kn
SHU display
Target vessel observations:
  1000 hrs 322°R 7.3 mi (Altar hdg 112°M)
  1006 hrs 321°R 6.3 mi (Altar hdg 110°M)
  1012 hrs 316°R 5.3 mi (Altar hdg 111°M)
Notes: <number>

## Slide 58: Compute
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Relative Motion Plot (RMP).
  Plot of the maneuvering vessel.
  The DRM (direction of relative motion).
Closest Point of Approach (CPA).
Target movement (maneuvering vessel).
  Target Course.
  Target Speed.
Notes: <number>

## Slide 59: Radar Worksheet
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Enter basic data
Altar
5.0
Notes: <number>

## Slide 60: Radar Worksheet
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Altar
5.0
M1
1000
7.3
112
322
M2
1006
6.3
110
321
M3
1012
5.3
111
316
Enter basic data
Enter target observation data
Notes: <number>

## Slide 61: Radar Worksheet
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Altar
5.0
M1
1000
7.3
112
322
M2
1006
6.3
110
321
M3
1012
5.3
111
316
074º
071º
067º
Enter basic data
Enter target observation data
Calculate Target Brg
  ( Hdg + R Brg )
Notes: <number>

## Slide 62: Radar Worksheet
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Altar
5.0
M1
1000
7.3
112
322
M2
1006
6.3
110
321
M3
1012
5.3
111
316
074º
071º
067º
Enter basic data
Enter target observation data
Calculate Target Brg
  ( Hdg + R Brg )
Plot on M-Board
Notes: <number>

## Slide 63: Relative Motion Plot (RMP)
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Plot & label target posits.
M1/00
M2/06
M3/12
Scales:
Distance: 1=1M
Speed: 1=1 kn
Notes: <number>

## Slide 64
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
DRM = 271º
Relative Motion Plot (RMP)
Plot & label target posits.
Draw & measure direction of rel motion (DRM)
M1/00
M2/06
M3/12
Scales:
Distance: 1=1M
Speed: 1=1 kn
Notes: <number>

## Slide 65
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
2.1 M
DRM = 271º
Relative Motion Plot (RMP)
Plot & label target posits.
Draw & measure direction of rel motion (DRM)
Measure dist between observations.
M1/00
M2/06
M3/12
Scales:
Distance: 1=1M
Speed: 1=1 kn
Notes: <number>

## Slide 66
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
2.1 M
DRM = 271º
Relative Motion Plot (RMP)
Plot & label target posits.
Draw & measure direction of rel motion (DRM)
Measure dist between observations.
Return to worksheet.
M1/00
M2/06
M3/12
Scales:
Distance: 1=1M
Speed: 1=1 kn
Notes: <number>

## Slide 67: Radar Worksheet
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Altar
5.0
M1
1000
7.3
112
322
M2
1006
6.3
110
321
M3
1012
5.3
111
316
074º
071º
067º
Enter DRM from Mo-Board.
271
Notes: <number>

## Slide 68: Radar Worksheet
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Altar
5.0
M1
1000
7.3
112
322
M2
1006
6.3
110
321
M3
1012
5.3
111
316
074º
071º
067º
Enter DRM from Mo-Board.
Enter measured distance between observations.
271
2.1
Notes: <number>

## Slide 69: Radar Worksheet
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Altar
5.0
M1
1000
7.3
112
322
M2
1006
6.3
110
321
M3
1012
5.3
111
316
074º
071º
067º
Enter DRM from Mo-Board.
Enter measured distance between observations.
Calculate time between observations.
271
2.1
12 min
Notes: <number>

## Slide 70: Radar Worksheet
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Altar
5.0
M1
1000
7.3
112
322
M2
1006
6.3
110
321
M3
1012
5.3
111
316
074º
071º
067º
Enter DRM from Mo-Board.
Enter measured distance between observations.
Calculate time between observations.
Calculate SRM.
271
2.1
12 min
10.5
Notes: <number>

## Slide 71: Radar Worksheet
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Altar
5.0
M1
1000
7.3
112
322
M2
1006
6.3
110
321
M3
1012
5.3
111
316
074º
071º
067º
Enter DRM from Mo-Board.
Enter measured distance between observations.
Calculate time between observations.
Calculate SRM.
Return to M-Board to determine CPA.
271
2.1
12 min
10.5
Notes: <number>

## Slide 72: Closest Point of Approach (CPA)
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
M1/00
M2/06
M3/12
DRM = 271º
Scales:
Distance: 1=1M
Speed: 1=1 kn
Erect perpendicular to RMP from origin.
Notes: <number>

## Slide 73: Closest Point of Approach (CPA)
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
M1/00
M2/06
M3/12
DRM = 271º
Scales:
Distance: 1=1M
Speed: 1=1 kn
Erect perpendicular to RMP from origin.
Intersection with DRM is CPA.
CPA
Notes: <number>

## Slide 74: Closest Point of Approach (CPA)
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
M1/00
M2/06
M3/12
DRM = 271º
Scales:
Distance: 1=1M
Speed: 1=1 kn
Erect perpendicular to RMP from origin.
Intersection with DRM is CPA.
Measure distance, CPA to origin.
CPA
2.1 M
Notes: <number>

## Slide 75: Closest Point of Approach (CPA)
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
M1/00
M2/06
M3/12
DRM = 271º
Scales:
Distance: 1=1M
Speed: 1=1 kn
Erect perpendicular to RMP from origin.
Intersection with DRM is CPA.
Measure distance, CPA to origin.
Measure distance of last observation to CPA for TCPA.
CPA
2.1 M
4.9 M
Notes: <number>

## Slide 76: Closest Point of Approach (CPA)
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
M1/00
M2/06
M3/12
DRM = 271º
Scales:
Distance: 1=1M
Speed: 1=1 kn
Erect perpendicular to RMP from origin.
Intersection with DRM is CPA.
Measure distance, CPA to origin.
Measure distance of last observation to CPA for TCPA.
Return to worksheet.
CPA
2.1 M
4.9 M
Notes: <number>

## Slide 77: Radar Worksheet
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Enter distance to CPA.
Altar
5.0
M1
1000
7.3
112
322
M2
1006
6.3
110
321
M3
1012
5.3
111
316
074º
071º
067º
271
2.1
12 min
10.5
2.2
Notes: <number>

## Slide 78: Radar Worksheet
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Enter distance to CPA.
Enter bearing of CPA.
Altar
5.0
M1
1000
7.3
112
322
M2
1006
6.3
110
321
M3
1012
5.3
111
316
074º
071º
067º
271
2.1
12 min
10.5
2.2
001
Notes: <number>

## Slide 79: Radar Worksheet
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Enter distance to CPA.
Enter bearing of CPA.
Calculate relative bearing of CPA.
Altar
5.0
M1
1000
7.3
112
322
M2
1006
6.3
110
321
M3
1012
5.3
111
316
074º
071º
067º
271
2.1
12 min
10.5
2.2
001
249
Notes: <number>

## Slide 80: Radar Worksheet
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Enter distance to CPA.
Enter bearing of CPA.
Calculate relative bearing of CPA.
Enter distance to last obs.
Altar
5.0
M1
1000
7.3
112
322
M2
1006
6.3
110
321
M3
1012
5.3
111
316
074º
071º
067º
271
2.1
12 min
10.5
2.2
001
249
4.9
Notes: <number>

## Slide 81: Radar Worksheet
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Enter distance to CPA.
Enter bearing of CPA.
Calculate relative bearing of CPA.
Enter distance to last obs.
Calculate time to traverse.
Altar
5.0
M1
1000
7.3
112
322
M2
1006
6.3
110
321
M3
1012
5.3
111
316
074º
071º
067º
271
2.1
12 min
10.5
2.2
001
249
4.9
28 min
Notes: <number>

## Slide 82: Radar Worksheet
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Enter distance to CPA.
Enter bearing of CPA.
Calculate relative bearing of CPA.
Enter distance to last obs.
Calculate time to traverse.
Calculate TCPA.
Altar
5.0
M1
1000
7.3
112
322
M2
1006
6.3
110
321
M3
1012
5.3
111
316
074º
071º
067º
271
2.1
12 min
10.5
2.2
001
249
4.9
28 min
1040
Notes: <number>

## Slide 83: Radar Worksheet
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Enter distance to CPA.
Enter bearing of CPA.
Calculate relative bearing of CPA.
Enter distance to last obs.
Calculate time to traverse.
Calculate TCPA.
Return to M-Board.
Altar
5.0
M1
1000
7.3
112
322
M2
1006
6.3
110
321
M3
1012
5.3
111
316
074º
071º
067º
271
2.1
12 min
10.5
2.2
001
249
4.9
28 min
1040
Notes: <number>

## Slide 84: Target Movement
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Plot and label your vessel’s vector.
M1/00
M2/06
M3/12
DRM = 271º
Scales:
Distance: 1=1M
Speed: 1=1 kn
CPA
2.1 M
4.9 M
112
5 kn
Notes: <number>

## Slide 85: Target Movement
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Plot and label your vessel’s vector.
Plot & label relative motion vector.
M1/00
M2/06
M3/12
DRM = 271º
Scales:
Distance: 1=1M
Speed: 1=1 kn
CPA
2.1 M
4.9 M
112
5 kn
271
10.5 kn
Notes: <number>

## Slide 86: Target Movement
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Plot and label your vessel’s vector.
Plot & label relative motion vector.
Plot and measure target vessel’s vector.
M1/00
M2/06
M3/12
DRM = 271º
Scales:
Distance: 1=1M
Speed: 1=1 kn
CPA
2.1 M
4.9 M
112
5 kn
271
10.5 kn
254
6.1 kn
Notes: <number>

## Slide 87: Target Movement
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Plot and label your vessel’s vector.
Plot & label relative motion vector.
Plot and measure target vessel’s vector.
Return to worksheet to enter target vessel’s course & speed.
M1/00
M2/06
M3/12
DRM = 271º
Scales:
Distance: 1=1M
Speed: 1=1 kn
CPA
2.1 M
4.9 M
112
5 kn
271
10.5 kn
254
6.1 kn
Notes: <number>

## Slide 88: Radar Worksheet
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Complete the worksheet by entering target vessel’s course & speed.
Altar
5.0
M1
1000
7.3
112
322
M2
1006
6.3
110
321
M3
1012
5.3
111
316
074º
071º
067º
271
2.1
12 min
10.5
2.2
001
249
4.9
28 min
1040
6.1 Kn
254
Notes: <number>

## Slide 89: Interpreting Target Behaviors
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Proceeding due north, S = 9.0
North-Up radar display
Following target positions recorded:
Third example in text.
Notes: <number>

## Slide 90: Interpreting Target Behaviors
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Scales:
Distance: 4 = 1M
Speed: 1 = 2 kn
NU Display
Choose scales, Plot ranges/brgs.
Something has changed!
Plot RMPs.
Measure DRMs.
Calc SRMs.
M1/29
M2/35
M3/38
M4/41
M5/47
M6/53
DRM1 = 291º
DRM2 = 285º
SRM1 = (60x1.7)/9.0 = 11.3
SRM2 = (60x1.65)/15.0 = 6.6
Notes: <number>

## Slide 91: Interpreting Target Behaviors
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Scales:
Distance: 4 = 1M
Speed: 1 = 2 kn
NU Display
M1/29
M2/35
M3/38
M4/41
M5/47
M6/53
DRM1 = 291º
DRM2 = 285º
SRM1 = (60x1.7)/9.0 = 11.3
SRM2 = (60x1.65)/15.0 = 6.6
C = 000
S = 9.0
RM1
C1 = 291
S1 = 11.3
C1 = 321
S1 = 17.0
Plot & label your vessel’s course & speed.
Plot & label target RM1.
Plot, measure & label target vector1.
  Direction1: 321
  Speed1: 17.0
Notes: <number>

## Slide 92: Interpreting Target Behaviors
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Scales:
Distance: 4 = 1M
Speed: 1 = 2 kn
NU Display
M1/29
M2/35
M3/38
M4/41
M5/47
M6/53
DRM1 = 291º
DRM2 = 285º
SRM1 = (60x1.7)/9.0 = 11.3
SRM2 = (60x1.65)/15.0 = 6.6
C = 000
S = 9.0
RM1
RM2
C2 = 285
S2 = 6.6
C2 = 321
S2 = 10.0
Now, plot & label target RM2.
Finally, plot, measure & label target vector2.
  Direction2: 321
  Speed2: 10.0
What changed was speed, not direction!
Notes: <number>

## Slide 93: Using Radar
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Understanding radar displays takes practice.
Like any other navigation skill, you must practice in clear weather to become proficient.
Newer radar sets offer automation of some of the plotting functions.
Notes: <number>

## Slide 94: End Chapter 9
<number>
15 DEC 04
Advanced Coastal Navigation - Chapter 9 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>