## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Basic Coastal Navigation
Approved USCG Auxiliary - Department of Education Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Chapter 6
Piloting
Notes: <number>

## Slide 3: What You Will Learn
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Definitions of terms
Determination, plotting and utility of:
  Line-of-position (LOP)
  Visual fix
  Electronic fix
  Running fix
  Danger bearing
Notes: <number>

## Slide 4: Contrast: Piloting & DR
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Piloting
Position at an instant in time
Opportunities for Fixes limited
Dead Reckoning
Projects position into future
Can be used when Fixes not possible
Notes: <number>

## Slide 5: Piloting Defined
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Navigation involving frequent reference to charted landmarks.
Involves:
  Frequent comparison of real world to chart of both natural and man-made features.
  Reconstruction of relationships of direction, angular differences and distances to establish position of a vessel.
Notes: <number>

## Slide 6: Buoys & Piloting
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Fixed ATONs and charted, shore-based objects usually preferred for piloting.
Floating ATONs might be off station.
However, ATONs are built expressly to aid the navigator!
Simply be aware and suspicious of inconsistent information.
Notes: <number>

## Slide 7: Line of Position (LOP)
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Line, established by observation or measurement, on which a vessel can be expected to be located.
“I’m somewhere
on this line.”
LOP
Notes: <number>

## Slide 8: Types of LOPs
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
087°
100°
276°
Bearing from charted object
  Visual observation using hand-held compass, pelorus or by swinging the bow
  Radar bearing
Range
Distance from object
  Vertical angle
  Radar range
Notes: <number>

## Slide 9: Choosing Appropriate Objects
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Object must be charted and readily identifiable
  Closer over distant
  Taller over shorter
  Fixed over floating
  Range over single object
Plot carefully
Notes: <number>

## Slide 10: Plotting an LOP
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
1530
090
Select appropriate object.
Obtain bearing by most efficient means.
Plot and label bearing on chart.
  Time (military) above the line.
  Bearing (T) below the line.
Notes: <number>

## Slide 11: LOP Illustrated
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Select appropriate object.
Obtain bearing by most efficient means.
Plot and label bearing on chart.
Notes: <number>

## Slide 12: LOP by Range
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Select two fixed & charted objects in line.
Draw LOP.
Label with time only.
Notes: <number>

## Slide 13: Distance by Radar Observations
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Identify object on radar.
Determine distance using range rings.
Set drafting compass to distance.
Scribe arc using object as center.
Label:
  Time above line.
  Distance below line.
Notes: <number>

## Slide 14
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Distance by Radar Observations
Notes: <number>

## Slide 15: Distance by Vertical Angle
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
For a tall object of known height (h)
Angle (H) measured using a sextant:
Formula: d = h / (6076 x tan(H))
Angle (H)
Notes: <number>

## Slide 16: Uses For a Single LOP
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
LOP directly ahead or astern can determine whether vessel is on course.
  e.g. “running up or down a range”.
Pre-determined LOP may be used to identify a turning point.
Can be used, with DR plot, to create estimated position (EP).
Notes: <number>

## Slide 17: Estimated Position (EP)
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Draw and label LOP.
Draw dotted line, from LOP to DR position perpendicular to LOP.
  Represents location on LOP closest to DR
Identify EP with square.
Do not start new DR plot.
Notes: <number>

## Slide 18: Determining an EP
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
DR Position
LOP
EP
Notes: <number>

## Slide 19: Fixes
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
LOP 1
LOP 2
An accurate position determination.
Intersection of two or more lines of position.
1237
Notes: <number>

## Slide 20: Kinds of Fixes
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Two or more crossed bearings
Range and bearing
Two ranges
Two distances
Distance and bearing of an object
Passing close to a fixed aid to navigation
Bearing and line of soundings
Notes: <number>

## Slide 21: Fix by Range & Visual Bearing
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>

## Slide 22: Fix by Two Radar Distances
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>

## Slide 23: Running a Range
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Taking bearings while running range is an important technique
Running range keeps vessel in channel.
Bearings confirm position along course.
Turn bearings can be established in advance.
Notes: <number>

## Slide 24: Running a Range
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Range
Lights
Bearings started on this light to keep angle of intersection near 60º to 90º
Bearings shifted to this light to keep angle of intersection near 60º to 90º
Note turning bearing of 000º
Notes: <number>

## Slide 25: Running Fix (R FIX)
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Not always possible to get 2 LOPs at same time.
  Due to poor visibility or few charted objects.
Running fix (R FIX) may be possible.
  Relies on “advancing” LOP on same or different object taken at different time.
Notes: <number>

## Slide 26: Running Fix
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Select 1st object, obtain bearing, plot & label.
Later, take 2nd bearing on same or other object, plot & label.
“Advance” 1st LOP along DR line for distance run between bearings.
Point where advanced LOP crosses 2nd LOP is R FIX.
New DR plot is started from this point.
Notes: <number>

## Slide 27: R FIX Example
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
DR
1st LOP
2nd LOP
1st LOP
Advanced
Notes: <number>

## Slide 28: Doubling the Angle on the Bow
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
R FIX without the chart work.
Special case of R FIX on the same object.
Dist Run = Dist Off
“Angle on Bow” table for other angles.
Charted
Object
1st Brg

2nd Brg
2
Dist Run
Dist Off
Notes: <number>

## Slide 29: Danger Bearings
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
A kind of LOP used to avoid dangers.
  Shoals, sand bars, coral reefs, fish traps
Bearing plotted to visible object so as to stay clear of danger.
Objective to stay on safe side of DB.
Labeled to indicate safe side of DB:
  NLT (not less than) or
  NMT (not more than)
Notes: <number>

## Slide 30: Danger Bearing Plot
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
1200
Danger
Area
Charted
Aid
1200
DR Plot
1230
Danger Bearing
NLT 090
Notes: <number>

## Slide 31: Summary of Symbols
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
DR Plot
C 090
S 10.5
DR Position
0930
1000
LOP
045
1030
Est. Position
1030
270
1030
1030
Visual Fix
1100
1100
1100
130
045
Electronic Fix
1500 RADAR
Running Fix
R FIX
1030
Known Position
1420
Notes: <number>

## Slide 32: Most Probable Position (MPP)
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Coastal navigation is an art, not a science.
Navigators often have conflicting information.
MPP takes into account best information at hand.
What to include is a judgement call.
Notes: <number>

## Slide 33: Practical Tips
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Read, consider and test the ideas presented at the end of this chapter.
Only rarely do most navigators actually need to have frequent fixes.
You really do need to practice so you can be confident when the need does arise!
Notes: <number>

## Slide 34: Congratulations!
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
You have completed the six lessons of BCN.
We invite you to continue with: Advanced Coastal Navigation
This is the week to begin working on the “Cruise Problem”, Appendix 1A, in your Work Book.
GOOD LUCK !!
Notes: <number>

## Slide 35: End Chapter 6 End Basic Coastal Navigation
<number>
13 DEC 04
Basic Coastal Navigation - Chapter 6 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>