## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Advanced Coastal Navigation
Approved USCG Auxiliary - Department of Education Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Chapter 8
Tides and Tidal Currents
Notes: <number>

## Slide 3: What We’ll Learn
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Relevance of tide and tidal current information.
How to read & interpret tide and tidal current tables.
How to make tide and tidal current predictions.
How to use the information in voyage planning.
Notes: <number>

## Slide 4: Tides and Tidal Currents
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Tides: Vertical motion of water.
Tidal Currents: Horizontal motion of water.
Notes: <number>

## Slide 5: What We Know About Tides and Tidal Currents
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
They are periodic and predictable.
  Hour-by-hour
  Day-by-day
  Season-by-season
  Year-by-year
Result from gravitational effects of sun and moon.
Notes: <number>

## Slide 6: Effect of Sun & Moon on Tides & Tidal Currents
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
SUN
MOON
N
EARTH
Gravitational pull of moon and sun creates a tidal bulge as water moves toward body.
Opposite side bulge develops to establish equilibrium due to centrifugal rotational forces.
Force of sun only 44% that of moon due to distance.
Tidal day matches the lunar day
  24 hrs 50 min
Notes: <number>

## Slide 7: Sources of Tidal Information
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Tide and Tidal Current Tables:
  Formerly NOAA publications.
Private, specialty publications.
Newspapers & local publications.
Television & radio weather broadcasts.
Computer programs.
Notes: <number>

## Slide 8: Tides
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Vertical motion of water.
Notes: <number>

## Slide 9: Common Tidal Terms
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
High Water:
  Maximum height of tide.
Low Water:
  Minimum height of tide.
Tidal Range:
  Height difference between consecutive high and low water.
Notes: <number>

## Slide 10: Tidal Range Variations
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
MOON
MOON
SUN
EARTH
  Sun & Moon in Alignment: (Syzygy)
  Full or new moon
  Maximum tidal range
  “Spring” tides
Notes: <number>

## Slide 11: Tidal Range Variations
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
MOON
MOON
SUN
  Sun & Moon not aligned (in quadrature)
  Half moon
  Minimum tidal range
  “Neap” tides
EARTH
Notes: <number>

## Slide 12: Principal Tidal Patterns
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Diurnal: (Pensacola, FL)
Cycle of one lunar day - one high and one low tide.
Semidiurnal: (Boston, MA)
Cycle of one-half lunar day - two highs and two lows.
Mixed: (San Francisco, CA)
Large inequality in height of two highs or lows.
Notes: <number>

## Slide 13: Importance of Tide Info
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Safety:
  Avoid running aground.
  Choosing among alternate routes.
Clearance:
  Sufficient room under a bridge?
Anchoring:
  Determine scope of anchor rode.
  How much swing room is needed?
Tying to a Dock:
  Amount of slack needed in lines.
Notes: <number>

## Slide 14: Computation of Predicted Tides
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Computations tedious.
Computations, themselves, trivial.
Use of tables and worksheets reduces potential for errors.
Remember, tide calculations only estimate water height.
Also affected by wind.
Notes: <number>

## Slide 15: Using Tide Tables
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Tables 1, 2 & 3 used for tide calculations.
  Table 1: Daily times and heights of high and low tides for Reference Stations.
  Table 2: Tidal differences and other constants for Subordinate Stations.
  Table 3: Correction table for determining heights of tides at any time.
Notes: <number>

## Slide 16: Table 1: Daily Predictions
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Predictions for a specific reference station:
Time of each high and low tide for each day of the year.
  Standard time in 24 hour system.
  Must convert for daylight savings time.
Height of each high or low tide in feet & cm above or below datum.
Notes: <number>

## Slide 17: Reading Daily Predictions
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Month
Date/Day
Moon phase
Low tide
High tide
Another low tide
Another high tide
Notes: <number>

## Slide 18: Table 2: Tidal Differences
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Relates tide for a substation to a location with daily predictions.
Time and height differences given for highs and lows.
Notes: <number>

## Slide 19: Reading Tidal Differences
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Reference No.
Station Name
Location
Reference station
Time diffs
Height diffs/ratios
Height ranges
Average height
Notes: <number>

## Slide 20: Tide Worksheet
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Substation info.
Ref station info.
Time diffs
Height ratios
Reference tides
Calculated substation tides
Penikese
1 Jan 99
1103
Penikese
Newport
Newport
-0:17
-0:16
*0.97
*0.97
0001 -0.8
0642 4.8
1255 -0.7
1906 3.9
2345 -0.8
0625 4.7
1239 -0.7
1849 3.8
Notes: <number>

## Slide 21: Tide at any Time
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Determine 0900 Penikese tide:
Calc the time to rise: 0625 to 1239
Time from nearest tide @ 0625.
Calc range of tide
Height of nearest tide.
Penikese
Newport
-0:17
-0:16
1 Jan 99
1103
*0.97
*0.97
Newport
0001 -0.8
0642 4.8
1255 -0.7
1906 3.9
Penikese
2345 -0.8
0625 4.7
1239 -0.7
1849 3.8
Penikese
0900
1 Jan 99
Continue with tide worksheet.
6:14
2:35
5.4
4.7
6:14
2:35
5.4
Notes: <number>

## Slide 22: Table 3: Tide at Anytime
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Duration of rise or fall
Time from nearest high or low water
Range of tide
Correction to height
Used to “interpolate” between high and low tide heights for any time between predicted high and low times.
Notes: <number>

## Slide 23: Tide at any Time
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Penikese
Newport
-0:17
-0:16
1 Jan 99
1103
*0.97
*0.97
Newport
0001 -0.8
0642 4.8
1255 -0.7
1906 3.9
Penikese
2345 -0.8
0625 4.7
1239 -0.7
1849 3.8
Penikese
6:14
2:35
5.4
4.7
0900
1 Jan 99
Enter correction from Table 3.
Calculate height of tide from height of nearest tide.
1.9
2.8
Now, return to the tide worksheet:
Notes: <number>

## Slide 24: Avoid Common Calculation Errors
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Convert from daylight to standard time.
Be alert to date changes when calculating tides for subordinate stations.
Apply calculated tide differences correctly.
Remember that factors, denoted with an asterisk, must be multiplied, not added or subtracted.
Notes: <number>

## Slide 25: Computer Programs For Tide Predictions
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Tide table calculations not difficult, but:
  Time consuming.
  Easy to make errors .
Computer programs give quick and easy picture of day’s tidal pattern.
Predictions can be generated for several substations along planned route.
Notes: <number>

## Slide 26: Computer Predictions for Penikese Island
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
PENIKESE ISLAND,
1 January 1999
High Water
High Water
Low Water
2.3 Feet Above Charted Depth at 0900
Notes: <number>

## Slide 27: Tidal Current
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Horizontal flow of water due to tide.
Notes: <number>

## Slide 28: Effects of Tidal Current
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Tidal currents of only 1 or 2 knots can critically affect your voyage
  Fuel consumption planning
  Course to steer.
  Speed made good.
Notes: <number>

## Slide 29: Effect of Current
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
3.2 kn
5.2 kn
Consider a sailboat beating, S = 6 kn
  With 1 kn vs.
  Against 1 kn
Almost 2/3 better SMG running with the current!
Wind
Notes: <number>

## Slide 30: Tidal Current Terms
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Flood: Flow from seaward.
Ebb: Flow toward seaward.
Slack: Period of minimum / no current.
  Flood & ebb designations sometimes arbitrary in canals, between islands, etc.
  Time of max flows generally not same as high or low tide.
Notes: <number>

## Slide 31: Tidal Current Tables
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Based on predictions made by NOS.
Organized similarly to Tide Tables.
Locations of reference and subordinate stations usually different than Tide Tables.
Notes: <number>

## Slide 32: Five Current Tables
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Table 1 -- Daily Current Predictions at reference stations
Table 2 -- Current Differences and other constants
Table 3 -- Speed of Current at any Time
Table 4 -- Duration of Slack
Table 5 -- Rotary Currents
Notes: <number>

## Slide 33: Table 1: Daily Predictions
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Like tides, predictions for a specific reference station:
  Time of each slack, max flood & max ebb.
    Standard time, convert to daylight.
  Speed of each maximum.
Notes: <number>

## Slide 34: Reading Daily Predictions
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Time of Slack
Ebb or Flood
Time of Max Flow
Speed of Max Flow
Name of Reference
Current Directions
Notes: <number>

## Slide 35: Table 2: Current Differences
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Relates current for a substation to a location with daily predictions.
Time differences and speed ratios given currents.
Notes: <number>

## Slide 36: Reading Current Differences
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Reference No.
Station name
Location
Time differences
Speed ratios
Average speeds & directions
Notes: <number>

## Slide 37: Current Worksheet
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Header information
Time differences
Speed ratios
Reference currents
Calculate substation currents
Penikese
Pollack
27 Feb 1999
Pollack Rip
Penikese
050
254
-1:37
-:25
-:55
-:57
0.6
0.6
0408 1.8
0656 0
0954 1.7
1258 0
1639 2.2
1939 0
2236 1.6
0036 0
0343 1.1
0601 0
0857 1.0
1121 0
1614 1.3
1844 0
2239 1.0
2259 0
Notes: <number>

## Slide 38: Current at Any Time
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Use bottom section of the worksheet.
Compute interval between slack and desired time.
Compute interval between slack and max.
Note the max current for use in Table 3.
Penikese
Pollack
27 Feb 1999
Pollack Rip
Penikese
0343 1.1
0601 0
0857 1.0
1121 0
1614 1.3
1844 0
2239 1.0
2259 0
0408 1.8
0656 0
0954 1.7
1258 0
1639 2.2
1939 0
2236 1.6
0036 0
-1:37
-:25
-:55
-:57
0.6
0.6
050
254
Penikese
0900
27 Feb 1999
0221
0224
1.0
Notes: <number>

## Slide 39: Table 3A: Speed of Current at Any Time
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Find interval between slack and max.
Find interval between slack and desired time.
Find correction factor.
Notes: <number>

## Slide 40: Current at Any Time
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Return to the worksheet.
Insert the tabled correction factor.
Apply the correction factor to the max current.
Note the direction for the current.
Penikese
Pollack
27 Feb 1999
Pollack Rip
Penikese
0343 1.1
0601 0
0857 1.0
1121 0
1614 1.3
1844 0
2239 1.0
2259 0
0408 1.8
0656 0
0954 1.7
1258 0
1639 2.2
1939 0
2236 1.6
0036 0
-1:37
-:25
-:55
-:57
0.6
0.6
050
254
Penikese
0900
27 Feb 1999
0221
0224
1.0
1.0
254
1.0
Notes: <number>

## Slide 41: Table 4: Duration of Slack
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Table assumes slack duration related to maximum current speed.
Some inlets and bridges best transited when current is weak.
Notes: <number>

## Slide 42: Estimating Tidal Current
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Set and drift can also be estimated:
  Observation of water flow around stationary objects.
  Calculated as-you-go using DR & fix.
  Coast Pilot also provides useful data and information on currents.
Remember, current is seldom constant across a body of water.
Notes: <number>

## Slide 43: Computer Generated Tidal Current Graph
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
PENIKESE ISLAND
27 February, 1999
Slack Water
Slack Water
Maximum Ebbs
Maximum Floods
Notes: <number>

## Slide 44: Using a Current Diagram
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
For an eastbound vessel at 8 kts, place parallels on appropriate speed line.
Adjust parallel line on current diagram to find favorable time to start.
In this example, depart Gay Head about 1.5 hrs before flood begins to have fair current.
Notes: <number>

## Slide 45: Using Tidal Charts
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Tidal charts, like diagrams, are published in sets for selected bodies of water.
A set consists of one chart for each hour in the tidal current cycle.
Simply consult the chart for the time of interest.
Notes: <number>

## Slide 46: Final Notes
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Tide tables will aid you in:
  Determining vertical clearances.
  Anticipating expected depths.
  Choosing appropriate anchorage areas.
Current tables will aid in:
  Selecting the best departure times.
  Choosing among alternate routes.
  Planning to compensate for set and drift.
Notes: <number>

## Slide 47: End Chapter 8
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 8 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>