## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Advanced Coastal Navigation
Approved USCG Auxiliary - Department of Education Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Chapter 7
Current Sailing
Notes: <number>

## Slide 3: Current Sailing
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Process of determining and allowing for the effect of "current" on the motion of a vessel.
“Current” includes:
  Horizontal motion of water over the ground.
  Effect of wind & seas.
  Other error effects including steering, compass, speed curve, fouled bottom, etc.
Notes: <number>

## Slide 4: Navigator’s Objectives
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Determine the actual current affecting the vessel’s movement.
Improve DR positions with better estimated positions (EP).
Compensate for the effects of currents.
Notes: <number>

## Slide 5: Steps in Underway Navigation
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Start
Update DR Plot
Search for FIX Opportunities
Piloting
Use Visual Methods
Electronic Navigation
Use Shipboard Electronics
Celestial
Observations
Compare FIX With DR Plot
Compute Current
Set and Drift
Repeat this process every 30 minutes while underway
A Circular System
Notes: <number>

## Slide 6: Current Sailing Topics
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
How to determine the current.
Creating an EP using current.
Use of maneuvering (M) boards.
Standards for plotting.
Planning track (TR) and speed of advance (SOA).
Role of GPS.
Voyage planning.
Notes: <number>

## Slide 7: Basic Current Determination
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Compare fix with DR plot.
Difference is “current” Current has characteristics of:
  Direction: Set
  Speed: Drift
Actual direction and speed of vessel:
  Direction: CMG
  Speed: SMG
1500
1400
1500
C 065
S 6.0
Set 120º
Drift 1.5 kts
CMG 075º
SMG 7.0
Notes: <number>

## Slide 8: Choosing Your Workspace
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Current problems can be solved directly on a chart.
  Clutters chart.
  Scale may not work well.
Maneuvering (Mo) boards are convenient place to work.
Notes: <number>

## Slide 9: Maneuvering Board
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Ten equally spaced, concentric rings.
  Represent speed or distance.
36 bearing lines.
  1° divisions on outer ring.
Auxiliary scales
T/S/D calculator.
Notes: <number>

## Slide 10: Using “Mo” Board
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Choose a scale.
Plot course line.
Using parallels and dividers, plot current line.
Close triangle with resultant:
  TR / SOA or CMG / SMG
C 065
S 6.0
TR 075
SOA 7.0
Drift 1.5
Set 120
Scale 1:1
Notes: <number>

## Slide 11: Using Current for an EP
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
1500
1400
1500
C 065
S 6.0
Set 120º
Drift 1.5 kn
CMG 075º
SMG 7.0
1500
1600
C 065
S 6.0
Set 120º
Drift 1.5 kn
1600
Remember when we first determined the current?
Let’s move forward one hour in time and use the 1500 current to plot an EP at 1600.
Plot the current from the 1600 DR.
The end of the current line is our 1600 EP.
Notes: <number>

## Slide 12: What to do with EP?
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Remember, this is an EP, not a fix.
Do not start a new DR plot.
Continue the DR plot.
Annotate the chart to reflect the EP.
Notes: <number>

## Slide 13: EP w/ Current & LOP
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
1500
1600
C 065
S 6.0
Set 120º
Drift 1.5 kn
1600
Let’s go back to the last example from 1600.
Say we also got a LOP.
1st, estimate effect of current on DR.
2nd, drop a perpendicular to the LOP.
1600
295
Intersection is the EP.
Notes: <number>

## Slide 14: Working on the Chart
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Leave Quick’s Hole @ 1330 hrs
  C 213, S 5.0
Plot DR position every 30 min to 1500 hrs.
At 1450 hrs get a cross bearing fix:
  Cuttyhunk light brg is 355
  Buzzard’s Bay light brg 301
Compute set and drift.
Notes: <number>

## Slide 15: Doing One On a Chart
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Plot DR.
Plot fix.
Determine current.
Notes: <number>

## Slide 16: The Current Triangle
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Really a vector diagram.
  Each element has both magnitude and direction.
Adds vessel “course” head-to-tail with “current” to yield “track or CMG”.
Result independent of the order of addition.
Course
Course
Current
Current
TR/CMG
Notes: <number>

## Slide 17: Another Kind of Problem
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Knowing current, determine course to steer to arrive at destination.
  Destination (CMG) bears 050°.
  S = 8 kn.
  Current: Set = 130, Drift = 2 kn.
Determine C and SOA.
Notes: <number>

## Slide 18: Course to Steer & SOA
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Scale 1:1
TR 050
SOA 8.1
C 036
Drift 2.0
Set 130
S 8.0
Compass
Arc
Plot current.
Set compass to S = 8.0 and draw arc intersecting track.
Choose a scale.
Plot track.
Measure SOA and C.
Notes: <number>

## Slide 19: Let’s Do One More
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
This time, determine the C and S to maintain to achieve a specific track and SOA.
  ETD: 1015, ETA 1045.
  Destination bears 280°, 4.5 NM distant.
  Current: Set 150°, Drift is 3.0 kn.
Determine course to steer and speed to maintain?
(S = 60D/T = 60(4.5)/30 = 9.0 kn)
Notes: <number>

## Slide 20: Course to Steer & Speed
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Scale 1:1
TR 280
SOA 9.0
Drift 3.0
Set 150
C 292
S 11.2
Plot current.
Plot resultant course.
Choose a scale.
Plot track.
Measure C with parallels and S with dividers.
Notes: <number>

## Slide 21: Current w/ Multiple Legs
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Plot DR.
Plot fix.
Determine current.
Note: Number of DR legs doesn’t really matter.
Notes: <number>

## Slide 22: TR/SOA vs CMG/SMG
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
TR and CMG are nearly identical as are SOA and SMG.
  TR & SOA are a statement of intent, the result of planning.
  CMG & SMG are history, what actually happened.
Do you really care?
Notes: <number>

## Slide 23: How Accurate is Current Determination, Really?
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
We’ve assumed that current, determined once, doesn’t change.
In fact, it does.
  As we’ve determined it, it is historical.
  What we really want is a forecast.
  Future current depends on tidal current, location and other factors, all of which change.
Always use the best information you have.
Notes: <number>

## Slide 24: Current & GPS
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
GPS can directly calculate CMG, SMG, cross-track error (XTE), ETA, etc.
  Is there really a need to do conventional current sailing procedures?
Yes!
  Planning, especially in high current areas.
  Electronics fail.
  Problem: GPS does not measure current directly.
Notes: <number>

## Slide 25: End Chapter 7
<number>
14 DEC 04
Advanced Coastal Navigation - Chapter 7 Copyright ©2004 Coast Guard Auxiliary Association, Inc.
Notes: <number>