## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Auxiliary Communications Specialty (AUXCOM)
<number>
Chapter 10
Rescue 21
AUXCOM 2009 v0.98
Notes: <number>
US COAST GUARD AUXILIARY – Auxiliary Communications Specialty Course (“AUXCOM”)
2009 UPDATE, version 0.98
Slide 1. Chapter cover slide.
Chapter 10: “Rescue 21”
(no author notes).

## Slide 3: Chapter 10 Outline
AUXCOM – Auxiliary Communications Specialty Course
<number>
Introduction
Rescue 21
Rescue 21 Disaster Recovery System (DRS)
How Rescue 21 Works
Review Questions
Notes: Slide 2: Chapter 10 Outline
(no author’s notes).
<number>

## Slide 4: Introduction
Coast Guard has rising challenges
  Currently, responds to 60,000 emergency calls and saves about 5,000 people yearly
  August 2005, during Hurricane Katrina, the Coast Guard saved over 33,000 lives in 2 weeks
Maritime activity and waterway congestion increasing
  Both the size and the numbers of ships using the inland, coastal, and international waterways keep increasing
  Fishing vessels travel farther offshore
  Oil platforms are greater distances from shore
  Number of personal watercraft & time spent in recreational boating continues to grow yearly
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 3: Introduction
(no author’s notes).
<number>

## Slide 5: Rescue 21
AUXCOM – Auxiliary Communications Specialty Course
<number>
Rescue 21 Coverage, Autumn 2009
Rescue 21- being installed to meet growing challenges. When complete, the system will cover more than 95,000 miles of coastline, navigable rivers, and waterways in the continental United States, Alaska, Guam, Hawaii, and Puerto Rico.
Notes: Slide 4: Rescue 21
(no author’s notes).
<number>

## Slide 6: Rescue 21
Provides the communications infrastructure for:
  Search and Rescue
  Marine Safety and Security
  Maritime Law Enforcement
  Maritime Environmental Protection and Response
  Homeland Security
First life saved by Rescue 21 November 2005
First commissioned in Atlantic City, NJ, December 2005
Expected to complete deployment 2011.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 5: Rescue 21, continued
(no author’s notes).
<number>

## Slide 7: Rescue 21 – Search and Rescue
Features to reduce time between call and rescue:
  Radio Direction Finding (RDF) & Digital Selective Calling (DSC)
  Can detect weak signals (1 watt for 2 seconds); pinpoint location (+/- 2 degrees on line-of-bearing)
Digital information increases range & utility:
  In some areas, able to receive calls from 25-watt radios over 100 miles out to sea; can zero in on a 1-watt radio, 2 feet above the water, 20 miles offshore
  Clarity of distress calls improved
  Simultaneous monitoring of 6 channels
  Distress calls can be heard clearer through improved recording and playback features.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 6: Rescue 21 – Search and Rescue
(no author’s notes).
<number>

## Slide 8: Rescue 21 – Search and Rescue
Improves interoperability between federal, state, and local agencies
  improves data accuracy and routes information to appropriate responding units
Can determine if MAYDAY calls are false
  RDF can display if the call is coming from on the water or from on land - advances in tracing calls should immediately reveal most hoaxes
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 7: Rescue 21 – Search and Rescue
(no author’s notes).
<number>

## Slide 9: Rescue 21 - DSC
Supports Digital Selective Calling (DSC) for registered boaters
  DSC enables a mariner to press a “panic button” on a VHF-FM marine radio and automatically send a distress message
  Position information included if VHF radio interfaced with GPS
  When registered with a Mobile Maritime Service Identity (MMSI) DSC radio signals vital vessel information
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 8: Rescue 21 – DSC
(no author’s notes).
<number>

## Slide 10: Rescue 21 – Disaster Recovery System (DRS)
With 24 hours notice, a fully autonomous, rapidly deployable emergency communications package (DRS) can be deployed
  The Coast Guard has four sets of DRS: 3 stored in Chesapeake, VA & 1 stored in Pointe Reyes, California
  Each consists of a truck with transmitting equipment, a portable telescoping antenna tower, two satellite dishes, and auxiliary generators
  Can restore lost communications from man-made or natural disasters
  Provides voice and data connectivity, caller position location and communications recording, archiving, and retrieval
  Connects to the Coast Guard Data Network (CGDN+) via satellite.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 9: Rescue 21 – Disaster Recovery System (DRS)
(no author’s notes).
<number>

## Slide 11: Rescue 21 – Disaster Recovery System (DRS)
AUXCOM – Auxiliary Communications Specialty Course
<number>
During recent CA wildfires, CG provided emergency communications.
Notes: Slide 10: Rescue 21 – Disaster Recovery System (DRS)
(no author’s notes).
Photos from CG support on 2009 CA wildfires.
<number>

## Slide 12: Rescue 21 – How It Works
Boater has a standard VHF-FM marine radio – DSC will help and is recommended
Distress/MAYDAY call is sent
  The station receiving it will automatically record and digitize it.
  One or more Rescue 21 towers with RDF LOB from where MAYDAY signal originated
  MAYDAY audio & LOB are sent to the closest Ground Center(s); planes, helicopters, and boats are immediately dispatched, even across regional boundaries. The resources will fly down the LOB to find the person(s) in distress
“Rescue 21 takes the search out of search and rescue.”
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 11: Rescue 21 – How It Works
(no author’s notes).
<number>

## Slide 13: Rescue 21 – How It Works
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 12: Rescue 21 – How It Works
(no author’s notes).
<number>

## Slide 14: Rescue 21 – How It Works
Watchstanders use radio monitors and two display monitors
  One monitor display shows the location of mariners based on their lines of bearing from the Remote Fixed Facility (RFF)
  Calls on Channel 16 appear red on the screen. Normal mariner calls are in blue
Rescue 21 consists of:
  46 Coast Guard region/sector command centers
  220 stations/field offices equipped with:
    Rescue 21 hardware & software & supporting communications equipment
    About 3,000 handheld communication devices
    350 communication towers.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 13: Rescue 21 – How It Works
(no author’s notes).
<number>

## Slide 15: Some Chapter Questions
AUXCOM – Auxiliary Communications Specialty Course
<number>
QUESTION | ANSWER
How many miles of coastline, navigable rivers, and waterways in the continental United States, Alaska, Guam, Hawaii, and Puerto Rico will Rescue 21 cover when completed? | 
A (___) watt transmission for about (___) seconds can be received by the Rescue 21 system. | 
What is “MMSI”? | 
What is “DRS”? | 
How is a mariner in distress found when Rescue 21 has only one line of bearing? | 
95,000.
1-watt, 2-seconds.
Maritime Mobile Service Identity – a unique number assigned to the DSC radio (and thereby links to vessel information).
“Disaster Recovery System” – a portable communications station.
Rescue units traverse the LOB.
Notes: <number>
Slide 14: Some Chapter Questions
ANIMATIONS
Five questions are displayed.
[CLICK] to display each answer in sequence. Font change used to simulate human handwriting.
After last answer displayed, one more [CLICK] to next screen (allows instructor pause for last answer).
* * * * * * * * * * (end comments).

## Slide 16: End of Chapter 10
AUXCOM – Auxiliary Communications Specialty Course
<number>
Questions?
Next: Chapter 11, “Communications Staff Officers”
Notes: <number>
Slide 15: End of Chapter 10
(no author’s notes).
Last slide of this deck intended to be normally displayed.

## Slide 17
AUXCOM – Auxiliary Communications Specialty Course
<number>
(This slide intentionally left blank.)
Notes: <number>
Slide 16: endslide
This slide is not intended to be normally displayed.