## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Auxiliary Communications Specialty (AUXCOM)
<number>
Chapter 8
Coast Guard Communications
AUXCOM 2009 v0.98
Notes: <number>
US COAST GUARD AUXILIARY – Auxiliary Communications Specialty Course (“AUXCOM”)
2009 UPDATE, version 0.98
Slide 1. Chapter cover slide.
Chapter 8: “Coast Guard Communications”
(no author notes).

## Slide 3: Chapter 8 Outline
AUXCOM – Auxiliary Communications Specialty Course
<number>
General Introduction
Frequency Allocation
CG All-Station Broadcasts
CG Communications Organization – District
CG Communications Watchstanding
Review Questions
Notes: Slide 2: Chapter 8 Outline
(no author’s notes).
<number>

## Slide 4: General Introduction
Reliable communications essential to all CG operations – from SAR to port security, and more
Auxiliary communications most uses CG radiotelephone procedures – which are designed for simplicity and clarity
Uniformity is important – become familiar and adhere to common procedures
There are organizational, operational and administrative standpoints to this topic.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 3: General Introduction
(no author’s notes).
<number>

## Slide 5: Frequency Allocations
ITU (International Telecommunication Union) allocates radio frequencies to various radio services per covenant
“Radio Services” include radio navigation, maritime mobile, broadcast commercial radio/TV, etc. – much competition for available spectrum
NTIA (National Telecommunications and Information Administration) assigns allocated frequencies to US Gov’t agencies (advised by IRAC, Interdepartment Radio Advisory Committee, working for the President)
FCC (Federal Communications Commission) assigns allocated frequencies to civil/non-federal agencies
CG Commandant (G-SCT) responsible for surface agencies frequency assignments … (next slide)
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 4: Frequency Allocations
(no author’s notes).
<number>

## Slide 6: Frequency Allocation
AUXCOM – Auxiliary Communications Specialty Course
<number>
(SYMBOLIC DEPICTION OF FREQUENCIES)
Coast Guard “Frequency Plan” (index of frequencies used, utilization procedures and circuit listings, etc.) contained in COMDTINST M2400.1
Notes: Slide 5: Frequency Allocation
ANIMATIONS
Basic slide displayed with allocation chart and representative spectrum illustrations.
[CLICK] info balloon displayed.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 7: CG All-Station Broadcasts
CG makes Urgency, Safety and scheduled marine information broadcasts; broadcasts have vital info to maritime interests in US waters and vicinity (i.e., the Caribbean)
Urgency Broadcasts (“Pan-Pan”) – sent on VHF Channel 16, 2182 KHz and (possibly) district working frequency
  Broadcasts upon receipt, 15 minutes later, then in regular broadcast schedule (as below)
Safety Broadcasts (“Sécurité”) – sent on VHF Channel 22 and 2670 KHz; similar schedule to Urgency, as above
Scheduled Broadcasts – sent on VHF Channel 22 and 2670 KHz; schedule times vary according to the District
  Important Notices to Mariners, oceanographic information, meteorological warnings, etc.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 6: CG All-Station Broadcasts
(no author’s notes).
<number>

## Slide 8: CG Communications Organization (District)
AUXCOM – Auxiliary Communications Specialty Course
<number>
District Commander publishes all District-wide communications instructions and plans in the District Operations Plan (OPLAN).
District Commander designates the Chief, Telecommunications Branch (dt) responsible for planning, organization, operation, inspection, supervision and coordination of all communications activities in the District.
Auxiliarists should be familiar with applicable information published in the OPLAN.
Notes: Slide 7: CG Communications Organization (District)
ANIMATIONS
Slide displayed with simulated OPLAN binder and info balloon.
[CLICK] binder dissolves into smaller, open binder. New, appropriate info balloon shown.
[CLICK] next slide.
* * * * * * * * * (end comments).
<number>

## Slide 9: CG Communications Organization (District)
CAMS (Communication Area Master Stations) – overall control of all radio circuits, speak for/with authority of Area Commander; maintain responsibility for circuit discipline
Group/Activity commands – maintain discipline on radiotelephone circuits within AOR (“Area of Operations Responsibility”), speak with authority of Commander
Individual radio-equipped units – each have their own communications responsibility; guidance obtained from Area commander, but unit commanding officers/OICs are responsible for maintaining reliable comms capability
Any radio-equipped unit, ashore, afloat or aloft, speaks with the authority of its commander/OIC
Operational on-scene commanders might also have proper delegated authority.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 8: CG Communications Organization (District), continued
(no author’s notes).
<number>

## Slide 10: CG Communications Organization (District)
Communication equipment varies by location, mission and type of vessels supported
VHF-FM most common (and is carried in all CG small boats); HF SSB often found; in vessels, larger size usually implies more equipment options – i.e., larger cutters might carry satellite terminals, VHF and UHF AM, weather fax, data fax and more; buoy tenders usually carry HF SSB
Watchstanders usually operate landline data circuits in the station telecommunications center
CG callsigns vary – geographic (COMMSTA SAN DIEGO); small boats use 5-6 numbers (1st 2 are boat length), e.g., 47452, 25894; larger vessels are named (“Eagle,” “Rush”) – text has more details.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 9: CG Communications Organization (District), continued
(no author’s notes).
<number>

## Slide 11: CG Communications Watchstanding
Full-time communications watch maintained by all CG Groups and many stations – monitoring local distress and calling frequencies
Auxiliary communicators are a welcome and needed augment to the CG staff – interested Auxiliarists should follow their chain to see how to attain qualification
“Group and Stations Communications Watchstander Qualification Guide,” COMDTINST M16120.7 – the same criteria the CG uses for their own watchstanders – is used for the Auxiliary
Possible additional qualification criteria defined by the District or Station, plus local area knowledge needed.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 10: CG Communications Watchstanding
(no author’s notes).
<number>

## Slide 12: Some Chapter Questions
AUXCOM – Auxiliary Communications Specialty Course
<number>
QUESTION | ANSWER
Since the Coast Guard is a government agency, the frequencies it uses are assigned by whom? | 
The Coast Guard makes three (3) types of “all station” broadcasts. What are they? | 
Who is responsible for coordination and organization of communications with a District? | 
Radio operators speak with whose authority? | 
Watchstander qualification at a station usuallyrequires completing what criteria? | 
NTIA, as advised by IRAC and managed by G-SCT
Distress (“Mayday”), Urgency (“Pan-Pan”), Safety (“Securite”)
Chief, Telecommunications Branch
Unit Commander or Officer-In-Charge.
Those contained in the qualification guide.
Notes: <number>
Slide 11: Some Chapter Questions
ANIMATIONS
Five questions are displayed.
[CLICK] to display each answer in sequence. Font change used to simulate human handwriting.
After last answer displayed, one more [CLICK] to next screen (allows instructor pause for last answer).
* * * * * * * * * * (end comments).

## Slide 13: End of Chapter 8
AUXCOM – Auxiliary Communications Specialty Course
<number>
Questions?
Next: Chapter 9, “Radio Direction Finding”
(SYMBOLIC DEPICTION OF FREQUENCIES)
Notes: <number>
Slide 12: End of Chapter 8
(no author’s notes).
Note the symbolic depiction of radio frequency spectrum and assignments – intended to convey a sense of the few frequencies actually used of the available spectrum, and through careful analysis of the picture, how some frequencies are shared by differing services and users, permitting cross-group communications.
This is the last typically-displayed slide of this deck.

## Slide 14
AUXCOM – Auxiliary Communications Specialty Course
<number>
(This slide intentionally left blank.)
Notes: <number>
Slide 13: endslide
This slide not typically displayed.