## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Auxiliary Communications Specialty (AUXCOM)
AUXCOM – Auxiliary Communications Specialty Course
<number>
Chapter 1
Basic Marine Radiotelephone Systems, Nomenclature and Theory
AUXCOM 2009 v0.98
Notes: <number>
AUXILIARY COMMUNICATIONS SPECIALTY COURSE (“AUXCOM”)
2009 UPDATED VERSION
* * * * * * * * * *
History:
2009/12/10 – final review copy published, mjb. Comments solicited.
* * * * * * * * * *
INSTRUCTOR NOTES
This course is substantially similar to the previous AUXCOM, “refreshed” to remove some obsolete content, add some important new content (esp. addition of a new Chapter 10, “Rescue 21” and Chapter 11, “Roles of the Communication Staff Officer). In the case of the PowerPoints to accompany the course refresh, substantial effort has been made to improve the overall graphic presentation of material.
Note that many slides in the PowerPoints contain “animations” – that is, objects will appear, disappear and in some cases, move, based on clicks to advance the presentation (either mouse clicks, or PgDn). The PPT author will provide a “click script” for each such slide in these notes to aid the instructor.
The PowerPoints typically follow the flow of the updated textbook. In some cases, select material has been re-arranged from the flow in the text in order to make a better presentation. In more cases, the PPT material is somewhat – or even substantially – less detailed than the text, due to the nature of the content being presented. On-screen notes will alert the class and instructor when the author feels there is sufficient divergence between the PPT and text.
No audio is included in these presentations. No video. No links to external files or content. All chapter presentations are self-contained. All graphics (photos and drawings) are part of the presentation.
* * * * * * * * * * (end comments)

## Slide 3: Chapter 1 Outline
AUXCOM – Auxiliary Communications Specialty Course
<number>
Introduction
Communications Nomenclature
Characteristics of Radio Waves
Types of Circuits
Radiotelephone Systems
Single Sideband
156-162 MHz VHF-FM System
Cell Phones
Citizens Band Service
Remote Base Station Operation
Radio Repeaters
Antennas
Review Questions
Notes: Slide 2: Outline
(No author notes).
<number>

## Slide 4: Introduction
AUXCOM – Auxiliary Communications Specialty Course
<number>
Emphasis in this chapter – basic understanding of radio and radiotelephone systems
Radio-equipped units of the Auxiliary normally operate radios as certified facilities authorized by the Coast Guard to operate on specific government frequencies.
Notes: Slide 3: Introduction
(No author notes).
<number>

## Slide 5: Communications Nomenclature
AUXCOM – Auxiliary Communications Specialty Course
<number>
Cycle
  Single, complete reversal of an alternating current
Frequency
  Number of cycles per second
  Measured in “Hertz” (Hz)
  1 Hz = 1 cycle per second
Amplitude
  Measure of wave height from zero to its maximum and is indicative of the strength of the wave. Watts are the measure of power.
Notes: <number>
Slide 4: Communications Nomenclature (I)
ANIMATIONS
slide with text & empty graphic displayed.
[CLICK] 3 cycles displayed in sequence, last cycle remains onscreen after completing animation
[CLICK] next slide.
* ** * * * * * * * (end comments).

## Slide 6: Sine Wave, Cycles and Frequency
AUXCOM – Auxiliary Communications Specialty Course
<number>
3 CYCLES IN 1 SECOND MAKES THIS A 3-HERTZ FREQUENCY.
Notes: <number>
Slide 5: Sine Wave, Cycles and Frequency
ANIMATIONS
Basic slide displayed (instructor describes). Corresponds to Figure 1-1 in the text.
[CLICK] balloon displays with note on 3-Hz.
[CLICK] next slide.
* * * * * * * * * * (end comments).

## Slide 7: Frequency Magnitudes
AUXCOM – Auxiliary Communications Specialty Course
<number>
HERTZ | PREFIX | ABBREVIATION | EXAMPLE
0 - 999 | (none) | Hz | 300 Hz
1000 – 999,999 | K (“Kilo”) | KHz | 2182 KHz
1,000,000 – 999,999,999 | M (“Mega”) | MHz | 156.8 MHz
1,000,000,000 – 999,999,999,99 | G (“Giga”) | GHz | 2 GHz
“2182 KHz” is an international standard distress frequency
Equivalent to 2,182,000 Hz, 2.182 MHz or 0.2182 GHz. Customarily referred to as “2182 KHz”
Notes: Slide 6: Frequency Magnitudes
(No author notes).
<number>

## Slide 8: More Communications Nomenclature
AUXCOM – Auxiliary Communications Specialty Course
<number>
Frequency Spectrum
  “Spectrum”: range of frequencies
    “Audio Spectrum” (“AF”): 15 – 15,000 Hz
    “Radio Spectrum” (“RF”): 30,000 Hz – 30,000 MHz
      For convenience, and related to their varying characteristics, the RF spectrum is divided into “bands” (see next slide)
      Remember, 30,000 MHz = 300 GHz
      Note that the bands are divided by powers of 10 of the frequency.
Notes: <number>
Slide 7: More Communications Nomenclature
(No author notes).

## Slide 9: Frequency Spectrum Bands
AUXCOM – Auxiliary Communications Specialty Course
<number>
FREQUENCY RANGE | BAND NAME | AUXILIARY INTEREST | EMERGENCY FREQUENCIES
3 – 30 KHz | VLF – Very Low Frequency |  | 
30 – 300 KHz | LF – Low Frequency |  | 
300 – 3000 KHz | MF – Medium Frequency | 2 – 3 MHz | 2182 KHz
3 – 30 MHz | HF – High Frequency | 3 -28 MHz | 
30 – 300 MHz | VHF – Very High Frequency | 156 – 162 MHz (Marine VHF) | Channels 16, 70 (121.5 MHz) (243 MHz)
300 – 3000 MHz | UHF – Ultra High Frequency |  | 406 MHz
3 – 30 GHz | SHF – Super High Frequency |  | 
30 – 300 GHz | EHF – Extremely High Frequency |  | 
Notes: <number>
Slide 8: Frequency Spectrum Bands
(No author notes).

## Slide 10: Radio Wavelengths
AUXCOM – Auxiliary Communications Specialty Course
<number>
Wavelength
  Radio travels speed of light (called “c”)
  each cycle a “wave”
  186,000 miles/second (300,000,000 meters/second)
  “Wavelength” is distance traveled by a single radio wave in 1 cycle, in meters (ex: “2-meter band”)
  Wavelength depends on frequency ( λ = c/f )
  3 MHz radio frequency has a wavelength of 300 meters (i.e., 300 = 300,000,000/3,000,000)
  156.8 MHz radio frequency has a wavelength of approximately 2 meters.
Notes: Slide 9: Radio Wavelengths
(No author notes).
<number>

## Slide 11: More Nomenclature
AUXCOM – Auxiliary Communications Specialty Course
<number>
Bandwidth
  Portion of frequency band occupied by an RF signal
  in FM: width of band of frequencies where radiated power appears
  in SSB: equal to highest audio modulating frequency used
  FCC regulates radios to a specific frequency tolerance
Day / Night (Communications Definitions)
  “Day”: 2 hours after local sunrise to 2 hrs before local sunset at transmitter – unless otherwise indicated
  “Night”: 2 hours before local sunset to 2 hrs after local sunrise at transmitter – unless otherwise indicated.
Notes: <number>
Slide 10: More Nomenclature
(No author notes).

## Slide 12: More on Bandwidth
AUXCOM – Auxiliary Communications Specialty Course
<number>
NARROW BANDWIDTH
WIDE BANDWIDTH
BANDWIDTH CONTROL IS IMPORTANT.
THE RADIO FREQUENCY SPECTRUM
HAS MANY COMPETING USES.
THE FCC REGULATES
RF ALLOCATIONS
IN THE US.
MARINE RADIOTELEPHONE
USE DEMANDS ONLY A SMALL PART OF THE SPECTRUM.
MARINE VHF IS HERE.
Notes: Slide 11: More on Bandwidth
ANIMATIONS
Base slide with empty chart, amplitude versus frequency.
[CLICK] “Narrow Bandwidth” bar displayed. Note how close to 3 KHz the bar stays. The internal coloring is intended to show greatest intensity at the chosen frequency, but that some radio emissions exist above and below that frequency.
[CLICK] “Wide Bandwidth” bar displayed.
[CLICK] US Frequency Allocations chart displayed. Note that each horizontal band is 10x the frequency range of the one above it. Each radio service is marked with a color and show on its frequency assignment. Explanatory balloon also displayed. Note that no comparable version of this chart exists in the text.
[CLICK] Previous explanatory balloon disappears. Pink circle crosses to straddle the marine VHF band. Small explanatory balloon displayed.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 13: Radio Waves / Intensity
AUXCOM – Auxiliary Communications Specialty Course
<number>
Radio Waves
  Reflection
  Refraction
Intensity
  Intensity diminishes rapidly …inversely proportional to the square of the distance from the source (i.e., 2x distance = ¼ intensity)
  Example (at right): a low-power handheld VHF radio may only have a range of a few miles (as illustrated by the diminishing intensity of the color).
Notes: <number>
Slide 12: Radio Waves / Intensity
(No author notes).

## Slide 14: Wave Types
AUXCOM – Auxiliary Communications Specialty Course
<number>
Radio waves propagate along altitude-related “paths” classified as:
  Ionospheric (“Sky”) Waves – portion of signal radiated here
    Ionosphere: 50 – 250 miles altitude
    Depending on conditions, may reflect or refract radio waves – reflected waves return to earth
    Condition vary greatly (day vs. night)
  Tropospheric Waves
    Troposphere: 5 miles high (poles), 11miles (equator)
    Air masses: refraction & reflection (temperature, moisture)
  Ground Waves
    Stay close to the surface of the Earth
    Propagate without Ionospheric reflection or refraction.
Notes: Slide 13: Wave Types
(No author notes).
<number>

## Slide 15: Sky Waves and the Ionosphere
AUXCOM – Auxiliary Communications Specialty Course
<number>
SKY WAVE REFLECTS
FROM IONOSPHERE
SKY WAVE REFRACTS FROM IONOSPHERE
Notes: <number>
Slide 14: Sky Waves and the Ionosphere
ANIMATIONS
Base slide displayed with two-ship-ocean with ionosphere sketch.
[CLICK] Skywaves reflecting from ionosphere. Repeats 3 times ship-to-ship.
[CLICK] Skywaves refracting from ionosphere. Text may refer to this as penetration.
[CLICK] next slide.
* * * * * * * * * * (end comments).

## Slide 16: MF Propagation Characteristics
AUXCOM – Auxiliary Communications Specialty Course
<number>
GROUND WAVE
SKY WAVE
SKIP ZONE
SKIP DISTANCE
Beyond a few miles, nearly all communications in the MF band are made by means of the sky wave.
Notes: <number>
Slide 15: MF Propagation Characteristics
ANIMATIONS
Base slide with with two-ship-ocean and ionosphere sketch displayed.
[CLICK] animation of 3 transmissions, comprised of skywaves (red) & ground waves (yellow). When the transmissions end, the last set remains displayed. Note that radio waves radiate in circular (or spherical) waves; the ground waves on this slide attempt to depict this. The “straight line” sky wave depiction is for convenience, not realism.
[CLICK] label for sky wave. Progressive clicking for labels allows the instructor to speak the material.
[CLICK] label for ground waves.
[CLICK] label and line for skip zone.
[CLICK] label and line for skip distance.
[CLICK] next slide.
* * * * * * * * * * (end comments)

## Slide 17: Day/Night Ionosphere and Skywaves
AUXCOM – Auxiliary Communications Specialty Course
<number>
THE IONOSPHERE IS NOT A SIMPLE RADIO BARRIER, BUT A COMPLEX, MULTI-LAYERED STRUCTURE THAT CHANGES ITS ALTITUDE AND COMPOSITION FROM DAY TO NIGHT DUE TO THE SUN’S INFLUENCE.
DURING THE DAY, THE IONOSPHERE LOWERS AND AN ADDITIONAL LAYER IS FORMED. HIGHER FREQUENCIES (SHORTER WAVELENGTHS) ARE USED TO PROPAGATE THE SKYWAVE BY SKIP.
AT NIGHT, THE HIGHER FREQUENCIES WILL GENERALLY NOT PROPAGATE WELL, AS THEY WILL REFRACT RATHER THAN REFLECT, AND THE SIGNAL WILL BE LOST.
AT NIGHT, LOWER FREQUENCIES (LONGER WAVELENGTHS) ARE USED FOR SKYWAVE PROPAGATION BY SKIP.
Notes: Slide 16: Day/Night Ionosphere and Skywaves
ANIMATIONS
Base slide is displayed with two-ship-ocean and daytime-sky ionosphere sketch displayed. Ionosphere is depicted as a layered structure, suggesting its real nature.
[CLICK] explanatory balloon displayed.
[CLICK] explanatory balloon displayed.
[CLICK] daytime reflective transmissions animation (3x). Line format suggests “short wavelengths.”
[CLICK] Sketch reformats as a night-sky picture.
[CLICK] Short-wavelength transmission depicts night-sky refraction, with explanatory balloon displayed.
[CLICK] Depicts longer-wavelength transmission (line format suggests this with longer dashes).
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 18: VHF Propagation Characteristics
AUXCOM – Auxiliary Communications Specialty Course
<number>
Straight-line, line-of-sight; range dependent on heights of antennas (curve of earth and visible horizon) – 25 miles or more can be obtained with sufficiently high antennas.
VHF-FM WAVES BEAMED SKYWARDS WILL PENETRATE THE IONOSPHERE DAY AND NIGHT.
RADIO HORIZON IS 15% FARTHER THAN VISIBLE HORIZON. DETAILS IN TEXT.
Notes: <number>
Slide 17: VHF Propagation Characteristics
ANIMATIONS
Slide with two-ship-ocean graphic displayed.
[CLICK] VHF straight line transmissions (3x). One remains displayed when complete.
[CLICK] explanatory balloon on ionosphere penetration displayed.
[CLICK] explanatory balloon on radio horizon displayed.
[CLICK] next slide.
* * * * * * * * * * (end comments).

## Slide 19: Simplex and Duplex Circuits
AUXCOM – Auxiliary Communications Specialty Course
<number>
#!@
Simplex Send & Receive
156.8 MHz (Ch 16)
Duplex Send & Receive
161.8 MHz & 157.2 MHz (Ch 24)
Notes: <number>
Slide 18: Simplex and Duplex Circuits
ANIMATIONS
slide with basic graphic displayed.
[CLICK] Simplex legend displayed. Instructor can discuss topic.
[CLICK] back and forth transmissions. Final transmission is simultaneous from both stations, results in a collision. Timing and pause allows instructor to elaborate.
[CLICK] displays duplex legend.
[CLICK] duplex transmissions, ends with one set displayed. Instructors note color signifies frequency, no collisions on simultaneous transmissions.
[CLICK] next slide.
Corresponds to Figure 1-5 in text.
* * * * * * * * * * (end comments).

## Slide 20: Radiotelephone Systems
AUXCOM – Auxiliary Communications Specialty Course
<number>
Two Marine Voice Systems
  Ship-to-Ship, Ship-to-Shore communications
  SSB: Single Sideband, 3-30 MHz range
  VHF-FM, 156-162 MHz
  Not all potential frequencies in the ranges above are used (VHF, for instance, uses “channels” of designated frequencies rather than directly dialing a frequency)
Three (3) Basic Functions Provided
  Safety, Operational, Business.
Notes: <number>
Slide 19: Radiotelephone Systems
(no author notes).

## Slide 21: Radiotelephone System Functions
AUXCOM – Auxiliary Communications Specialty Course
<number>
(1st Function) – Safety – Highest Priority
  International Distress & Calling Frequencies
    2182 KHz in 2-30 MHz
    156.8 MHz (Channel 16) in VHF-FM
    used for calling and answering
    maintain radio watch / maximum potential stations
  Weather, notices and other safety information broadcasted.
Notes: Slide 20: Radiotelephone System Functions
(no author notes).
<number>

## Slide 22: Radiotelephone System Functions
AUXCOM – Auxiliary Communications Specialty Course
<number>
(2nd Function) – Operational
  Navigation, movement or operation of vessels
(3rd Function) – Business
  Economic or commercial purposes of the vessel.
Notes: Slide 21: Radiotelephone System Functions
(no author notes).
Photo: Tug with very large barge in tow in relatively narrow channel abreast of Sandy Hook, NJ, at entrance to NY Harbor.
<number>

## Slide 23: SSB System Overview - Basics
AUXCOM – Auxiliary Communications Specialty Course
<number>
Relatively long-range band
  Range depends on transmitter power
  FCC regulates to 150 Watts
Congestion in many areas
Subject to interference (natural and man-made)
Skip common (especially at night) – may overwhelm local contacts
Frequencies in this 2-30 MHz band are available for other services: facsimile, Morse, radio printer, data transmission, digital selective calling and public correspondence.
FREQUENCY | USE | AREAS
2003 KHz | SHIP-TO-SHIP | GREAT LAKES
2182 KHz | DISTRESS AND SAFETY CALLING | ALL
2638 KHz | SHIP-TO-SHIP | ALL
2670 KHz | COAST GUARD PUBLIC LIAISON | ALL
2738 KHz | SHIP-TO-SHIP | ALL OTHER
2830 KHz | SHIP-TO-SHIP | GULF OF MEXICO
SHIP-TO-SHIP FREQUENCIES ARE ALSO USED FOR BUSINESS. |  | 
Notes: <number>
Slide 22: SSB System Overview – Basics
(no author notes).

## Slide 24: SSB System Overview - Safety
AUXCOM – Auxiliary Communications Specialty Course
<number>
2182 KHz as “International Distress and Calling Frequency” is key – widely monitored (“guarded”); excellent chance of being heard
Additional simplex frequencies available for distress and safety communications: 4125, 6215, 8291, 12290, 16420 KHz.
Notes: Slide 23: SSB System Overview – Safety
(no author notes).
<number>

## Slide 25: Sidebands
AUXCOM – Auxiliary Communications Specialty Course
<number>
A simple carrier wave signal, with no modulation, has an amplitude peak at the carrier wave frequency.
A modulated signal, with information superimposed on the carrier wave, creates two equivalent, but frequency-shifted sidebands.
The sideband at lower frequencies to the carrier wave is called the Lower Sideband (“LSB”). The other, the Upper Sideband (“USB”).
The carrier wave and sidebands each take power to transmit. The carrier requires 2/3 the total wattage.
2/3 OF TOTAL POWER
1/6
1/6
To make the transmission more efficient, only one of the sidebands is actually transmitted. This is “Single Sideband” (“SSB”) radio. The receiver reconstitutes the signal by adding back a synchronized carrier wave it generates internally.
The choice of which sideband to transmit typically depends in what frequency range you are operating in by general agreement.
LSB
USB
Notes: <number>
Slide 24: Sidebands
ANIMATIONS
Basic slide with empty amplitude vs. frequency chart displayed.
[CLICK] display of unmodulated carrier wave and carrier wave on chart, with some explanatory text.
[CLICK] display of AM modulated signal, sidebands, explanatory text. Note that the varying intensity of color in the sidebands is meant to illustrate the fact that the sidebands span a range of frequencies, but the majority of power is in a central range.
[CLICK] display of power distribution among carrier and sidebands.
[CLICK] display of USB only – shows signal using SSB conserves power.
[CLICK] next slide.
* * * * * * * * * * (end comments).

## Slide 26: SSB vs. AM
AUXCOM – Auxiliary Communications Specialty Course
<number>
SSB has many advantages over AM:
  Minimizes distortion (phase errors)
  Increases effective power (only sideband transmitted)
  Doubles available channels (halves bandwidth demand)
  Reduces interference (multiple carriers heterodyne = squeals and howls; SSB suppresses the carrier).
Notes: Slide 25: SSB vs. AM
(no author notes).
<number>

## Slide 27: VHF Overview
AUXCOM – Auxiliary Communications Specialty Course
<number>
VHF Uses Frequency Modulation (FM)
  Superior to AM, but wider bandwidth
  156 – 162 MHz, frequencies assigned as “channels” for convenience, FCC tightly controls utilization. Most channels are simplex, some are duplex
  Line-of-sight, range depends on heights of transmitting & receiving antennas, can range up to 25 miles (hand-helds, usually 1-2 miles)
  FCC limit 25 Watts; 1 Watt for short range communications (to avoid congestion)
  Channels available for weather, commercial and non-commercial use.
Notes: Slide 26: VHF Overview
(no author notes).
<number>

## Slide 28: Selected VHF Channels Overview
AUXCOM – Auxiliary Communications Specialty Course
<number>
CHANNEL | FREQUENCY | USE / DESCRIPTION
09 | 156.450 MHz | COMMERCIAL USE (SHIP-TO-SHIP AND SHIP-TO-COAST); ALTERNATE CALLING CHANNEL FOR RECREATIONAL VESSELS
13 | 156.650 MHz | BRIDGE-TO-BRIDGE
16 | 156.800 MHz | INTERNATIONAL SAFETY, DISTRESS AND CALLING
21A | 157.050 MHz | COAST GUARD WORKING FREQUENCY
22A | 157.100 MHz | COAST GUARD LIAISON/WORKING FREQUENCY
23A | 157.075 MHz | COAST GUARD WORKING FREQUENCY
70 | 156.525 MHz | DIGITAL SELECTIVE CALLING
MORE VHF CHANNELS AND FREQUENCIES LISTED IN TEXT.
Notes: Slide 27: Selected VHF Channels Overview
(no author notes).
<number>

## Slide 29: Cell Phones
Cell phones are not preferable to VHF-FM radios
  Cell phone coverage on the water is not consistent
  The Coast Guard cannot monitor cell phone frequencies
  Cell phones are intended for private communications
  The great advantage of the VHF-FM radio is that all receivers in the area can receive a distress call and respond if they are able to.
AUXCOM – Auxiliary Communications Specialty Course
<number>
IN ONE RECENT (12/2009) EXAMPLE, THE CG ULTIMATELY RESCUED THE 4-PERSON CREW OF A SAILBOAT SEVEN MILES OFFSHORE IN FLORIDA , IN BAD WEATHER AND ROUGH SEAS. THE CREW HAD ONLY A CELL PHONE WITH POOR RECEPTION FOR COMMUNICATIONS, WHICH DELAYED RESCUE RESPONSE (VIA INITIAL RELAY FROM ONSHORE FRIENDS) AND IMPAIRED BOTH LOCATING THE DISTRESSED VESSEL AND COORDINATION WITH CG SAR UNITS. NEARBY GOOD SAMARITAN VESSELS WITH VHF HELPED THE CG ACTION.
Notes: Slide 28: Cell Phones
(no author notes).
<number>

## Slide 30: Citizen’s Band (CB)
AUXCOM – Auxiliary Communications Specialty Course
<number>
27 MHz band, 40 channels, both AM and SSB modes, 5 Watts maximum power. Extremely crowded.
NOT recommended for safety purposes – use VHF (recommendation also applies to FRS, GMRS):
  no emergency weather or marine information broadcasts
  no radio watch required
  foreign or US government vessels do not use
  transmitter power limitation
  Coast Guard does not support.
Notes: <number>
Slide 29: Citizen’s Band (CB)
(no author notes).

## Slide 31: Remote Base Station
The Coast Guard (and many commercial operators) enhances its (usually VHF) communications capabilities by using remotely-operated base stations
  Paired radio receivers & transmitters located on radio towers or the tops of buildings (“high sites”) for longer range operations
  A CG communications hub might have multiple high sites available, each selectable for use
    A base station hub control console selects frequencies at the remote site(s) & provides audio and control functions to the operator
  Some high sites consist of multiple receivers and switchable transmit frequencies (several channels may be monitored simultaneously). These systems may extend the usable communications distances many hundreds of miles from the base station hub.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 30: Remote Base Station
(no author notes).
<number>

## Slide 32: Repeaters
AUXCOM – Auxiliary Communications Specialty Course
<number>
VHF-FM receiver / transmitter
Receives one frequency, transmits received signal on a different frequency (duplex circuit)
Usually elevated as high as possible; handheld range can be increased up to 50 miles with repeaters
INPUT FREQUENCY
OUTPUT FREQUENCY
NOTE: REPEATER FREQUENCIES ARE NOT THE SAME AS MARINE VHF FREQUENCIES.
Repeaters are a substantial investment; seek approval before establishment
Extremely useful in emergency or disaster situations
“Net” use – coordinate actions and operations
May support additional services, such as connection to telephone systems (“autopatch”) and digital data services.
Notes: <number>
Slide 31: Repeaters
ANIMATIONS
Explanatory text displayed, basic repeater graphic displayed.
[CLICK] animation of stations and repeater transmissions.
[CLICK] second block of explanatory text displayed.
[CLICK] next slide.
* * * * * * * * * * (end comments).

## Slide 33: Antennas
AUXCOM – Auxiliary Communications Specialty Course
<number>
HF antennas vary considerably
  Shipboard: often a long whip
  Land/Fixed: wire or directional beam
  Seek specialist assistance
VHF: smaller, more easily installed
  Higher = more coverage (“radio horizon” further away)
  Shipboard: usually fiberglass whip
  Rated by “gain factor” (3, 6 or 9 dB – higher gain means more horizontal concentration of beam energy radiating from the antenna); “dB” means “decibel”
  Higher-gain antennas require more vessel stability (sailboats usually 3 dB [due to heel], runabouts typically 6 dB and larger boats 9 dB).
Notes: Slide 32: Antennas
(no author notes).
<number>

## Slide 34: Vertical Antenna Gain Patterns
AUXCOM – Auxiliary Communications Specialty Course
<number>
3 dB
6 dB
9 dB
Notes: <number>
Slide 33: Vertical Antenna Gain Patterns
ANIMATIONS
1. Basic slide with antenna graphic displayed
2. [CLICK] 3db pattern lobes pulse (3x). After pulsing, last one remains in view.
3. [CLICK] 6db pattern lobes pulse (3x). After pulsing, last one remains in view.
4. [CLICK] 9db pattern lobes pulse (3x). After pulsing, last one remains in view.
5. [CLICK]. 3,6,9 db lobe patterns (right side only) superimposed for relative comparison.
6. [CLICK]. Next slide.
Note that the depicted gain patterns are for general-discussion relative comparison only, and do not represent a technically- accurate lobe shape. The gain pattern lobe colors are used on subsequent slides for continuity.
* * * * * * * * * * (end comments)

## Slide 35: Antenna Gain: Roll and Pitch
AUXCOM – Auxiliary Communications Specialty Course
<number>
ROLL AND PITCH CAN CAUSE SIGNAL LOSS WITH NARROW-BAND HIGH-GAIN ANTENNAS.
LOWER-GAIN ANTENNAS ARE LESS AFFECTED BY ROLL AND PITCH IN NORMAL COVERAGE AREAS.
SAILBOATS WILL HEEL AND SHOULD NOT USE HIGH-GAIN MASTHEAD ANTENNAS.
Notes: <number>
Slide 34: Antenna Gain: Roll and Pitch
ANIMATIONS
Slide with two-ship-ocean graphic displayed.
[CLICK] 9db emissions lobe displayed – intended to show rolling ship and high-gain antenna might direct radio energy away from receiving antenna.
[CLICK] 6 db emissions lobe displayed – along with 9db lobe for comparison – intended to show lower-gain antenna better for rolling ships
[CLICK] previous picture cleared, graphic of heeling sailboat (superimposed side-to-side heeling) with high-gani 9db lobe and explanatory text that sailboats should not use high-gain antennas.
[CLICK] next slide.
* * * * * * * * * * (end comments)

## Slide 36: More on Antennas
AUXCOM – Auxiliary Communications Specialty Course
<number>
VHF on Land: more choices on antenna types (based on coverage desired): directional or omni-directional
Lighting protection: arresters, grounding, disconnection/depowering during storms
Radio stations consist of 3 main components: power source, radio equipment and antenna. The antenna feed line is a critical element: proper selection, installation and maintenance required for peak efficiency
Antenna safety: locate away from power and telephone lines, cautions during installation and in case of antenna falling; FCC cautions on RF radiation exposure.
Notes: <number>
Slide 35: More on Antennas
(no author notes).
NOTE: after 2000, FCC upped emphasis on reducing/eliminating RF radiation exposure reduction which could be touched on here. Too detailed to go in to in depth – essential message is, siting and other antenna parameters should be done with professional care to reduce or eliminate RF exposure to humans.
* * * * * * * * * * (end comments).

## Slide 37: Some Chapter Questions
AUXCOM – Auxiliary Communications Specialty Course
<number>
QUESTION | ANSWER
The band named “Very High Frequency” covers what frequency range? | 
Express 2.182 MHz in kilohertz. | 
What is the typical range of VHF-FM communications? | 
What is a most important characteristic of VHF-FM communications? | 
The bridge tender will most likely be listening to which VHF channel? | 
30 - 300 MHz
2182 KHz
Up to 25 miles, line-of-sight, depending on height of antenna. Handhelds, 1-2 miles.
They are line-of-sight frequencies.
Channel 13
Notes: <number>
Slide 36: Some Chapter Questions (1 of 2)
ANIMATIONS
Five questions are displayed.
[CLICK] to display each answer in sequence. Font change used to simulate human handwriting.
After last answer displayed, one more [CLICK] to next screen (allows instructor pause for last answer).
* * * * * * * * * * (end comments).

## Slide 38: More Chapter Questions
AUXCOM – Auxiliary Communications Specialty Course
<number>
QUESTION | ANSWER
What is the marine VHF-FM distress and calling channel? | 
What is the HF SSB distress and calling frequency? | 
Why is Class D Citizens Band radio unreliable for boaters? | 
What is a radio repeater? | 
List the three basic communications functions of the marine radiotelephone system in priority order. | 
Channel 16, 156.8 MHz
2182 KHz
No CG watch, low power, no weather/information broadcasts.
A station that receives on one frequency and retransmits on another & can be a relay, range extender or offer other services.
Safety, Operations, Business
Notes: <number>
Slide 37: More Chapter Questions (2 of 2)
ANIMATIONS
Five questions are displayed.
[CLICK] to display each answer in sequence.
Following display of final answer, [CLICK] to advance slide.
* * * * * * * * * * (end comments).

## Slide 39: End of Chapter 1
AUXCOM – Auxiliary Communications Specialty Course
<number>
Questions?
Next: Chapter 2, “Voluntarily Installed Marine Radiotelephone Station Regulations”
Notes: <number>
Slide 38: End of Chapter 1
(no author notes).
INSTRUCTOR NOTE: THIS IS LAST NORMALLY-DISPLAYED SLIDE OF THE DECK.

## Slide 40
AUXCOM – Auxiliary Communications Specialty Course
<number>
(This slide intentionally left blank.)
Notes: <number>
Slide 39: endslide
(no author notes).