## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Auxiliary Communications Specialty (AUXCOM)
<number>
Chapter 7
The Radiotelephone Log
AUXCOM 2009 v0.98
Notes: <number>
US COAST GUARD AUXILIARY – Auxiliary Communications Specialty Course (“AUXCOM”)
2009 UPDATE, version 0.98
Slide 1. Chapter cover slide.
Chapter 7: “The Radiotelephone Log”
(no author notes).

## Slide 3: Chapter 7 Outline
AUXCOM – Auxiliary Communications Specialty Course
<number>
General Introduction
Minimum Coast Guard Requirements
Log Sections
The Log Section
The Message File Section
The Reference File Section
Operator Notes
Review Questions
The purpose of this chapter is to explain how to fulfill CG requirements using a standard log book format and organization.
Notes: Slide 2: Chapter 7 Outline
(no author’s notes).
<number>

## Slide 4: General Introduction
Radio Logs and Formal Message Logs must be maintained by owner or operator of radio facility
If mobile station is in communication with a fixed land station, land station keeps log (see Chapter 5)
If two mobile stations are in communications, then they keep logs.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 3: General Introduction
(no author’s notes).
<number>

## Slide 5: Minimum CG Requirements
Ledger or log book, tape recorder or computer – retention policy for all media is the same
If written, use ink; be legible, readable and easy to understand
Transcripts of tapes, hard copies of computer files are often generated
A log book binder (or binders) is often used.
AUXCOM – Auxiliary Communications Specialty Course
<number>
LOGS MAY VARY IN DETAILS PER POLICIES OF THE CG STATION IN QUESTION.
Notes: Slide 4: Minimum CG Requirements
(no author’s notes).
<number>

## Slide 6: Logbook Sections
AUXCOM – Auxiliary Communications Specialty Course
<number>
The Log section contains communication records (see next slide).
The Message File section contains all recorded messages sent or received.
The Reference File section contains assorted information which might be required for communications.
Notes: Slide 5: Logbook Sections
ANIMATIONS.
Empty slide (title only) displayed.
[CLICK] simulated ring-style logbook displayed, open to “Log” section with explanatory balloon.
[CLICK] simulated logbook opened to “Messages” section overlays previous.
[CLICK] simulated logbook opened to “Reference” section overlays previous.
[CLICK] next slide.
* * * * * * * * * * (end comments).
1.
<number>

## Slide 7: The Log Section
AUXCOM – Auxiliary Communications Specialty Course
<number>
Use this log style or acceptable equivalent format. CG requires following entries:
Vessel name (each page)
Vessel call sign (each page)
Page number sequence
Date of entry(ies)
Local Time Zone abbreviation
Time radio watch is begun
Time radio watch ends or is interrupted
Frequency used or guarded
Station called or calling
Message reference number or call summary
Operator’s signature.
Required when operating as a “government station.”
Notes: Slide 6: The Log Section
ANIMATIONS
Basic slide displayed with simulated logbook opened to communications log page.
[CLICK] dissolve of larger simulated logbook; display of relevant info and a smaller image.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 8: The Log Section (Detail)
AUXCOM – Auxiliary Communications Specialty Course
<number>
Sea Breeze
25894
1
04-Jul
(2009)
1500
1507
VHF 16
Wind Dancer
Urgency – adrift / sails damaged, no engine
Q
MJB
Box sizes are for guidelines and neatness – use as many as needed for clarity and essential details.
Might sign once per page covering all entries; also possible for multiple watchstanders to sign as a group at bottom.
Notes: Slide 7: The Log Section (Detail)
ANIMATIONS.
Basic slide displayed with empty communications log page.
[CLICK] longer-running animation progressively fills in log page entries: vessel name, call sign, page number, local time symbol, date/time, etc.
[CLICK] displays info balloon on use of boxes (multiline entries).
[CLICK] displays info balloon on signatures.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 9: The Message File Section
AUXCOM – Auxiliary Communications Specialty Course
<number>
Use this section to file and hold all recorded messages sent and received by the station. The Coast Guard requires the message pages to be numbered in sequence, with cross-reference on the appropriate Section 1 log sheet.
See Chapter 6 for details on messages, content and procedures.
Notes: Slide 8: The Message File Section
ANIMATIONS.
Basic slide displayed with large simulated logbook opened to messages file section. Iconic message displayed (e.g., simular in appearance to Chapter 6 message icons).
[CLICK] large logbook dissolves, replaced with smaller representation and an appropriate info balloon.
[CLICK] next slide.
* * * * * * * * * * (end comments)
<number>

## Slide 10: The Reference File Section
AUXCOM – Auxiliary Communications Specialty Course
<number>
This section has reference materials intended to the station operator(s) in a broad range of circumstances. The exact content will vary by station.
Chapter 7, lists recommended items, including:
Local CG units and locations, phone numbers, call signs etc.
Local Auxiliary facilities, flotilla rosters and reach numbers
Civilian agencies reach numbers
Area of Operations (AOR) info
Distress & SAR “scripts” & forms
CG, State and other forms
… and more.
Notes: Slide 9: The Reference File Section
ANIMATIONS.
Basic slide displayed with simulated logbook opened to reference file section, showing an assortment of data.
[CLICK] logbook image dissolves, replaced with a smaller version and an appropriate info balloon.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 11: Operator Notes
“OP NOTES” added to the log are helpful to describe log entries to remind operators later on situation or activity which required the communication
Be descriptive: “Safety Patrol,” “Comms Drill,” “Weather Alert,” etc.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 10: Operator Notes
(no author’s notes).
<number>

## Slide 12: Some Chapter Questions
AUXCOM – Auxiliary Communications Specialty Course
<number>
QUESTION | ANSWER
When operating as a government station, what is the minimum log requirement? | 
What are the three sections of a log? | 
What are some recommended items to be kept in the reference section? | 
When is an Auxiliary facility required to maintain a log? | 
What are OP NOTES? | 
A station log, in ink, in a ledger or log book.
Log, Messages and Reference
Local unit phone numbers, local agency phone numbers, AOR data, “scripts” and forms, …
When mobile and NOT under direction of a fixed land station, or when mobile-to-mobile calling.
Annotations in the log to describe the communications.
Notes: <number>
Slide 11: Some Chapter Questions
ANIMATIONS
Five questions are displayed.
[CLICK] to display each answer in sequence. Font change used to simulate human handwriting.
After last answer displayed, one more [CLICK] to next screen (allows instructor pause for last answer).
* * * * * * * * * * (end comments).

## Slide 13: End of Chapter 7
AUXCOM – Auxiliary Communications Specialty Course
<number>
Questions?
Next: Chapter 8, “Coast Guard Communications”
Notes: <number>
Slide 12: End of Chapter 7
(no author’s notes).
This is the last slide normally displayed.

## Slide 14
AUXCOM – Auxiliary Communications Specialty Course
<number>
(This slide intentionally left blank.)
Notes: <number>
Slide 13: endslide
Not normally displayed.