## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Auxiliary Communications Specialty (AUXCOM)
Chapter Two
Voluntarily Installed Marine Radiotelephone
Station Regulations
AUXCOM 2009 v0.98
Notes: US COAST GUARD AUXILIARY – Auxiliary Communications Specialty Course (“AUXCOM”)
2009 UPDATE, version 0.98
Slide 1. Chapter cover slide.
Chapter 2: “Voluntarily Installed Marine Radiotelephone Station Regulations”
(no author notes).
<number>

## Slide 3: Chapter 2 Outline
Overview
Station and Operator License
Frequency Assignments
Station Identification and Required Documents, Other Regulations
Revocation and Suspension of License
Summary of Radiotelephone Operating Practices
GMDSS, DSC, AIS, Rescue 21
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 2: Chapter 2 Outline
(no author notes).
<number>

## Slide 4: Overview
This Chapter:
  Digest of rules for voluntarily installed stations
  Voluntary = “not required”; mandatory installations not covered in this course
  Rules change constantly – evolving technology drives much of this change
  Telecommunications Act of 1996 – major changes to 47 CFR Part 80, defining FCC regulations.
AUXCOM – Auxiliary Communications Specialty Course
<number>
An “OPERATOR LICENSE”
is held by an individual and can be used at multiple stations.
A “STATION LICENSE” refers to the radio installed on a boat; cannot transfer license to another person or boat – a new owner must apply for a new license.
The student should validate the information in this presentation and course against prevailing FCC regulations.
Notes: Slide 3: Outline
ANIMATIONS
Basic slide displayed.
[CLICK] station license explanatory balloon displayed.
[CLICK] operator license explanatory balloon displayed.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 5: FCC Station License
AUXCOM – Auxiliary Communications Specialty Course
<number>
NO LICENSE REQUIRED, if:
  Voluntary Installation (typically recreational vessels)
  Operating in US waters
  VHF-FM, RADAR, AIS, EPIRBs
LICENSE REQUIRED, if:
  Non-voluntary Installation
  Operating in non-US waters
  Satellite or MF/HF SSB
  Must apply to FCC; must be citizen
  Must post license if possible; if unable to post (due to exposure to elements in an open boat, for instance), must carry at all times
  Interim Ship Station License permits operation while waiting for FCC to act on license application
  Renew between 90 and 30 days of expiration
License application form available at FCC website:
http://www.fcc.gov/formpage.html
or any FCC field office.
Notes: Slide 4: FCC Station License
(no author notes).
<number>

## Slide 6: Operator License
AUXCOM – Auxiliary Communications Specialty Course
<number>
“DOMESTIC MARITIME SERVICE”:
No operator license requirement for VOLUNTARY installed maritime radiotelephone stations – in the US
In foreign waters, “RESTRICTED RADIOTELEPHONE OPERATOR” permit recommended
Adjustments and Tests – must be performed by or under immediate supervision of a “FIRST-” or “SECOND-CLASS RADIOTELEGRAPH LICENSE”, or a “GENERAL RADIOTELEPHONE OPERATOR LICENSE”
Notes: Slide 5: Operator License
(no author notes).
<number>

## Slide 7: Distress and Calling Frequencies
2-30 MHz Band
  2182 kHZ
156-162 MHz Band
  156.800 MHz (Channel 16)
    Ship radiotelephone stations
  156.450 MHz (Channel 9)
    Alternate for recreational vessels
  156.525 MHz (Channel 70)
    DSC equipped vessels
Listening watch must be maintained when radio is on and not in use for communications on another frequency.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: <number>
Slide 6: Distress and Calling Frequencies
(no author notes).

## Slide 8: Use of Distress And Calling Frequencies
Distress calls (“Mayday”)
  Grave or imminent danger, immediate assistance required
Urgency calls (“Pan Pan”)
  Very urgent message regarding safety of a person, ship, aircraft or other vehicle
  Pronounced “PAWN PAWN”
Safety calls (“Sécurité”)
  Message regarding safety of navigation or important meteorological warnings
  Pronounced “SAY-CURE-EE-TAY”
Initial call and reply to specific station
  Brief exchange of operating signals – then agree on a working channel.
AUXCOM – Auxiliary Communications Specialty Course
<number>
PRIORITY HIGHEST
PRIORITY LOWEST
Notes: <number>
Slide 7: Use of Distress and Calling Frequencies
ANIMATIONS
Basic slide displayed.
[CLICK] message priority indicator displayed.
[CLICK] next slide.
* * * * * * * * * * (end comments).

## Slide 9: Channel 16 Time Limitations
Call – 30 Seconds Max No Reply – Wait 2 Minutes
Call – 30 Seconds Max No Reply – Wait 2 Minutes
Call – 30 Seconds Max No Reply – Wait 15 Minutes (If Channel Unused, 3 Minute Wait)
AUXCOM – Auxiliary Communications Specialty Course
<number>
START OVER
In an emergency,
time limits do not apply!
Notes: <number>
Slide 8: Channel 16 Time Limitation
ANIMATIONS
Slide with title only displayed.
[CLICK] call step 1 displayed.
[CLICK] call step 2 displayed.
[CLICK] call step 3 displayed.
[CLICK] “start over” loop displayed.
[CLICK] emergency time limits note displayed.
[CLICK] next slide.
* * * * * * * * * * (end comments).

## Slide 10: 2 – 30 MHz Ship-to-Ship Working Frequencies
AUXCOM – Auxiliary Communications Specialty Course
<number>
FREQUENCY | AREA AND USE
2003 KHz | GREAT LAKES
2082.5 KHz | ALL EXCEPT GREAT LAKES
2142 KHz | PACIFIC COAST, SOUTH OF LATITUDE 42 DEGREES NORTH, DAYLIGHT ONLY
2203 KHz | GULF OF MEXICO
2638 KHz | ALL AREAS
2738 KHz | ALL AREAS, EXCEPT: GREAT LAKES AND GULF OF MEXICO
2830 KHz | GULF OF MEXICO
IN U.S., UPPER SIDEBAND ALWAYS USED
Notes: Slide 9: 2-30 MHz Ship-to-Ship Working Frequencies
(no author notes).
<number>

## Slide 11: 156 – 162 MHz Ship-to-Ship Working Frequencies
AUXCOM – Auxiliary Communications Specialty Course
<number>
FREQUENCY | CHANNEL | USE
156.300 MHz | 06 | INTERSHIP SAFETY. MANDATORY CHANNEL.
156.800 MHz | 16 | DISTRESS, SAFETY, CALLING. MANDATORY.
156.425 MHz | 68 | INTERSHIP AND SHIP-TO-COAST. AVAILABLE FOR THE WIDE SCOPE OF NEEDS FOR NONCOMMERCIAL BOATS.
156.625 MHz | 72 | INTERSHIP. AVAILABLE ON INTERIM BASIS FOR NON-COMMERCIAL COMMUNICATIONS FOR FLEET OPERATIONS DURING A CRUISE OR RENDEZVOUS.
156.450 MHz | 09 | ALTERNATE CALLING FOR RECREATIONAL VESSELS. INTERSHIP AND SHIP-TO-COAST.
156.525 MHz | 70 | DIGITAL SELECTIVE CALLING (DSC).
Notes: Slide 10: 156-162 MHz Ship-to-Ship Working Frequencies
(no author notes).
<number>

## Slide 12: Ship-to-Ship Working Frequencies
Use:
  Primary – Safety
    Distress, Urgency, Safety
  Secondary – Operational
    Navigation, Movement, Management
  Thirdly – Non-Commercial
    On a “not to interfere basis”
Time Limits:
  3 minutes maximum, after establishing contact
  10 minutes must elapse after an exchange before same two stations use frequency again
  Safety emergencies override time limitations.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 11: Ship-to-Ship Working Frequencies
(no author notes).
<number>

## Slide 13: Station Identification
Station With Permanent License
  Use station’s assigned call sign
  Identification made:
    Beginning and end of each communication
    Beginning and end of each transmission for any other purpose
    Intervals not exceeding 15 min. when transmission sustained for period exceeding 15 min.
Station Without License
  Use name of vessel or land station.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: <number>
Slide 12: Station Identification
(no author notes).

## Slide 14: Transmitter Adjustments to Radiotelephone Equipment
Station licensee bears responsibility for proper operation of equipment
Transmitter adjustments or tests made under supervision of person holding First or Second Class Radiotelegraph or General Radiotelephone license.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 13: Transmitter Adjustments to Radiotelephone Equipment
(no author notes).
<number>

## Slide 15: Radio Ground Connection
SSB
  Effective antenna operation depends on adequate grounding
  Metal hull: ground directly
  Non-metallic hull: ground plate mounted below waterline
VHF
  Antenna systems usually don’t require grounding.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 14: Radio Ground Connection
(no author notes).
<number>

## Slide 16: Secrecy of Communications
Secrecy Requirements are defined in the Telecommunications Act and Radio Regulations – listeners cannot use or divulge information gained
Station Licensee, Vessel Master, Radio Operator or anybody who knows content of radio communications is bound by the rules
Doesn’t apply to distress calls or broadcasts for use of general public.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 15: Secrecy of Communications
(no author notes).
<number>

## Slide 17: Obscenity, Indecency, and Profanity
Prohibited
Criminal offense (U.S. Criminal Code)
  Fines up to $10,000
  Jail up to 2 years.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Remember: radio is a “party line”!
(all conversations open and overheard by others)
Notes: <number>
Slide 16: Obscenity, Indecency and Profanity
(no author notes).

## Slide 18: Revocation and Suspension of License
Violations of regulations have potential consequences
  Revocation of station license
  Revocation of operator license
  Fines against licensee and operator
  Fines against licensee
  $100 - $20,000 each separate instance and 5 years for false distress
Licensee responsible for transmissions.
AUXCOM – Auxiliary Communications Specialty Course
<number>
REFER TO THE TEXT FOR MORE DETAILS.
Notes: <number>
Slide 17: Revocation and Suspension of License
(no author notes).

## Slide 19: Operating Practices (I)
Licensee Responsibilities
  Avoid unnecessary calls
  Listen first – to see if channel in use
  Station identification – clear and distinct
  Prevent unauthorized use when transmitter easily accessible
  Do not continuously call and cause interference at other stations
  Technical repairs or adjustments by or under supervision of appropriately licensed operators
  When a licensed operator permits another person to talk on the air, they remain responsible.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: <number>
Slide 18: Operating Practices (I)
(no author notes).

## Slide 20: Operating Practices (II)
Effective voice technique
  Loud enough to be distinct, not loud enough to distort
  Articulate clearly, avoid monotone
  Microphone usually 2-6 inches from lips
Prowords and abbreviations
  As appropriate for accuracy and clarity
Phonetic alphabet
  Standard phonetic alphabet (Alpha, Bravo, Charlie, …) increases understanding when used properly.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 19: Operating Practices (II)
(no author notes).
<number>

## Slide 21: Operating Practices (III)
Testing
  Announce the test to avoid confusion
  Be as brief as possible, do not interfere with communication on the same channel
  Use station call sign or vessel name
  Regular testing recommended – especially when radio used only occasionally for calling
  No radio checks with Coast Guard on VFH Channel 16
    licensed FCC technicians and inspectors are authorized to conduct radio checks with the Coast Guard during repairs or inspections.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 20: Operating Practices (III)
(no author notes).
<number>

## Slide 22: GMDSS (I)
Global Maritime Distress and Safety System
  Designed for efficient/effective emergency and safety communications to all ships
    Navigational, meteorological and other urgent safety messages
    incorporate the resources of numerous MF, HF, VHF and satellite communications systems operating in a Digital Selective Calling (DSC) mode
  Digital Selective Calling (DSC)
    when used also with GPS, allows automatic transmission and reception of distress calls with vessel ID and position
    FCC requires new (after 1999) marine radios to include DSC capabilities (does not apply to hand-held units)
    DSC (VHF) – Channel 70; HF also has DSC (on several frequencies, such as 2187.5 kHz).
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 21: GMDSS (I)
(no author notes).
<number>

## Slide 23: GMDSS (II)
  GMDSS DSC
    On VHF – Channel 70: voice use of Channel 70 forbidden
    Radio watch on Channel 16 by cargo or passenger ships voyaging internationally no longer required
    DSC – like the dial and bell of a telephone: allows "direct dial" and "ring" to other radios, or allow others to "ring" you
  MMSI (“Marine Mobile Service Identity”)
    The DSC “phone number” – must be encoded into the radio after purchase – can call individual vessels in this way as well
    Obtained from BoatUS or Sea Tow
  Automatic Position Information
    Many radios now equipped for NEMA 0183 interface to GPS … allows position data to be automatically embedded in DSC messages.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 22: GMDSS (II)
(no author notes).
<number>

## Slide 24: GMDSS (III)
Minimum DSC Capabilities: Class D (VHF) or Class E (HF)
  Includes
    Distress call, All-ships call, Individual station call
    Use of distress, urgency, safety and routine priorities
    Nature of distress
    Time for last (distress) position update
    Type of subsequent communications
    Radio VHF channel or HF frequency
    Display
    Receive distress relay and distress calls.
  Tutorial
    http://www.boatus.com/mmsi
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 23: GMDSS (III)
(no author notes).
<number>

## Slide 25: AIS (I)
Universal Shipboard Automated Information System (AIS)
  Supplements DSC, uses same MMSI as DSC
  Info overlaid onto chartplotter, provides identity, position, heading, speed and additional data
  Transponder operates in VHF maritime band, capable of handling thousands of reports per minute and updates as often as every two seconds
  Presently used with larger commercial shipping, transponders may soon be affordable for recreational vessels
  Can use for effective, direct communication, rather than imprecise “Hailing vessel off my port bow …”
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 24: AIS (I)
(no author notes).
<number>

## Slide 26: AIS (II)
AUXCOM – Auxiliary Communications Specialty Course
<number>
PORTION OF AN INTERNET-BASED AIS DISPLAY OF NEW YORK HARBOR, 25 SEPTEMBER 2009 (from marinetraffic.com).
Notes: Slide 25: AIS (II)
(no author notes).
<number>

## Slide 27: Coast Guard National Distress System and Rescue 21
CG Began modernizing CGNDS in 2003
Rescue 21
  Begun as modernization of CGNDS
  Ensures compatibility with GMDSS
  Improved coverage in coastal regions and Western Rivers
  Implementation rolling by region through 2012, Alaska later.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Rescue 21 is covered in more detail in Chapter 10.
Notes: Slide 26: Coast Guard National Distress System and Rescue 21
(no author notes).
<number>

## Slide 28: Some Review Questions
AUXCOM – Auxiliary Communications Specialty Course
<number>
QUESTION | ANSWER
An efficient listening watch is required on which VHF channel and under what conditions? | 
When a station does not respond to a call sent three times at intervals of two minutes, you are permitted to call again after how many minutes have passed? | 
What is the basic procedure to initiate a call on a ship's radiotelephone? | 
After two ship stations have established contact on an intership working frequency, FCC regulations limit the maximum duration of the communication to what period of time? | 
What is the VHF distress and calling frequency for the GMDSS? | 
Channel 16 … always, when radio on and not being used to communicate.
Fifteen (15) minutes.
Listen, Hail & Make Contact, Agree Working Channel, Switch Channel.
Three (3) minutes.
Channel 70 … 156.625 MHz.
Notes: Slide 27: Some Chapter Questions (1 of 2)
ANIMATIONS
Five questions are displayed.
[CLICK] to display each answer in sequence. Font change used to simulate human handwriting.
After last answer displayed, one more [CLICK] to next screen (allows instructor pause for last answer).
* * * * * * * * * * (end comments).
<number>

## Slide 29: More Review Questions
AUXCOM – Auxiliary Communications Specialty Course
<number>
QUESTION | ANSWER
All transmitter adjustments to marine radiotelephone transmitters must be performed by or under the immediate supervision of a person holding which class of license? | 
The secrecy provision of the communications regulations does not apply to what type of communications? | 
What are some of the violations which can cause license revocation or fines against the licensee or operator? | 
What are desirable voice characteristics when speaking on a radio? | 
Which SSB working frequency can be used in all areas? | 
First or Second Class Radiotelegraph or a General Radiotelephone Operator License.
Communications relating to ships in distress or broadcasts intended for use by the general public.
False distress calls; use of obscene, indecent, or profane language; repeated violation of FCC regulations.
Clear, distinct, loud enough but not too loud, no monotone.
2638.0 KHz.
Notes: Slide 28: More Chapter Questions (2 of 2)
ANIMATIONS
Five questions are displayed.
[CLICK] to display each answer in sequence.
Following display of final answer, [CLICK] to advance slide.
* * * * * * * * * * (end comments).
<number>

## Slide 30: End of Chapter 2
Questions?
Next: Chapter 3, “Calling and Answering Procedures”
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 29: End of Chapter 2
(no author notes).
INSTRUCTOR NOTE: THIS IS THE LAST NORMALLY-DISPLAYED SLIDE OF THIS DECK.
<number>

## Slide 31
AUXCOM – Auxiliary Communications Specialty Course
<number>
(This slide intentionally left blank.)
Notes: Slide 30: endslide
(no author notes).
<number>