## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Auxiliary Communications Specialty (AUXCOM)
Chapter 5
Auxiliary Communications System
<number>
AUXCOM 2009 v0.98
Notes: <number>
US COAST GUARD AUXILIARY – Auxiliary Communications Specialty Course (“AUXCOM”)
2009 UPDATE, version 0.98
Slide 1. Chapter cover slide.
Chapter 5: “Auxiliary Communications System”
(no author notes).

## Slide 3: Chapter 5 Outline
AUXCOM – Auxiliary Communications Specialty Course
Auxiliary Communications System
Radio Facilities
Radio Call Signs
Administration
Citizens Band (CB) Radio
Radio Logs
Authorized/Required Frequencies
Inspection
Auxiliary Communications Watchstanders
Responding to Mariners’ Requests for Information
Communication With Civilian Emergency Services
Review Questions
<number>
Relative to some other chapters, much more information is in the text than this accompanying presentation.
Notes: Slide 2: Chapter 5 Outline
(no author’s notes).
Note: due to the nature of the material in this chapter, more information is to be found in the text than in this presentation. Especially procedural and forms-related data.
<number>

## Slide 4: Auxiliary Communications System
Consists of designated “radio facilities,” plus vessels and aircraft with radios
Radio facilities are offered by their owner for use by the Auxiliary, and inspected / accepted by the Director – after which they are operational
Radio facilities may be:
  fixed land stations
  land mobile stations
  radio detection finding (“RDF”) stations
A given radio may not be used for more than one facility
Transmitters must be FCC accepted/type approved (see section B.5 in text).
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 3: Auxiliary Communications System
(no author’s notes).
<number>

## Slide 5: Auxiliary Communications System
Purpose
  Coordinate authorized Auxiliary activities in support of Coast Guard operations
  Augment Coast Guard communications system when required
  Communicate urgent matters of official Auxiliary business
  Training
  Assist national resources in time of disaster
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 4: Auxiliary Communications System, continued
(no author’s notes).
<number>

## Slide 6: Auxiliary Communications System
Control
  District Commander controls – including training and drill activities. DC authorizes frequencies (listed in test)
  Each Auxiliary district must conduct communications drills, at least quarterly
  District commanders may also authorize use of the Federal Telecommunications System and local Coast Guard landlines.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 5: Auxiliary Communications System, continued.
(no author’s notes).
<number>

## Slide 7: Radio Facilities
Fixed Land Radio Facility
  Operated from a fixed location (home, garage, office, etc.). May also have RDF capability
  “Transportable Station” – fixed land radio facility transported to various location but not used while in motion.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 6: Radio Facilities
(no author’s notes).
<number>

## Slide 8: Radio Facilities
Land Mobile Radio
  Operated while in motion – in a vehicle, walking, etc.
  Can include portable radios (“walkie-talkies,” “H/T’s,” etc.), as well as marine radios
  Portable Radio: can be hand-carried and have a self-contained antenna and power source. The Director may certify a portable radio for a facility under certain conditions, where one is appropriate to the facility’s mission; additional power, antenna or other capabilities may be required by the Director to augment the unit.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 7: Radio Facilities, continued
(no author’s notes).
<number>

## Slide 9: Radio Facilities
VHF RDF
  Passive direction-finding capability
  Land-line or other non-marine communications must be available
  Units must meet standards of accuracy, range and scope of direction
Auxiliary Vessels and Aircraft
  “Facilities with radios,” not “radio facilities.”
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 8: Radio Facilities, continued
(no author’s notes).
<number>

## Slide 10: Radio Facilities
Government Station
  A station, when assigned Coast Guard duty, is a Coast Guard radio station and a legal “government station”
  To operate as a government station, the radio must be on board a surface or aircraft facility, or be accepted for use as a radio facility by the Director
  Auxiliarists may operate the facility if they meet the owner/operator requirements, or are under direct supervision of the owner/operator – compliance is responsibility of the facility owner
  When under orders, operators of radio-equipped facilities may (and must) operate on government frequencies; all surface and air facilities must be VHF-FM equipped. Only frequencies authorized by the District Commander may be used as local working frequencies.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 9: Radio Facilities, continued
(no author’s notes).
<number>

## Slide 11: Radio Facilities
FCC License
  Auxiliary surface or aircraft facility when operating under orders or performing a mission directed or scheduled by the Coast Guard does not need an FCC license
  Most Auxiliarists also use their equipment for recreational uses, and must have an FCC license if required – the Director can waiver if the facility is used only for government purposes
  Auxiliarists do not directly contact the FCC on Auxiliary matters
  More details in text, Chapter 5, Section B.3.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 10: Radio Facilities, continued
(no author’s notes).
<number>

## Slide 12: Radio Facilities
Owner/Operators must have the following training:
  Owners or operators of fixed land, land mobile or RDF facilities – AUXCOM and other training as required by the District Commander
  Operators on boats, aircraft or special-purpose facilities must have appropriate crew qualifications or AUXCOM, and other training as required by the District Commander
  Auxiliarists standing communications watches at Coast Guard units are “BQ” and meet the watchstander qualification of that unit.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 11: Radio Facilities, continued
(no author’s notes).
<number>

## Slide 13: Radio Facilities
VHF-FM RDF Facility Requirements
  Minimum range 10 miles; arc of unobstructed direction finding 130 degrees, no reflected signals noted; demonstrated bearing error +/- 5 degrees
  Located close to assigned patrol areas; must provide accurate DF support to operational facilities in patrol area
  Landline or non-marine communications capability – operator is NOT to pass LOPs and fixes on VFH-FM unless requested
  See text regarding certain other requirements, Section B.1.e.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 12: Radio Facilities, continued
(no author’s notes).
<number>

## Slide 14: Radio Call Signs
Authorization
  Auxiliary radio facilities must use Auxiliary radio call signs when:
    Conducting SAR, emergency or patrol communications
    Conducting official Coast Guard or Auxiliary business on Coast Guard frequencies
  Do not use an FCC call sign along with an Auxiliary call sign
  Written orders are not required to use Auxiliary call signs
Designations
  Vary by situation. Refer to text (Section C.2).
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 13: Radio Call Signs
(no author’s notes).
<number>

## Slide 15: Administration
Coast Guard Director:
  Coordinates general supervision of Auxiliary communications
  Approves potential station owners for membership
  Accepts/rejects facility inspections
  Approves drill schedules
  Encourages maximum level of effectiveness
  Maintains current list of available facilities
  Maintains the approved call sign numbering system
  Coordinates with CG District telecommunications branch on use or distribution of CG-supplied equipment to Auxiliarists.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 14: Administration
(no author’s notes).
<number>

## Slide 16: Administration
Decal Display
  Miniature decal and wreath can be displayed on exterior or interior of building in which the equipment is housed
  Decal may also be placed in any legal position on a vehicle or the radio itself
  Large-size decal & wreath not used.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 15: Administration, continued
(no author’s notes).
<number>

## Slide 17: Citizen’s Band (CB) Radio
Coast Guard has no requirements to monitor or support CB radio
  Auxiliary facilities may use CB equipment to communicate with boats when no other method available – CG prefers Auxiliary using marine frequencies only
  Auxiliarists using CB will use Auxiliary call signs and proper radiotelephone procedures; no “10” code (e.g., “10-4”), no CB slang (e.g., “good buddy”)
  CB equipment does not satisfy requirements for radio facility status.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 16: CB Radio
(no author’s notes).
<number>

## Slide 18: Radio Logs
Operators of all boat, aircraft and radio facilities must maintain radio logs and formal message logs
Some exceptions exist when operating for a CG or Auxiliary shore unit (see text)
A fixed shore-side radio facility is better able to maintain logs than a boat or aircraft; facilities not under direct control of a CG station or Auxiliary fixed land facility must make log entries
Logs to be available to cognizant authority when asked
Logs must be maintained for 1 year; 3 years when distress traffic recorded; longer if an investigation or claim is open
Keeping a log must not interfere with safe operation of the facility – see text on details re: deferred entries (G.5).
AUXCOM – Auxiliary Communications Specialty Course
<number>
CHAPTER 7 HAS A FULL DESCRIPTION OF RADIO LOGS.
Notes: Slide 17: Radio Logs
(no author’s notes).
<number>

## Slide 19: Authorized / Required Frequencies
AUXCOM – Auxiliary Communications Specialty Course
<number>
PURPOSE | AUTHORIZED FREQUENCY (ALL VHF-FM) | REQUIRED LAND | REQUIRED AIR / SURFACE
CG WORKING | Channel 21A | X | X
 | Channel 23A | X | X
 | Channel 81A | X | X
 | Channel 83A | X | X
CG LIAISON/WORKING | Channel 22A | X | X
DISTRESS, SAFETY, CALLING | Channel 16 | X | X
ALTERNATE CALLING | Channel 09 |  | 
INTERSHIP SAFETY / SAR SHIP TO AIRCRAFT | Channel 06 | X | X
SEE TEXT, CHAPTER 5, SECTION “I” FOR MORE COMPLETE LISTING, INCLUDING NON MARINE VHF-FM FREQUENCIES.
Notes: Slide 18: Authorized/Required Frequencies
(no author’s notes).
<number>

## Slide 20: Inspection
Each facility is initially inspected, then re-inspected every 3 years
Only AUXOP or communications officer (any level) having completed AUXCOM may conduct inspection; may not inspect own equipment or that of immediate family
Radio equipment permanently installed on boats or aircraft is boat/aircraft equipment
Owner of inspected equipment solely responsible for maintenance
Land mobile owners may carry a copy of their Radio Facility Inspection Report (Form 2736A) in their vehicle, along with Auxiliary ID card and facility decal to satisfy potential enforcement agency inquiries on vehicle-carried equipment.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 19: Inspection
(no author’s notes).
<number>

## Slide 21: Auxiliary Communications Watchstanders
Auxiliary Communicators – an integral part of CG network
Auxiliary Communicator IS the CG to the public, and must work to maintain public trust
Qualifications:
  At CG Units – must meet unit training and qualifications
  At Auxiliary Facilities – AUXCOM and other requirements per the Director
  Local Knowledge – must be thoroughly familiar with local operating area in addition to training and qualifications
Group and Station Communications Watchstanders Qualification Guide, COMDTINST M16120.7
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 20: Auxiliary Communications Watchstanders
(no author’s notes).
<number>

## Slide 22: Auxiliary Communications Watchstanders
The public will likely exhibit a wide range of emotions, including confusion, panic, impaired thinking (intoxication, hypothermia, fatigue, etc.), ignorance and more – remain cool and professional to complete necessary communications and provide effective help
Important Communicator skills include:
  Speaking clearly, evenly, not too fast, not too loud
  Clear thinking before speaking
  Relate to level of caller: child, novice, professional, etc.
  Full attention – active listening, note taking
  Calm, Confident, Objective, Professional
  Accept your limits & distance between yourself and the crisis
  More, see Chapter 5, Section M.2.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 21: Auxiliary Communications Watchstanders, continued
(no author’s notes).
<number>

## Slide 23: Responding to Requests for Information
Information requests from the public to Auxiliary Communicators are guided by Auxiliary policy or local CG policies for watchstanders at CG units. Expanded details in the text, Chapter 5, Section N
  Navigational Information – Auxiliarists may pass any information contained in recognized published documents, but may not give or recommend compass courses
  Lost or Disoriented – see text
  Weather – Auxiliarists may pass weather information, but be clear the CG does not forecast weather
  Third party Radio Traffic – CG does not usually handle 3rd party traffic – see text for situational details
  Accuracy & Timeliness – see text.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 22: Responding to Requests for Information
(no author’s notes).
<number>

## Slide 24: Communication With Civilian Emergency Services
CG resources interact with civilian emergency services in many SAR and disaster situations – all resources need to communicate and coordinate
Preferable for civilian station to shift to government frequency for the duration, such as VHF-FM Channels 21A, 23A or 83A (note Channel 22A would raise interference problems if another SAR situation arises locally)
Channel 81A is used for environmental problems
Using government frequencies, Auxiliary is precluded from involvement in law enforcement, CAP, DOD or other services with differing operating procedures – most units working maritime SAR have marine VHF-FM capabilities
Use of government channels by non-government stations in these cases is allowed by FCC rules.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 23: Communication With Civilian Emergency Services
(no author’s notes).
<number>

## Slide 25: Some Chapter Questions
AUXCOM – Auxiliary Communications Specialty Course
QUESTION | ANSWER
Can an individual radio used on a vessel facility be accounted for in any other facility? | 
What are the various types of Auxiliary Radio Facilities? | 
Can a portable radio qualify as a facility? | 
Vessel facility radios are considered government stations under what circumstances? | 
Can land mobile radio facilities engage in personal business on their facility radio frequencies? | 
No
Fixed Land, Land Mobile, RDF
Yes – sometimes.
When operating under orders; when performing CG duty
No – not on CG frequencies
<number>
Notes: <number>
Slide 24: Some Chapter Questions (1 of 2)
ANIMATIONS
Five questions are displayed.
[CLICK] to display each answer in sequence. Font change used to simulate human handwriting.
After last answer displayed, one more [CLICK] to next screen (allows instructor pause for last answer).
* * * * * * * * * * (end comments).

## Slide 26: More Chapter Questions
AUXCOM – Auxiliary Communications Specialty Course
QUESTION | ANSWER
Under what conditions may fixed land, land mobile or RDF facilities be activated? | 
What training is required for an Auxiliarist to be able to use a vessel facility radio? | 
What are the conditions under which CB radio may be utilized? | 
Vessel and aircraft facilities must be capable of operating on which VHF-FM marine channels? | 
Communication with civil emergency services is preferred on what VHF-FM marine channels? | 
Mission, Distress, Technical Testing, need to contact CG to see if Aux help needed (B.1.h).
Boat Crew qualified or AUXCOM plus other training required by District Commander
No other method available.
CG protocols used; no “10 codes,” no CB slang.
Channels 6, 16, 21A, 22A, 23A, 81A, 83A.
Channels 21A, 23A, 83A. 81A for environmental events.
<number>
Notes: <number>
Slide 25: More Chapter Questions (2 of 2)
ANIMATIONS
Five questions are displayed.
[CLICK] to display each answer in sequence. Font change used to simulate human handwriting.
After last answer displayed, one more [CLICK] to next screen (allows instructor pause for last answer).
* * * * * * * * * * (end comments).

## Slide 27: End of Chapter 5
AUXCOM – Auxiliary Communications Specialty Course
Questions?
Next: Chapter 6, “Messages”
<number>
Notes: <number>
Slide 26: End of Chapter 5
(no author’s notes).
Intended as the last normally-displayed slide of this deck.

## Slide 28
AUXCOM – Auxiliary Communications Specialty Course
(This slide intentionally left blank.)
<number>
Notes: <number>
Slide 27: endslide
Not normally intended to be displayed.