## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Auxiliary Communications Specialty (AUXCOM)
<number>
Chapter 3
Calling and Answering Procedures
AUXCOM 2009 v0.98
Notes: <number>
US COAST GUARD AUXILIARY – Auxiliary Communications Specialty Course (“AUXCOM”)
2009 UPDATE, version 0.98
Slide 1. Chapter cover slide.
Chapter 3: “Calling and Answering Procedures”
(no author notes).

## Slide 3: Chapter 3 Outline
AUXCOM – Auxiliary Communications Specialty Course
<number>
Calling Procedures
  General
  Ship-to-Ship Calls
  Ship-to-Shore Calls
Answering Procedures
Test Transmissions
Radio Checks
Review Questions
Notes: Slide 2: Chapter 3 Outline
(no author’s notes).
<number>

## Slide 4: General
First, Listen Carefully – ensure frequency is clear
Second, Establish Contact – use Distress and Calling Frequency (VHF Channel 16 or 2182 KHz)
  Alternate Channel (VHF) – Channel 9
Third, Agree on a Working Channel, then shift to it
Sometimes, a call might be initiated on a working frequency if known that the called station “guards” it (maintains a listening watch on it) – as an example, commercial riverboat traffic often uses VHF Channel 13 (e.g., the “bridge-to-bridge” channel).
AUXCOM – Auxiliary Communications Specialty Course
<number>
The Coast Guard Navigation Center,
http://www.navcen.uscg.gov/marcomms/boater.htm
has samples of calls, outlines of radio procedures and rules.
Notes: Slide 3: General
(no author’s notes).
<number>

## Slide 5: Ship-to-Ship Calls
(1): listen for clear frequency
(2): call the desired station
  Note: since FCC deregulation, most recreational vessels do not have FCC call signs. Use the vessel name.
(3): the called and calling station names or call signs are repeated up to 3 times each. Entire calling transmission is less than 30 seconds
(4): if contact is NOT established, repeat call twice after waiting 2 minutes each time. If still fail to connect, wait 15 minutes before repeating cycle
(5): at the end of the call, do not say “Returning to Channel 16” (or 2182 KHz) – this is understood
(6) Allow 10 minutes to elapse before the same two stations communicate again (unless emergency).
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 4: Ship-to-Ship Calls
(no author’s notes).
<number>

## Slide 6: Ship-to-Ship Calls: Initiating
NOTE: IN AUXILIARY COMMUNICATIONS, AUXILIARY FACILITY IDENTIFICATIONS ARE USED. VESSEL NAMES USED HERE FOR SIMPLICITY.
AUXCOM – Auxiliary Communications Specialty Course
<number>
“Minnow, Minnow, this is Bay Breeze over.”
“Bay Breeze, this is Minnow over.”
“Minnow, shift to Channel 68 over.”
“This is Minnow. Wilco out.”
Notes: Slide 5: Ship-to-Ship Calls: Initiating
ANIMATIONS
Base slide displayed.
[CLICK] Simulated dialog begins – call initiated.
[CLICK] Response from called vessel.
[CLICK] Directive to switch to working channel from calling vessel.
[CLICK] Acknowledgement from called vessel.
[CLICK] next slide.
Note that in Auxiliary communications, the Auxiliary facility identification is used if the station is a facility.
In this simulated dialog, vessel names are used for simplicity.
* * * * * * * * * * (end comments).
<number>

## Slide 7: Ship-to-Ship Calls: After Shifting to Working Frequency
AUXCOM – Auxiliary Communications Specialty Course
<number>
“Minnow, this is Bay Breeze over.”
“Bay Breeze, this is Minnow over.”
“This is Bay Breeze, [THE MESSAGE], over.”
“This is Minnow, [RESPONSE TO THE MESSAGE], over.”
“This is Bay Breeze, out.”
“This is Minnow, out.”
Notes: Slide 6: Ship-to-Ship Calls – After Shifting to Working Frequency
ANIMATIONS.
Base slide displayed.
[CLICK] simulated dialog from previous slide resumes with calling station calling on working frequency.
[CLICK] called station responds.
[CLICK] calling station relays the “message” (no details of message provided here).
[CLICK] called station responds to the “message” (no details provided).
[CLICK] calling station terminates message (“out”).
[CLICK] called station terminates message (“out”).
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 8: Ship-to-Shore Calls
Cell phones have made VHF “public correspondence” calls (telephone calls) generally obsolete (few services remain) inland and near-shore; still used on HF
Billing procedures vary; most users have prearranged accounts for billing security – remember, these are public airways and all listeners can hear credit card or charge account details
Vessel hails marine operator on selected (empty) channel; operator facilitates connection
Hailing a marina or other shore facility on VHF is not a “ship-to-shore” call in the sense intended here.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 7: Ship-to-Shore Calls
(no author’s notes).
Note: the continued use and existence of public correspondence operators varies by time and locale. This once-widespread VHF service has been eclipsed by cell phone coverage in most areas, sat phone coverage in more remote areas. Marine VHF operators may be active in the Gulf of Mexico and/or Pacific/Alaska areas. SSB marine operator coverage remains available. As of 12/2009, internet searching on “ShipCom LLC” produces positive results.
<number>

## Slide 9: Ship-to-Shore Calls
AUXCOM – Auxiliary Communications Specialty Course
<number>
“Clearwater Marine Operator, this is Island Time, over.”
Marine Operator radio protocols vary somewhat by provider and will not be repeated here.
“This is Island Time. I wish to place a call to Tampa, Florida, area code 727 number 555-1212, over.”
Marine Operator confirms the details and initiates the call. Remember: the call is carried on the open airways.
“This is Island Time, out.”
Notes: Slide 8: Ship-to-Shore Calls
ANIMATIONS.
Basic slide displayed.
[CLICK] simulated dialog commences with call to marine operator.
[CLICK] note on marine operator procedures.
[CLICK] more simulated dialog.
[CLICK] more marine operator notes.
[CLICK] end of simulated dialog.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 10: Answering Procedures
Receiver “on,” tuned to correct frequency (VHF Channel 9 or 16, HF 2182 KHz)
Second receiver to watch other frequencies, or “dual watch” feature (hardware scanning to monitor more than one frequency)
Answer as illustrated above in “calling procedures.”
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 9: Answering Procedures
(no author’s notes).
<number>

## Slide 11: Test Transmissions
Take every precaution to avoid interference:
  Reduce power output
  Ensure frequency clear first
  Obtain permission first; broadcast an announcement, “This is (call sign) Test.” – a reply of “Wait” is an objection to the test and is to be honored
  Test duration, not including test identification, 10 seconds or less
  Do not repeat on VHF Channel 16 or 2182 kHz for at least 5 minutes; on other frequencies, do not repeat for at least 1 minute.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 10: Test Transmissions
(no author’s notes).
<number>

## Slide 12: Test Transmissions
AUXCOM – Auxiliary Communications Specialty Course
<number>
“This is Seafarer. Test.”
(No objection received): Proceed
“This is Seafarer. Testing. One. Two. Three. Four. Five. Six. Seven. Eight. Nine. Ten. Seafarer, Point Judith Light. Out.”
The test transmission is patterned like:
“This is (vessel) Testing … (count or sequence up to 10 seconds) … (vessel) … (general location) … Out.”
Notes: Slide 11: Test Transmissions
ANIMATIONS.
Basic slide displayed with notes on dialog template for test transmissions.
[CLICK] sample test transmission dialog commences.
[CLICK] note on “no objections, proceed.”
[CLICK] test transmission sample dialog continues.
[CLICK] next slide.
* * * * * * * * * * ( end comments).
<number>

## Slide 13: Test Transmissions
Test transmissions, aside from identification elements, should consist of number sequences or other non-confusing content (“Alpha, Bravo, Charlie, …”) – less than 10 seconds in duration
Do not use figures (“I hear you 5 by 5”) in response
Use the descriptive word “hear” rather than “read” (which implies a meter check reading on the signal).
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 12: Test Transmissions, continued
(no author’s notes).
<number>

## Slide 14: Radio Checks
Requests for Radio Checks to the Coast Guard burden the safety and distress frequencies
  FCC rules and regulations make calls to the Coast Guard on VHF Channel 16 or 2182 KHz illegal, unless:
    An FCC representative is making the tests
    Qualified radio technicians are installing or servicing station radio equipment
    In such cases, the test is identified as “FCC” or “TECHNICAL” – and logged accordingly.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 13: Radio Checks
(no author’s notes).
<number>

## Slide 15: Radio Checks
AUXCOM – Auxiliary Communications Specialty Course
<number>
Requests for Radio Checks are not broadcast to all listeners, but made to a specific station.
Establish contact using the regular calling procedures described previously.
Do not answer radio check calls not directed to your station.
“Bay Breeze, Bay Breeze. This is Seafarer. Over.”
“Seafarer, this is Bay Breeze. Over.”
“Bay Breeze switch to 68. Seafarer Out.”
“Bay Breeze this is Seafarer. Over.”
“Seafarer, this is Bay Breeze. Over.”
“Bay Breeze, how do you hear me? Over.”
“Seafarer, I hear you …
Loud and Clear
(-- or -- )
Weak but Clear
(-- or --)
Loud but Distorted
(-- or --)
Other Strength and Quality
… Over.”
“This is Bay Breeze. Wilco. Out.”
Notes: Slide 14: Radio Checks
ANIMATIONS.
Basic slide displayed with notes on radio check dialog template.
[CLICK] simulated dialog begins with call to initiate radio check.
[CLICK] simulated dialog continues, acknowledgement of radio check request.
[CLICK] simulated dialog continues, directive to switch to working frequency.
[CLICK] simulated dialog continues, acknowledgement of working frequency switch.
[CLICK] simulated dialog continues, calling station re-establishes contact on working frequency.
[CLICK] simulated dialog continues, called station acknowledges.
[CLICK] simulated dialog continues, actual radio check request by calling station.
[CLICK] simulated dialog continues, suggested responses by called station.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 16: Some Chapter Questions
AUXCOM – Auxiliary Communications Specialty Course
<number>
QUESTION | ANSWER
What should you do before calling a station? | 
In the 2-30 MHz band, are the calling procedures same as the VHF band? | 
When calling another station, what are the time limits on the initial call and any additional calls? | 
Who may conduct radio checks with the Coast Guard? | 
Who may answer requests for a radio check? | 
Listen to ensure the frequency is clear.
Yes.
Initial call, up to 30 seconds.
Can repeat twice, 2 minutes between attempts.
When call complete, 10 minutes to elapse before next call.
FCC technicians or authorized radio specialists only.
Only whomever was directly called.
Notes: <number>
Slide 15: Some Chapter Questions
ANIMATIONS
Five questions are displayed.
[CLICK] to display each answer in sequence. Font change used to simulate human handwriting.
After last answer displayed, one more [CLICK] to next screen (allows instructor pause for last answer).
* * * * * * * * * * (end comments).

## Slide 17: End of Chapter 3
AUXCOM – Auxiliary Communications Specialty Course
<number>
Questions?
Next: Chapter 4, “Distress, Urgency and Safety Messages”
Notes: <number>
Slide 16: End of Chapter 3
(no author’s notes).
Last normally-displayed slide of this deck.

## Slide 18
AUXCOM – Auxiliary Communications Specialty Course
<number>
(This slide intentionally left blank.)
Notes: <number>
Instructor NOTE: behind this slide will be branched-to detail slides from main body of show.