## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Auxiliary Communications Specialty (AUXCOM)
<number>
Chapter 9
Radio Direction Finding
AUXCOM 2009 v0.98
Notes: <number>
US COAST GUARD AUXILIARY – Auxiliary Communications Specialty Course (“AUXCOM”)
2009 UPDATE, version 0.98
Slide 1. Chapter cover slide.
Chapter 9: “Radio Direction Finding”
(no author notes).

## Slide 3: Chapter 9 Outline
AUXCOM – Auxiliary Communications Specialty Course
<number>
General Introduction
Applications
Precautions
Theory of Operation
Equipment
Operator Training
Review Questions
Notes: Slide 2: Chapter 9 Outline
(no author’s notes).
(Presumably, that’s a waterproof VHF radio, not an EPIRB [note antenna style] the swimmer is holding).
<number>

## Slide 4: Introduction
Members interested in establishing a RDF capability must :
  complete this course
  have a working knowledge of piloting, navigation fundamentals, and related subjects
Members owning radio facilities will have a practical appreciation of VHF RDF operations and may have some of the equipment required
Members who are also Amateur Radio operators or Military Auxiliary Radio Service (MARS) members can usually provide technical guidance
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 3: Introduction
(no author’s notes).
<number>

## Slide 5: Introduction, continued
Members might express interest in establishing a RDF capability without appreciating technical and legal constraints imposed on its operation
Two basic types of RDF units: manual and automatic
  Both can be operated as fixed or mobile, including hand carried
  Some (expensive) "off-the-shelf " equipment available for automatic direction finding
  Manual requires a modest technical ability to assemble and operate
  Casually-interested members might better limit efforts to a portable homing capability
AUXCOM – Auxiliary Communications Specialty Course
<number>
This discussion is not meant to discourage committed Auxiliarists; those interested need to be aware of, and willing to expend, the necessary funds, effort, and time to provide a RDF capability.
Notes: Slide 4: Introduction, continued
ANIMATIONS.
Base slide displayed.
[CLICK] info balloon displayed.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 6: Applications of RDF
Location of distressed vessels
Location of distress beacons
Vectoring of SAR Units
Hoax investigation
Locating interfering signals
AUXCOM – Auxiliary Communications Specialty Course
<number>
Distressed vessels operating VHF-FM radios can be located with RDF gear. RDF extremely useful when the vessel does not have an accurate position knowledge.
Many vessels now carry (EPIRBs), activated in distress and transmitting a signal on 406 MHz (see Chapter X). Aircraft carry a similar unit called an Emergency Locator Transmitter (ELT). Commercially available scanners can usually receive theses non-marine band signals.
If a SAR unit does not have an operational RDF or radar capability, several RDF stations coordinating bearings to obtain a fix can direct the SAR resources to merge with a distressed vessel.
The Coast Guard gets about 700 hoax MAYDAY calls each year, costing about $6 million. RDF is one way to locate illegal transmissions. Auxiliarists can assist the Coast Guard in these efforts but must not be involved in any actual law enforcement operations.
Open mikes, especially on a distress frequency, can render a channel useless in a local area. RDF units are required to locate these (usually unintentional) transmissions. In these cases the Auxiliarist should use discretion, and take no action of questionable liability.
Notes: Slide 5: Applications of RDF
ANIMATIONS.
Base slide displayed. Location of distressed vessels.
[CLICK] Location of distress beacons.
[CLICK] Vectoring of SAR units.
[CLICK] Hoax investigation.
[CLICK] Locating interfering signals.
[CLICK] Next slide.
For each click, photo and explanatory text changes, prev. bullet fades.
* * * * * * * * * * (end comments).
<number>

## Slide 7: Precautions
When engaged in RDF operations, the mission is in support of a Coast Guard operation
Bearing information is only given to Coast Guard approved recipients and no one else
Bearing information should not be exchanged on marine channels (they are open and easily monitored by the public)
Landline communication is the most secure means available to Auxiliarists
AUXCOM – Auxiliary Communications Specialty Course
<number>
When using mobile or portable RDF, an Auxiliarist is not allowed to enter or pass through an private property without the express permission of the owner
An Auxiliarist has no law enforcement authority
Discretion must be used when engaging with the public during RDF – i.e., a boater must be informed that their radio has an "open mike", but cannot be ordered to correct the problem.
An Auxiliarist learning of a situation where RDF assistance may be required should always contact the Coast Guard authority coordinating the mission – usually the SAR Mission Coordinator (SMC) – prior to taking any action.
Notes: Slide 6: Precautions
ANIMATIONS
Base slide displayed.
[CLICK] additional explanatory text displayed.
[CLICK] additional explanatory test displayed.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 8: RDF Theory of Operation (Wavefronts)
AUXCOM – Auxiliary Communications Specialty Course
<number>
Radio waves spread outward from the transmitter like the ripples produced when a stone is thrown into a pond.
As the distance from the antenna increases, the wave fronts become nearly straight.
Notes: Slide 7: RDF Theory of Operation (Wavefronts)
ANIMATIONS
Base slide displayed (radiating antenna diagram and explanatory balloon).
[CLICK] picture of wavefront straightening, arrow progressing, next explanatory balloon.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 9: RDF Theory of Operation (Detecting Wavefronts)
The receiving antenna systems can determine the orientation of the wave fronts
If a line is drawn perpendicular to these waves, it will point at the transmitting antenna.
This line is known as a single Line of Position (LOP) and is a radio bearing
The operator knows the transmitter is located along this line but not where.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 8: RDF Theory of Operation (Detecting Wavefronts)
(no author’s notes).
<number>

## Slide 10: RDF Theory of Operation (LOPs and Fixes)
An LOP is a radio bearing
A mobile RDF station might take multiple bearings from multiple locations and thereby obtain a “fix” (location of the transmitter) through convergence of the bearings
A stationary RDF station might coordinate readings with other RDF station(s), mobile or fixed, for a fix
The more LOPs, and the larger the angles between them, the more accurate the fix
Bearings should be reported either as “True” or “Magnetic” – often small or mobile units use “Magnetic” while fixed stations use “True” (“True” enables direct chart plotting)
Knowing the exact position of the RDF unit at the time the LOP was taken is essential.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 9: RDF Theory of Operation (LOPs and Fixes)
(no author’s notes).
<number>

## Slide 11: RDF Theory of Operation (LOPs and Fixes Illustrated)
AUXCOM – Auxiliary Communications Specialty Course
<number>
RDF “A”
RDF “B”
TRANSMITTER
LOP “A”
LOP “B”
FIX
Notes: Slide 10: RDF Theory of Operations (LOPs and Fixes Illustrated)
ANIMATIONS
Base slide displayed. Simulated perspective ocean with unlabeled transmitter and two RDF stations. For the visually acute, yes, the RDF stations are deliberately not aligned.
[CLICK] transmitter label.
[CLICK] RDF labels.
[CLICK] LOP “A”.
[CLICK] LOP “B”.
[CLICK] Fix.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 12: RDF Theory of Operation (Bidirectionality)
The display unit indicates when the wave front is phased. This indication is usually visual or audible
When the RDF unit is in phase, the transmitting station is at right angles to the RDF antennas.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Two or more antennas near each other and properly connected (phased) with a display unit usually determine the orientation of the wavefront
The antennas are rotated until they both receive the same wavefront at the same time.
Simple RDF units using only two antennas may give bi-directional bearings (the operator can’t tell if the transmitter is ahead or 180 degrees behind the RDF unit) .
Additional bearings, either along the wave front or by other RDF units are required to determine the true direction of the bearing
Automatic RDF units, with multiple antennas, do not have the bidirectional characteristic .
Notes: Slide 11: RDF Theory of Operation (Bidirectionality)
ANIMATIONS.
Base slide displayed, text and diagram.
[CLICK] text replaced with additional text.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 13: Equipment
Most RDF antennas differ from communication antennas - Automatic Directional Finder (ADF) antennas do not have “gain”
Many RDF units enable the operator to change from RDF to radio communications
RDF antenna system must be calibrated after installation. Details in text.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 12: Equipment
(no author’s notes).
<number>

## Slide 14: Operator Training
Reliable RDF operations require skilled operators – VHF RDF is frequently subject to false readings from reflected and weak signals
RDF operators should periodically check the condition of their units on known signals
RDF operators should also frequently test their own capabilities by taking LOPs on mobile and weak signals to see just how well both they and the equipment are performing
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 13: Operator Training
(no author’s notes).
<number>

## Slide 15: Some Chapter Questions
AUXCOM – Auxiliary Communications Specialty Course
<number>
QUESTION | ANSWER
What type of bearing is usually taken by a mobile RDF? By a fixed RDF? | 
What law enforcement powers does an Auxiliarist have when discovering an illegal transmitter? | 
What are some of the uses of RDF units? | 
When several LOPs (lines of position) intersect at a point, this is called a (what)? | 
Bearing information should be provided to whom? | 
Mobile: relative, translated to Magnetic. Fixed: True bearings.
None.
Location of distressed vessels, Location of distress beacons, Locations of interfering signals, fraud detection, SAR vectoring.
Fix.
Coast Guard authorized recipients.
Notes: <number>
Slide 14: Some Chapter Questions
ANIMATIONS
Five questions are displayed.
[CLICK] to display each answer in sequence. Font change used to simulate human handwriting.
After last answer displayed, one more [CLICK] to next screen (allows instructor pause for last answer).
* * * * * * * * * * (end comments).

## Slide 16: End of Chapter 9
AUXCOM – Auxiliary Communications Specialty Course
<number>
Questions?
Next: Chapter 10, “Rescue 21”
Notes: <number>
Slide 15: End of Chapter 9
(no author’s notes).
This is the last slide of this deck intended to be displayed normally.

## Slide 17
AUXCOM – Auxiliary Communications Specialty Course
<number>
(This slide intentionally left blank.)
Notes: <number>
Slide 16: endslide
Not intended to be normally displayed.