## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Auxiliary Communications Specialty (AUXCOM)
<number>
Chapter 4
Distress, Urgency and Safety Messages
AUXCOM 2009 v0.98
Notes: <number>
US COAST GUARD AUXILIARY – Auxiliary Communications Specialty Course (“AUXCOM”)
2009 UPDATE, version 0.98
Slide 1. Chapter cover slide.
Chapter 4: “Distress, Urgency and Safety Messages”
(no author notes).

## Slide 3: Chapter 4 Outline
AUXCOM – Auxiliary Communications Specialty Course
<number>
General
Distress
Urgency
Safety
EPIRBs
March 2009, Coast Guard assists disabled trawler “Sea Siren” off New Bedford, MA.
NOTE: IN AUXILIARY COMMUNICATIONS, AUXILIARY FACILITY DESIGNATIONS ARE USED AS CALLSIGNS – IN THIS PRESENTATION, VESSEL NAMES ARE USED FOR SIMPLICITY IN THE ENCLOSED SCENARIOS.
Notes: Slide 2: Chapter 4 Outline
(no author’s notes).
<number>

## Slide 4: General
Distress, Urgency and Safety messages are broadcast to “any and all stations,” not a specific station
Calls made on VHF Channel 16 or 2182 KHz – may be preceded by alarm signal (2-tone warble, 30-60 sec.)
Distress (“Mayday”)
  Highest Priority – overrides all other communications
  Grave or imminent danger – immediate assistance required
Urgency (“Pan Pan”)
  Urgent message re: safety of ship, aircraft, vessel, person
Safety (“Sécurité”)
  Message re: safety of navigation or meteorological warning.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 3: General Information
(no author’s notes).
<number>

## Slide 5: Distress
“Mayday, Mayday, Mayday …”
  Should be sent only on authority of the person responsible for the vessel or aircraft (unless incapacitated)
  Stations hearing “Mayday” cease all other transmissions, then listen & record the distress message
  Radiotelephone Alarm Signal (if available) – intended to attract attention of radio watchstanders and/or activate automatic alarms. Used only is distress call follows or person overboard
  Speak clearly, slowly and distinctly to help transcribers.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 4: Distress (“Mayday”)
(no author’s notes).
<number>

## Slide 6: Distress
Mayday Message includes:
  WHO … (vessel name and callsign)
  WHERE … (GPS coordinates, bearings or best approximation of location)
  WHAT … (nature of the distress)
  HOW … (type of assistance required)
  NUMBER … (persons aboard & how many require assistance)
  CONDITION … (present seaworthiness of vessel)
  DESCRIPTION … (vessel or aircraft type, length, masts, color, etc.)
  SCHEDULE … (listening frequency & schedule).
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide: Distress, continued.
(no author’s notes).
<number>

## Slide 7: Distress - Call
AUXCOM – Auxiliary Communications Specialty Course
<number>
SIMULATED DISTRESS SCENARIO.
“Mayday, Mayday, Mayday … This is sailing vessel ‘Misty,’ drifting about 5 miles south of Santa Cruz Island – off Gull Island.
We have been dismasted and have seriously injured crew …”
“… We request immediate medical assistance for our injured crew. Two persons with bleeding head injuries, one not conscious, four persons aboard. We are afloat, entangled in mast and rigging and unable to motor. Misty is a 30-foot all-white sloop. I will maintain a watch on this channel and repeat this message every 2 minutes. Over.”
Most Mayday messages will not be this complete or measured. Shock, panic, pain, injury and other impediments to clear communication must be expected – including inexperience on the part of the distress caller and compromised transmitting capability. People, even trained, may not be at their best.
Notes: Slide 6: Distress Call
ANIMATIONS
Basic slide displayed. Scenario simulates distress call in neighborhood of Santa Cruz Island, CA. Picture is from CG of an actual distressed vessel – scenario is NOT the actual “Misty” response case.
[CLICK]. First part of distress message displayed. Pause allows instructor/presenter to comment.
[CLICK]. Second part of distress message displayed. Pause allows instructor/presenter to comment.
[CLICK]. Notice on expected quality of distress messages from the general public.
[CLICK]. Next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 8: Distress - Acknowledgment
AUXCOM – Auxiliary Communications Specialty Course
<number>
Upon hearing a Mayday call:
Record all details – the call might not be repeated.
Wait momentarily to see if the Coast Guard responds. While waiting, assess your capability to assist – either directly or as a radio relay.
If the Coast Guard doesn’t promptly acknowledge, vessels in immediate vicinity do.
Acknowledge as follows:
“MAYDAY … (distressed vessel name – 3 times) … THIS IS … (your vessel name or callsign – 3 times) … RECEIVED MAYDAY.”
Pause to listen for a better-situated responder.
“MAYDAY … (distressed vessel name) … THIS IS … (your vessel name or callsign) … (your position) … (your speed and time estimate to reach the distressed vessel).”
MAYDAY RELAYS ARE DISCUSSED ON A FOLLOWING SLIDE.
“MAYDAY. Misty, Misty, Misty. This is Seafarer, Seafarer, Seafarer. Received Mayday.”
(No other acknowledgements broadcast.)
“MAYDAY. Misty. This is Seafarer. We are north of you, about 1 mile south of Gull Island, our speed, 12 knots. We will be near your position in 20 minutes. This is Seafarer, over.”
Notes: Slide 7: Distress Acknowledgement
ANIMATIONS.
Basic slide displayed. Intent is to continue the “Misty” scenario from previous slide and discuss acknowledgement procedures. Basic slide explanatory note: 1. VERY IMPORTANT – record all details ASAP – the distress call may not be repeated. 2. Wait momentarily to see if CG acknowledges and is in better position to respond – or another vessel is better positioned/more able to respond. Instructor/presenter should note that this doesn’t mean the call recipient doesn’t respond to the distress, but that priority should be given to the more able (better equipped and positioned) responder. Any distress case may need multiple responders and not be immediately apparent to the original call recipient; primary responder may also want contingency backup.
[CLICK]. Original explanatory notes replaced with template dialog and notes on making an acknowledgement.
[CLICK]. Simulated dialog. Acknowledgement, first part.
[CLICK]. Simulated dialog. Pause to wait on other potential acknowledgers.
[CLICK]. Simulated dialog. No other acknowledgements; acknowledgement second part.
[CLICK]. Next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 9: Distress Communications
“Distress Communications” are all messages related to the immediate situation – each preceded by “MAYDAY”
“SEELONCE MAYDAY” – distressed vessel or station in control of communication may impose silence on interfering stations
“SEELONCE DISTRESS” – silence requested by other stations believing it necessary
“SEELONCE FEENEE” – when silence no longer required, or distress traffic has ceased
  “MAYDAY … HELLO ALL STATIONS (3 times) … THIS IS (callsign of terminating station) … (time) … (callsign of distressed vessel) … SEELONCE FEENEE.”
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 8: Distress Communications
(no author’s notes).
<number>

## Slide 10: Distress – Mayday Relays
Distress messages may be relayed by other craft:
  When the distressed craft is not capable of transmitting
  When a vessel or shore station considers further help necessary
  When a station not in position to render assistance hears a Mayday that has not been acknowledged
The relaying station takes all necessary steps to contact the Coast Guard.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 9: Distress – Mayday Relays
(no author’s notes).
<number>

## Slide 11: Distress – Mayday Relays
AUXCOM – Auxiliary Communications Specialty Course
<number>
“Mayday relay, mayday relay, mayday relay. This is Orion, Orion, Orion. Over.”
Precede the Mayday relay transmission with the radiotelephone alarm, if possible.
Notes: Slide 10: Distress – Mayday Relays
(no author’s notes).
<number>

## Slide 12: Urgency
“Pan Pan, Pan Pan, Pan Pan”
  pronounced “Pawn Pawn,” and spoken 3 times
  Person responsible for craft (if not incapacitated) has responsibility to send
  Priority over all other messages, except “Mayday”
  Similar “recommended content” as distress call:
    who, what, where, how, condition, number, description, schedule, etc.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 11: Urgency (Pan Pan)
(no author’s notes).
<number>

## Slide 13: Urgency
AUXCOM – Auxiliary Communications Specialty Course
<number>
SIMULATED URGENCY SCENARIO.
“Pan-Pan, Pan-Pan, Pan-Pan. This is Wind Dancer, 12 miles southeast of Montauk Point. High winds have shredded our sails, and our engine is not operating. We are adrift and require a tow. 5 persons on board. Wind Dancer is a 35-foot all-white sloop. This is Wind Dancer, over.”
Notes: Slide 12: Urgency
(no author’s notes).
Picture is from CG of a sailboat towed to Station Montauk (NY); simulated scenario here is NOT the actual situation.
<number>

## Slide 14: Safety
“Sécurité”
  pronounced “SAY-CURE-EE-TAY,” and spoken 3 times
  The safety message itself, following the initial call (on VHF Channel 16 or 2182 KHz), is often sent on a working frequency
  In areas with Coast Guard radio coverage, forward the information to the CG to decide whether or not to broadcast
  Auxiliarists on patrol in areas without CG radio coverage should send using Auxiliary callsigns.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 13: Safety (“Sécurité”)
(no author’s notes).
<number>

## Slide 15: Safety
AUXCOM – Auxiliary Communications Specialty Course
<number>
“Sécurité, Sécurité, Sécurité. This is Coast Guard Auxiliary 25894. Shift to VHF Channel 69 for a safety message. This is 25894 out.”
“Sécurité, Sécurité, Sécurité. This is Coast Guard Auxiliary 25894. A log approximately 20 feet long, 2 feet in diameter is adrift 1 mile southwest off Sombrero Key. Proceed with caution in the area.
This is 25894 out.”
(Switch to working frequency.)
Notes: Slide 14: Safety
ANIMATIONS
Basic slide displayed (picture only, no info).
[CLICK]. Safety message initiated – directive to switch frequency.
[CLICK]. Pause for switch to frequency.
[CLICK]. Safety message.
[CLICK]. Next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 16: EPIRBs
EPIRB: “Emergency Position Indicating Radio Beacon”
ELT: “Emergency Locator Transmitter”
Small emergency radios transmitting distress beacons – may be fully automatic, semi-automatic or hand-activated
EPIRBs: passive devices, maritime
ELTs: aeronautical use
Also: PLB – “Personal Locator Beacons”
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 15: EPIRBs
(no author comments).
<number>

## Slide 17: EPIRBs
Several classes of EPIRBs:
  CLASS A: operate on 121.5 and 243 MHz, automatically activated, 48-hour activity
  CLASS B: operate on 121.5 and 243 MHZ, manually activated, 48-hour activity
  CLASS C: operates on VHF Channels 15 & 16, sending special alerting and homing signals, for up to 24 hours
  Classes A, B & C have been phased out and are no longer responded to by the Coast Guard.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 16: EPIRBs
(no author’s notes).
<number>

## Slide 18: EPIRBs
More Classes of EPIRBs:
  CLASS S – used in survival craft, operate on 121.5 and 243 MHz, automatic or manual activation and may float. Continuous or intermittent operation. Phased out, no longer responded to by Coast Guard
  EPIRBs are detected by satellite systems; the high number of false alarms, detection and response delays, inaccuracy of position and lack of identification data led to phase-out of Classes A, B, C and S – THESE EPIRBS SHOULD BE REPLACED.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 17: EPIRBs
(no author’s notes).
<number>

## Slide 19: Category I & II EPIRBs
Category I & II EPIRBs are the currently-recognized emergency beacons
  Operate at 406 MHz, encoded with vessel identity data, endure at least 48 hours, and quickly detected by satellite. All information forwarded via the satellite system to the appropriate Rescue Coordination Center
  Category I – automatic activation (“float free”); SOLAS regulations require carriage by some classes of vessels
  Category II – manual activation
  EPIRB identity data consists of a unique registration number keyed to a NOAA-maintained database with detailed vessel information
  Often have a 121.5 MHz, low-power homing signal for SAR responders
  PLBs also operate on 406 MHz.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 18: Cat I & II EPIRBS
(no author’s notes).
<number>

## Slide 20: Category I & II EPIRBs
Very important to register EPIRB with NOAA, and keep related information up to date (no cost to user to update this database)
Some EPIRBs contain their own GPS for more accurate position location information.
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 19: Cat I & II EPIRBs
(no author’s notes).
<number>

## Slide 21: Automatic Distress Broadcasts
DSC radios have a general distress broadcast capability (“distress button”)
Broadcasts on VHF Channel 70, may include GPS information (if interfaced).
AUXCOM – Auxiliary Communications Specialty Course
<number>
Notes: Slide 20: Automatic Distress Broadcasts
ANIMATIONS.
Basic slide (picture & info) displayed.
[CLICK]. Highlight circle descends, positions over DISTRESS button.
[CLICK]. Next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 22: Some Chapter Questions
AUXCOM – Auxiliary Communications Specialty Course
<number>
QUESTION | ANSWER
Name the three words, any of which can be used to precede a broadcast to “any and all” vessels and stations. | 
You hear a distress broadcast and the nearby Coast Guard station does not answer. What do you do? | 
The vessel in distress, or the station controlling the distress communications may impose silence on interfering stations with what transmission? | 
What is the priority order for distress, urgent and safety messages? | 
What class of EPIRBs transmit identification, and on what frequency? | 
“Mayday,” “Pan-Pan” and “Sécurité”
Acknowledge receipt of the Mayday.
“SEELONCE MAYDAY.”
1- Distress (“Mayday”), 2- Urgency (“Pan-Pan”), 3-Safety (“Sécurité”)
Category I & II; 406 MHz
Notes: <number>
Slide 21: Some Chapter Questions
ANIMATIONS
Five questions are displayed.
[CLICK] to display each answer in sequence. Font change used to simulate human handwriting.
After last answer displayed, one more [CLICK] to next screen (allows instructor pause for last answer).
* * * * * * * * * * (end comments).

## Slide 23: End of Chapter 4
AUXCOM – Auxiliary Communications Specialty Course
<number>
Questions?
Next: Chapter 5, “Auxiliary Communications System”
Notes: <number>
Slide 22: End of Chapter 4
(no author’s notes).
Intended as the last normally-displayed slide of this deck.

## Slide 24
AUXCOM – Auxiliary Communications Specialty Course
<number>
(This slide intentionally left blank.)
Notes: <number>
Slide 23: endslide
(no author’s notes).
Not usually displayed.