## Slide 1
NOTICE:
The information contained within this document is copyright © U.S. Coast Guard Auxiliary
No attempts to add, modify or delete information contained within this document shall be made. If errors are discovered, please contact the U.S. Coast Guard Auxiliary’s National Training Department.
Notes: <number>

## Slide 2: Auxiliary Communications Specialty (AUXCOM)
<number>
Chapter 6
Messages
AUXCOM 2009 v0.98
Notes: <number>
US COAST GUARD AUXILIARY – Auxiliary Communications Specialty Course (“AUXCOM”)
2009 UPDATE, version 0.98
Slide 1. Chapter cover slide.
Chapter 6: “Messages”
(no author notes).

## Slide 3: Chapter 6 Outline
AUXCOM – Auxiliary Communications Specialty Course
<number>
Introduction
Message Parts
Transmitting the Message
Receiving Messages
Sample Messages
Signaling
Example of Coast Guard Forms
Review Questions
Notes: Slide 2: Chapter 6 Outline
(no author’s notes).
<number>

## Slide 4: Introduction
AUXCOM – Auxiliary Communications Specialty Course
<number>
“Message”: thought or idea expressed briefly and prepared in a manner for transmission by any means of communication
Most in-life messages are “informal” … in this chapter we discuss formal messages – messages with a prescribed format, content, purpose and disposition.
Notes: Slide 3: Introduction
(no author’s notes).
<number>

## Slide 5: Introduction: A Simple Message
AUXCOM – Auxiliary Communications Specialty Course
<number>
WHILE THE EMAIL IS A MESSAGE, IT IS NOT A “MESSAGE.”
IT DOES HOWEVER, CONTAIN A “MESSAGE” IN THE BODY OF THE EMAIL.
Sample Message: Commandant of the Coast Guard congratulates the Auxiliary on the occasion of its 70th anniversary. Relayed by e-mail from the Chief Director of the Auxiliary to all members.
THE MESSAGE HAS DEFINED PARTS:
DATE AND PRECEDENCE (PRIORITY) CODING
ORIGINATOR (AUTHOR OR SENDER)
INTENDED RECIPIENT(S)
ADDITIONAL CLASSIFICATION OR IDENTIFICATION INFORMATION
SUBJECT
CONTENT
Notes: Slide 4: A Simple Message
ANIMATIONS.
Basic slide displayed with email text. Real email and message, June 2009, from the Commandant to all Members, congratulating the Auxiliary on its 70th Anniversary. The format is a “message in a message” – the email is a message, but not a “message” and it does contain a “message.”
[CLICK]. Note on “message in a message.”
[CLICK]. A message has defined parts, such as: date and precedence coding. Highlighting circles relevant portion.
[CLICK]. Originator.
[CLICK]. Recipient.
[CLICK]. Additional classifications and coding.
[CLICK]. Subject.
[CLICK]. Message content.
[CLICK]. Next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 6: More Introduction to Messages
AUXCOM – Auxiliary Communications Specialty Course
<number>
Formal messages, with a precise format, are used for information that is required to be a matter of record … most Auxiliary information exchange is informal
Many varieties of messages exist, with differing formats – this chapter will focus on Auxiliary-related messages – qualified communications watchstanders will learn more
Most Auxiliary-pertinent messages will be SAR-related, could be actual or drill … need understanding of messages to function effectively as an Auxiliarist – our main concern: messages must reach their destination accurately, securely and promptly
Auxiliary administrative matters often handled in non-message manner: mail, telephone, facsimile, etc.
Notes: Slide 5: More Introduction to Messages
(no author’s notes).
<number>

## Slide 7: 3 Types of Messages
AUXCOM – Auxiliary Communications Specialty Course
<number>
SINGLE ADDRESS
One (1) addressee
Addressee is ACTION or INFO
MULTIPLE ADDRESS
More than one addressee
GENERAL ADDRESS
Wide distribution
ALDIST = “All Coast Guard Districts”
ALCOAST = “All Coast Guard Units”
ALMILACT = “All Military Activities”
Notes: Slide 6: 3 Types of Messages
ANIMATIONS.
Basic (empty) slide displayed with header.
[CLICK] Single Address message info. Note to instructor, the lined-paper depiction is used in this course as a visual icon for messages. The lines represent the required info lines of the message. Instructor should elaborate on the meaning of “ACTION” or “INFO” addressee.
[CLICK] Multiple Address message info.
[CLICK] General Address message info.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 8: Originator and Drafter
AUXCOM – Auxiliary Communications Specialty Course
<number>
Originator
  Authorized to transmit a message
Drafter
  Actually composes the message
May be the same person
Each role has separate responsibilities
INFORMATION
Originator
  Determines is message necessary
  Determines addressee and message type
  Indicates references for brevity & clarity
  Determines procedure
  Forwards for drafting and transmission
Drafter
  Prepares message text … makes it clear, accurate, brief
  Uses proper format for message type
Notes: Slide 7: Originator and Drafter
ANIMATIONS.
Basic slide displayed with info. AUTO animation sequence depicts flow of information from Originator to Drafter.
[CLICK] Originator info displayed.
[CLICK] Drafter info displayed.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 9: Message Parts
AUXCOM – Auxiliary Communications Specialty Course
<number>
Messages are composed of units called “lines” or “format lines.”
“Lines” may be single physical lines of spoken or typewritten text.
The message body text is considered one (1) “format line” and may obviously be comprised of many physical lines of text.
There are fourteen (14) format lines defined, numbered 1 through 13, with numbers 12A and 12B.
The information they contain, if used, must be present in the sequence defined.
Messages have two major parts: “heading” and “text.”.
Lines 1 through 4: “Initial Call,” not strictly part of the heading.
Lines 5 through 10: “Heading,” containing precedence, date-time group, originator, action address(es), information address(es) and accounting information.
Heading determines where the message is to go, and how it is to be handled. Determined by originator; only originator can change.
Line 11 is a “Break” (abbreviated BT), used to separate the heading from the text.
Message format line 12 is the message text.
Divided into 2 lines, 12A and 12B.
12A: message classification and SSIC (Standard Subject Classification Code).
Auxiliary messages are Unclassified (UNCLAS).
12B: message text, starting with subject line followed by the content the originator wished to express.
13: ends the message with a “break” (BT)
EXAMPLE:
R 042200Z JUL 09
FROM COMMANDER COAST GUARD ACTIVITIES BALTIMORE
TO COMMANDER COAST GUARD DISTRICT FIVE
INFORMATION COAST GUARD AUXILIARY VESSEL 42122
BREAK
UNCLAS
SUBJ: INDEPENDENCE DAY REGATTA
“BREAK” is end of message. May be followed by other information.
If sending by radiotelephone the transmission must end with “OVER” or “OUT.”
Notes: Slide 8: Message Parts
ANIMATIONS.
Base slide and info displayed.
[CLICK] message heading info and icon highlight.
[CLICK] message body info and icon highlight.
[CLICK] message lines in more detail. Blue example box on heading info.
[CLICK] blue example box on BT end of message.
[CLICK] next slide.
* * * * * * * * * (end comments).
<number>

## Slide 10: Precedence
AUXCOM – Auxiliary Communications Specialty Course
<number>
 | PRECEDENCE CODE | DESIGNATION | MEANING
 | Z | FLASH | Reserved for initial enemy contact reports and other special emergency operational combat messages. Priority over all other messages. Not encountered in Auxiliary communications.
 | O | IMMEDIATE | Used only for operational traffic, takes precedence over all except flash. Used for ops in progress, flight info, initial distress, medico, reports and warnings of grave natural disasters and more (p. 6-4).
 | P | PRIORITY | Used for SAR situation reports (sitreps), ATON deficiencies, important weather info, urgent administrative matters (the highest precedence normally authorized for administrative matters).
 | R | ROUTINE | Used for normal operational messages, ship movements, administrative matters requiring rapid transmission.
PRIORITY HIGHEST
PRIORITY LOWEST
Notes: Slide 9: Precedence
(no author’s notes).
<number>

## Slide 11: DATE-TIME GROUP & ZONE TIME
AUXCOM – Auxiliary Communications Specialty Course
<number>
Date-Time Group: 042200Z JUL 09 (“July 4, 2009 at 2200 Zulu time”)
  “Z” = “Zulu” or UTC (“Universal Coordinated Time”, f/k/a “GMT” – not “UCT” – “UTC” comes from French)
  Coast Guard communications use UTC (in text, line 12B, time may be in local zone with appropriate letter suffix – see next 2 slides)
  24-hour time (no A.M. and P.M.)
  0000 = midnight, 1900 = 7 P.M.
Notes: Slide 10: Date-Time Group & Zone Time
(no author’s notes).
<number>

## Slide 12: Time Zones
AUXCOM – Auxiliary Communications Specialty Course
<number>
GREENWICH, ENGLAND
“ZULU” (“UTC”, “GMT”)
NEW YORK CITY
“ROMEO”
LOS ANGELES
“UNIFORM”
HONOLULU
“WHISKEY”
Notes: Slide 11: Time Zones
ANIMATIONS.
Basic slide displayed, world time zones. Instructor should orient class to the zones and meanings, including: prime meridian, international date line, UTC, GMT, standard time, daylight time, etc. Every 15 degrees a new time zone, except where political or other boundaries slightly offset (360/24=15). Instructor should elaborate on the alphabetical naming convention and “Zulu.”
[CLICK] Zulu highlighted.
[CLICK] Romeo highlighted (NYC/Eastern time).
[CLICK] Uniform highlighted (California/Pacific time).
[CLICK] Whiskey highlighted (Hawaii).
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 13: US Time Zones
AUXCOM – Auxiliary Communications Specialty Course
<number>
 | AK | AK | AK | HI | PAC | MTN | CEN | EAST | ZULU
ST | Y | X | W | W | U | T | S | R | Z
ST HRS | -12 | -11 | -10 | -10 | -8 | -7 | -6 | -5 | 0
DT | X | W | V | W | T | S | R | Q | Z
DT HRS | -11 | -10 | -9 | -10 | -7 | -6 | -5 | -4 | 0
 ZONE | 2100 | 2200 | 2300 | 2300 | 0100 | 0200 | 0300 | 0400 | 0900 ST
 ZULU | 0200 | 0300 | 0400 | 0400 | 0600 | 0700 | 0800 | 0900 | 1400 ST
With appropriate suffix, would be written as “0300S” and pronounced “0300 SIERRA”
Even though these are in the previous day (040900Z = 032300W) this does not mean the “date line” has been crossed.
“ST” = “STANDARD TIME, “DT” = “DAYLIGHT TIME
Notes: Slide 12: US Time Zones
ANIMATIONS.
Basic slide displayed. Is a East-to-West grid displaying (from right): Zulu time, US Eastern time, Central, Mountain, Pacific, Hawaii, Alaska (3 zones). Rows (from top) are ST (standard time zone designator), ST HRS (ST hours offset from Zulu), DT (daylight time zone designator – instructor should convey alphabetic zone designators change with switch from ST to DT), DT HRS (DT hours offset from Zulu), “To Zone Time,” “To Zulu Time.” Instructor should spend time oriented class to this table.
[CLICK] info balloon on suffixing zone designator on hours time (“0300S”).
[CLICK] balloon disappears, gives instructor opportunity to introduce concept of date line and related computations. Note HI doesn’t change ST/DT.
[CLICK] info balloon on HI and AK time offset implications.
[CLICK] info balloon disappears, gives instructor clear table for any last words.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 14: Transmitting the Message
AUXCOM – Auxiliary Communications Specialty Course
<number>
Remember: transmitting on government frequencies subject to Coast Guard rules and regulations
Voice radio supplements, not replaces, digital and visual communication methods
Use proper procedures – carelessness has caused confusion and overload when good comms was needed
Voice radio considered most insecure means of communications – can be intercepted
Some specific practices are expressly forbidden.
FORBIDDEN PRACTICES:
Violation of radio silence
Unofficial conversation between operators
Transmitting in a directed net without permission
Excessive tuning, testing or radio checking
Unauthorized use of plain language
Transmitting an operator’s name or personal sign
Use of unauthorized prowords
Profane, indecent or obscene language.
Notes: Slide 13: Transmitting the Message
ANIMATIONS.
Basic info slide displayed.
[CLICK] info block on forbidden practices displayed.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 15: Some Microphone Recommendations
AUXCOM – Auxiliary Communications Specialty Course
<number>
Listen before transmitting | Pause occasionally during long messages to let higher-precedent stations break in
Speak clearly and distinctly | Transmit message and get off the air
Speak slowly at a copying speed in short phrases | Do not press push-to-talk until ready to transmit
Avoid extremes of voice pitch | Hold handset firmly
Be natural | Do not send test signals longer than 10 seconds
Use standard pronunciation | Do not use your own fcc call sign when operating on coast guard frequencies
Distance of 2 inches between lips and microphone | Do not use phonetics when plain words work (“Charlie Gulf Alpha” for “Coast Guard Auxiliary”)
Speak in a moderately strong voice | Keep earphone volume low
Shield microphone from noise | Keep speaker volumes moderate
Be accurate responding to radio check requests | Adhere to prescribed procedures
Notes: Slide 14: Some Microphone Recommendations
(no author’s notes).
<number>

## Slide 16: Pronunciation: Numerals
AUXCOM – Auxiliary Communications Specialty Course
<number>
Proword “FIGURES” (or “FIGURES FOLLOW”)
Numeral “0” is always “ZERO” (never “OH”)
Decimal Point: “DAY-SEE-MAL”
Bearings: always 3 digits (015, 030, 090, 180, 270, 345)
Exact multiples of hundreds and thousands: “seven thow-zand,” “too hund-dred”
NUMERAL | SPOKEN AS
0 | ZERO
1 | WUN
2 | TOO
3 | THUH-REE
4 | FO-WER
5 | FI-YIV
6 | SIX
7 | SEVEN
8 | ATE
9 | NINER
EXAMPLES:
“ … FIGURES FO-WER ZERO SIX MEGAHERTZ …”
“ … LATITUDE FO-WER ZERO DEGREES TOO SIX DAY-SEE-MAL THUH-REE FI-YIV MINUTES NORTH …”
“ … BEARING ZERO SEVEN ZERO DEGREES RANGE TOO HUND-RED YARDS …”
Notes: Slide 15: Pronunciation – Numerals
ANIMATIONS.
Basic slide (info and table) displayed.
[CLICK] sample dialog displayed.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 17: Pronunciation: Alphabet
AUXCOM – Auxiliary Communications Specialty Course
<number>
A standard phonetic alphabet (“A, B, C …” as “Alpha, Bravo, Charlie …”) is used to provide clarity – do not “make up” your own phonetic equivalents (e.g., “Alice, Brown, Circus, …”)
Initiate phonetic spelling in a message by the prowords “I SPELL”
Phonetic spelling should not be used when the actual word is better (“26 degrees West” rather than “26 degrees Whiskey”)
Phonetic spelling should not be used when an abbreviation is readily recognizable and authorized (“CGAUX”).
Notes: Slide 16: Pronunciation – Alphabet
(no author’s notes).
<number>

## Slide 18: Phonetic Alphabet
AUXCOM – Auxiliary Communications Specialty Course
<number>
LETTER | PHONETIC | SPOKEN AS | LETTER | PHONETIC | SPOKEN AS
A | ALPHA | AL-fah | N | NOVEMBER | no-VEM-ber
B | BRAVO | BRAH-voh | O | OSCAR | OSS-kah
C | CHARLIE | CHAR-lie | P | PAPA | pah-PAH
D | DELTA | DELL-ta | Q | QUEBEC | keh-BECK
E | ECHO | ECK-oh | R | ROMEO | ROW-me-oh
F | FOXTROT | FOKS-trot | S | SIERRA | see-AIR-rah
G | GOLF | GOLF | T | TANGO | TANG-go
H | HOTEL | ho-TELL | U | UNIFORM | YOU-nee-form
I | INDIA | IN-dee-AH | V | VICTOR | VIK-tah
J | JULIET | jew-lee-ETT | W | WHISKEY | WISS-key
K | KILO | KEY-low | X | XRAY | ECKS-ray
L | LIMA | LEE-mah | Y | YANKEE | YANG-key
M | MIKE | MIKE | Z | ZULU | ZOO-loo
Notes: Slide 17: Phonetic Alphabet
(no author’s notes).
<number>

## Slide 19: Punctuation and Prowords
AUXCOM – Auxiliary Communications Specialty Course
<number>
PUNCTUATION | SPOKEN AS
Comma | COMMA
Period | PERIOD
Parenthesis | PAREN … UNPAREN - or - OPEN BRACKETS … CLOSE BRACKETS
Stroke (“/”) | SLANT
Quotation Marks | QUOTE … UNQUOTE
Hyphen (“–”) | HYPHEN
Colon | COLON
Semicolon | SEMICOLON
PROWORDS | MEANING
BREAK | Separates two portions of message
I SAY AGAIN | Repeating
I SPELL | Next word is spelled
OUT | Transmission ends, no response
OVER | Transmission ends, response expected
ROGER | Transmission received / understood
SAY AGAIN | Request to repeat
SPEAK SLOWER | Request to speak slower
WAIT | Request to pause momentarily
WILCO | “I understand and will comply.”
Prowords (“procedure words”) speed transmission and are not simply jargon.
More listed in textbook.
Similar: “prosigns” usually abbreviations common in more code or digital transmission (ex: “BT” for “”break”).
Some prowords do not combine:
“Over and Out,” is not proper … either “over” or “out” (response expected or not).
“Roger Wilco,” is redundant and improper. “Wilco” contains the “understand” meaning of “roger.”
EXAMPLES:
“THIS IS 013 SAY AGAIN WORD AFTER BOAT OVER”
“THIS IS 122 I SAY AGAIN WORD AFTER BOAT SIGHTED OVER”
“THIS IS 013 ROGER OUT”
“THIS IS 013 NAME OF BOAT OWNER IS MILJANOVITCH I SPELL MIKE INDIA LIMA JULIET ALPHA NOVEMBER OSCAR VICTOR INDIA TANGO CHARLIE HOTEL MILJANOVITCH OVER”
Notes: Slide 18: Punctuation and Prowords
ANIMATIONS.
Basic slide (info tables) displayed.
[CLICK] Prowords info block displayed.
[CLICK] Another prowords info block displayed.
[CLICK] Sample dialog displayed.
[CLICK] next slide.
* * * * * * * * * * (end comments).
<number>

## Slide 20: Radiotelephone Net
AUXCOM – Auxiliary Communications Specialty Course
<number>
Organization of stations capable of direct communications on a common frequency
  may be authorized by CG District Commander
  Categorized by primary usage:
    Administrative: link an authority with subordinates, others
    Traffic: handles message traffic
    Training: technical and procedural training by CG and CGAUX operations
    Command and Control: coordination between District Commander, district units, Auxiliary comms units
    Operational: meets communications requirements of Auxiliary operations among Auxiliary comms units.
Notes: Slide 19: Radiotelephone Net
(no author’s notes).
<number>

## Slide 21: Calling and Answering
AUXCOM – Auxiliary Communications Specialty Course
<number>
Full Call and Answer
  Used to establish communications
  When calling foreign vessels or stations, use “United States”
Abbreviated Call and Answer
  After comms established, can omit call sign of called station when no confusion results
Collective Call
  Group of stations usually operating together when transmissions sent to all.
FULL CALL AND ANSWER EXAMPLE:
“COAST GUARD AUXILIARY VESSEL 42122 THIS IS COAST GUARD ANNAPOLIS STATION OVER”
“COAST GUARD ANNAPOLIS STATION THIS IS COAST GUARD AUXILIARY VESSEL 42122 OVER”
ABBREVIATED CALL AND ANSWER EXAMPLE:
“122 THIS IS ANNAPOLIS OVER”
“THIS IS 122 OVER”
Notes: Slide 20: Calling and Answering
ANIMATIONS.
Basic info slide displayed.
[CLICK] full call example.
[CLICK] related abbreviated call example.
[CLICK] next slide.
* * * * * * * * * * (end comments)
<number>

## Slide 22: More on Transmissions
AUXCOM – Auxiliary Communications Specialty Course
<number>
Operational messages from Auxiliary facilities under orders should be addressed to the command originating the orders, or relayed to the command
Messages from Auxiliary craft not under orders should be addressed to nearest Coast Guard unit or unit pertaining to the message subject
Only CG releases information to news agencies
Auxiliary units may not make public radio news broadcasts without specific authority of District Commander
Unauthorized disclosure or improper use of any information gained from an official assignment is prohibited under security regulations
Use initiative and common sense in unusual situations
Do not knowingly send or deliver false or forged messages.
Notes: Slide 21: More on Transmissions
(no author’s notes).
<number>

## Slide 23: Receiving Messages
AUXCOM – Auxiliary Communications Specialty Course
<number>
Incoming messages addressed to or received by you – for action, information and/or relay
  Always be prepared to copy: paper, pencils/pens, timepiece near the receiver
  For nights, red lights – therefore red ink invisible (use blue or black)
  Receipt of proword “MESSAGE” is an order to copy all of incoming message as it is received (no interpretations, omissions, summary, etc.).
Notes: Slide 22: Receiving Messages
(no author’s notes).
<number>

## Slide 24: Abbreviations
AUXCOM – Auxiliary Communications Specialty Course
<number>
Shortened form of a word or phrase conveying same unmistakable meaning as the long form
  Use to shorten message recording
  Must maintain intelligibility
    Do not over-use
    Use well-recognized abbreviations
    Compass points, chart coordinates, military commands and activities, titles/ranks/grades, geographic locations, common dictionary abbreviations and punctuation.
Notes: Slide 23: Abbreviations
(no author’s notes).
<number>

## Slide 25: Abbreviations (Some Examples)
AUXCOM – Auxiliary Communications Specialty Course
<number>
ABBREVIATION | MEANING | ABBREVIATION | MEANING
ASAP | AS SOON AS POSSIBLE | O/B | OUTBOARD
CGC | COAST GUARD CUTTER | OSC | ON-SCENE COMMANDER
CGSTA | COAST GUARD STATION | ETA | ESTIMATED TIME OF ARRIVAL
CCGD | COMMANDER, COAST GUARD DISTRICT | F/V | FISHING VESSEL
CGDIST | COAST GUARD DISTRICT | OIC | OFFICER IN CHARGE
EMERG | EMERGENCY | POB | PERSONS ON BOARD
EST | ESTIMATE | S/B | SAILBOAT
ETD | ESTIMATED TIME OF DEPARTURE | UNK | UNKNOWN
M/B | MOTORBOAT | PIW | PERSON IN WATER
MSG | MESSAGE | LOC | LOCATION
Notes: Slide 24: Abbreviations (Some examples)
(no author’s notes).
<number>

## Slide 26: Representative Messages
AUXCOM – Auxiliary Communications Specialty Course
<number>
Pleasure Cruise – Available for SAR
  Advising CG of availability for deployment while on pleasure outing
  If DO send such an availability message, then must also send a message before securing from radio watch
Patrols
  Usually minimum of (2) messages: patrol commences, patrol secures (ends) – may also need an “on station” message
  Addressed to CG unit authorizing patrol
ATON Discrepancy
  Hazard to safe navigation exists; precedence P message to local CG station or group to report malfunction or other discrepancy.
SEE TEXTBOOK FOR SAMPLE MESSAGE SCRIPTS.
Notes: Slide 25: Representative Messages
(no author’s notes).
<number>

## Slide 27: Representative Messages
AUXCOM – Auxiliary Communications Specialty Course
<number>
SITREP (Situation Report) Messages
  A continuing series (once started) of serially-numbered messages until situation concludes
  Last SITREP of a particular situation says “AND FINAL” – possible for a situation to open and close with one message (“SITREP ONE AND FINAL”) – also final SITREP must say at end of text, “CASE CLOSED THIS UNIT”
  Precedence P or O for all; final message precedence R
  Emergency phases: UNCERTAINTY, ALERT, DISTRESS
  MEDICO SITREP – used when medical advice and/or evacuation required – use precedence O
  Content, format specified in District OPLAN and/or COMMPLAN.
SEE TEXTBOOK FOR SAMPLE SITREP MESSAGE SCRIPTS.
Notes: Slide 26: Representative Messages
(no author’s notes).
Note use of Courier font to indicate required elements.
<number>

## Slide 28: Signaling / Coast Guard Forms
AUXCOM – Auxiliary Communications Specialty Course
<number>
Signal flags or Morse code may be used when/if radio communications fail or no common language
  International Code of Signals (US Edition)
  common instructions on signaling methods and list of typical messages
Sample Coast Guard Forms (included in text) – presented to make recording data easier
  SAR Report, Overdue Report, Flare Sighting Report.
Notes: Slide 27: Signaling/Coast Guard Forms
(no author’s notes).
Note that the signal flags, read top to bottom, spell “USCGAUX.”
<number>

## Slide 29: Some Chapter Questions
AUXCOM – Auxiliary Communications Specialty Course
<number>
QUESTION | ANSWER
What are the three basic types of messages? | 
What separates the parts of a message? | 
What are the message precedences and their abbreviations? | 
The entire Coast Guard communications organization operates on what time? | 
What is the proword to indicate numerals follow? | 
Single Address, Multiple Address, General Address
“BREAK” (or “BT”)
Z – Flash, O – Immediate,
P – Priority, R - Routine
UTC – Universal Coordinated Time (used to be called “GMT”)
FIGURES
Notes: <number>
Slide 28: Some Chapter Questions (1 of 2)
ANIMATIONS
Five questions are displayed.
[CLICK] to display each answer in sequence. Font change used to simulate human handwriting.
After last answer displayed, one more [CLICK] to next screen (allows instructor pause for last answer).
* * * * * * * * * * (end comments).

## Slide 30: More Chapter Questions
AUXCOM – Auxiliary Communications Specialty Course
<number>
QUESTION | ANSWER
The proword “WILCO” signifies what? | 
What does the proword “ROGER” mean? | 
What does the proword “OUT” mean” | 
Patrols usually require a minimum of two (2) messages. What are they? | 
Who determines the address of a message? | 
“I understand and will comply”
“I received last transmission satisfactorily”
“I am ending this transmission, no response from you expected”
First, “Underway” when commencing patrol. Second, “Secure” when patrol ends.
Originator
Notes: <number>
Slide 29: Some Chapter Questions (2 of 2)
ANIMATIONS
Five questions are displayed.
[CLICK] to display each answer in sequence. Font change used to simulate human handwriting.
After last answer displayed, one more [CLICK] to next screen (allows instructor pause for last answer).
* * * * * * * * * * (end comments).

## Slide 31: End of Chapter 6
AUXCOM – Auxiliary Communications Specialty Course
<number>
Questions?
Next: Chapter 7, “The Radiotelephone Log”
Notes: <number>
Slide 30: End of Chapter
(no author’s notes).
This is intended to be the last displayed slide of this deck.

## Slide 32
AUXCOM – Auxiliary Communications Specialty Course
<number>
(This slide intentionally left blank.)
Notes: <number>
Slide 31: endslide
This slide is generally not shown.